## Slide 1: Parallelism and Coherency
Caches and parallelism
  Opportunities and costs
  Intra-thread vs inter-thread locality
Coherency
  Interlocked memory accesses
  Basic MSI protocol
  MESI/MOESI protocol

## Slide 2: Caches and Parallelism
“Traditional” caches makes single-threaded code faster
  Temporal locality : reading or writing the same data again
  Spatial locality : reading or writing to nearby addresses
  Resource sharing : use Icache and Dcache over one memory bus
  Intra-core coherency : always read the last value written to address
Multi-core systems present opportunities and problems
  Inter-thread locality : two threads using the same data at once
  Resource sharing : cache storage shared amongst many cores
  Inter-core coherency : each address must have a unique value
  Inter-core consistency : is the history of operations consistent?

## Slide 3: The “good” side : data sharing
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 4: Sequential accesses
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 5: Sequential accesses
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 6: Sequential accesses
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 7: Sequential accesses
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 8: Sequential accesses with blocks
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 9: Sequential accesses with blocks
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 10: Sequential accesses with blocks
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 11: Sequential accesses with blocks
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 12: Sequential accesses with blocks
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 13: Sequential accesses with blocks
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 14: Sequential accesses with blocks
void mat_vec_mul_v1(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
dst[i]=0;
for(int j=0; j<n; j++){
dst[i] += m[j*n+i] * v[j];
}
}
}

## Slide 15: Good practice : avoid memory accesses
void mat_vec_mul_v2(
int n,
int *dst,
const int *m,
const int *v
){
for(int i=0; i<n; i++){
int sum=0;
for(int j=0; j<n; j++){
sum += m[j*n+i] * v[j];
}
dst[i] = sum;
}
}
Avoiding unneeded accesses may help compiler
It definitely helps the humans reading it

## Slide 16: Going parallel : two threads
void mat_vec_mul_v3(
int n,
int *dst,
const int *m,
const int *v
){
auto mul_range=[&](int begin, int end)
{
for(int i=begin; i<end; i++){
int sum=0;
for(int j=0; j<n; j++){
sum += m[j*n+i] * v[j];
}
dst[i] = sum;
}
};
std::thread worker([&](){
mul_range( 0, n/2 );
});
mul_range( n/2, n);
worker.join();
}

## Slide 17: Going parallel : thread 1 accesses
void mat_vec_mul_v3(
int n,
int *dst,
const int *m,
const int *v
){
auto mul_range=[&](int begin, int end)
{
for(int i=begin; i<end; i++){
int sum=0;
for(int j=0; j<n; j++){
sum += m[j*n+i] * v[j];
}
dst[i] = sum;
}
};
std::thread worker([&](){
mul_range( 0, n/2 );
});
mul_range( n/2, n);
worker.join();
}

## Slide 18: Going parallel : thread 2 accesses
void mat_vec_mul_v3(
int n,
int *dst,
const int *m,
const int *v
){
auto mul_range=[&](int begin, int end)
{
for(int i=begin; i<end; i++){
int sum=0;
for(int j=0; j<n; j++){
sum += m[j*n+i] * v[j];
}
dst[i] = sum;
}
};
std::thread worker([&](){
mul_range( 0, n/2 );
});
mul_range( n/2, n);
worker.join();
}

## Slide 19: Going parallel : both threads
void mat_vec_mul_v3(
int n,
int *dst,
const int *m,
const int *v
){
auto mul_range=[&](int begin, int end)
{
for(int i=begin; i<end; i++){
int sum=0;
for(int j=0; j<n; j++){
sum += m[j*n+i] * v[j];
}
dst[i] = sum;
}
};
std::thread worker([&](){
mul_range( 0, n/2 );
});
mul_range( n/2, n);
worker.join();
}

## Slide 20: Going parallel : both threads
void mat_vec_mul_v3(
int n,
int *dst,
const int *m,
const int *v
){
auto mul_range=[&](int begin, int end)
{
for(int i=begin; i<end; i++){
int sum=0;
for(int j=0; j<n; j++){
sum += m[j*n+i] * v[j];
}
dst[i] = sum;
}
};
std::thread worker([&](){
mul_range( 0, n/2 );
});
mul_range( n/2, n);
worker.join();
}

## Slide 21: Going parallel : both threads
void mat_vec_mul_v3(
int n,
int *dst,
const int *m,
const int *v
){
auto mul_range=[&](int begin, int end)
{
for(int i=begin; i<end; i++){
int sum=0;
for(int j=0; j<n; j++){
sum += m[j*n+i] * v[j];
}
dst[i] = sum;
}
};
std::thread worker([&](){
mul_range( 0, n/2 );
});
mul_range( n/2, n);
worker.join();
}

## Slide 22: Going parallel : both threads
void mat_vec_mul_v3(
int n,
int *dst,
const int *m,
const int *v
){
auto mul_range=[&](int begin, int end)
{
for(int i=begin; i<end; i++){
int sum=0;
for(int j=0; j<n; j++){
sum += m[j*n+i] * v[j];
}
dst[i] = sum;
}
};
std::thread worker([&](){
mul_range( 0, n/2 );
});
mul_range( n/2, n);
worker.join();
}

## Slide 23: Going parallel : both threads
void mat_vec_mul_v3(
int n,
int *dst,
const int *m,
const int *v
){
auto mul_range=[&](int begin, int end)
{
for(int i=begin; i<end; i++){
int sum=0;
for(int j=0; j<n; j++){
sum += m[j*n+i] * v[j];
}
dst[i] = sum;
}
};
std::thread worker([&](){
mul_range( 0, n/2 );
});
mul_range( n/2, n);
worker.join();
}

## Slide 24: This is the good side of parallel memory
Matrix m is split between processors
  Can make good use of separate caches
  Blocks are clean: can be evicted any time
Vector v is shared between processors
  Can exist in each processor’s cache
  Or… can share blocks between processors
Vector dst is split between processors
  Blocks are dirty : must write back on evict
  No shared blocks between processors
Note the many assumptions
  Matrix + vector aligned to block size
  Thread count aligned to block size

## Slide 25: An aside: more scalable solutions uses libraries
void mat_vec_mul_v4(
int n,
int *dst,
const int *m,
const int *v
){
tbb::parallel_for<int>(0, n, [&](int i){
int sum=0;
for(int j=0; j<n; j++){
sum += m[j*n+i] * v[j];
}
dst[i] = sum;
});
}
E.g. Intel TBB
Adapts to core count
  Works on 1 core or 128
Automatic load-balancing
  Other processes use cores too
Automatic granularity
  What if n is very small?

## Slide 26: Parallel memory : the problems
Our example was “good” parallel code
  Shared + read-only data : any core can access it
  Private + read-write data : only one core can access it
The problems arise with shared + read-write data
  Many cores can access a memory location
  Many cores can read and modify a memory location
This is not just a user code problem
  Run-time libraries : malloc/free, garbage collectors
  Operating system : moving a thread between cores
This is not just a functional correctness problem
  Concurrent accesses drastically affect performance

## Slide 27: Classic example: Counters
void TaskFunc(int *data)
{
...
(*data) += 1;
...
}
void TaskFunc(int *data)
{
...
int curr=*data;
int next=curr+1;
*data=next;
...
}

## Slide 28: Classic example: Counters
void TaskFunc(int *data)
{
...
int curr=*data;
int next=curr+1;
*data=next;
...
}
void TaskFunc(int *data)
{
...
int curr=*data;
int next=curr+1;
*data=next;
...
}

## Slide 29: Possible solutions
Languages
  Make data sharing impossible : e.g. rust
  Make data-races undefined behaviour : e.g. c/c++
  Add support for atomic primitives : atomic_inc
  Add libraries/constructs for locking : std::mutex, synchronized
ISAs + Architectures
  Eliminate data-races : far too slow; gets worse with more cores
  Cache line lock+unlock instructions : used in embedded systems
  Locked instructions : used in x86 and CISC-style architectures
  Conditional stores : used in MIPS/ARM and RISC-style architectures
  Transactional memory : Intel sort of support this (TSX); not common

## Slide 30: Solution : mutexes
void TaskFunc(int *data)
{
...
(*data) += 1;
...
}
void TaskFunc(std::mutex &m, int *data
){
...
{
std::unique_lock lk(m);
(*data) +=1 ;
}
...
}

## Slide 31: Solution : atomic increment
void TaskFunc(int *data)
{
...
(*data) += 1;
...
}
void TaskFunc(int *data){
...
atomic_fetch_add(data, 1);
...
}

## Slide 32: Solution : compare exchange
void TaskFunc(int *data)
{
...
(*data) += 1;
...
}
void TaskFunc(int *data){
...
int val = atomic_load(data);
while(1){
if(atomic_compare_exchange(
data, // Memory location
val, // Expected value
val+1 // New value
)
{
return;
}
}
...
}
This code is almost certainly buggy – don’t use it

## Slide 33: Cache Coherency + Consistency

## Slide 34: Coherency vs Consistency
Cache coherency : mainly about one memory location
  There is one true value for each memory location; or
  Each memory location behaves “as-if” there were no caches
Memory consistency : global property of all memory
  Do all processors observe a consistent sequence of values; or
  Does memory appear to change in “program order”
We will focus on coherency
  Consistency is fun, but complicated and spans languages + HW

## Slide 35: Parallel cores : simple model
Simple parallel model
  CPUs are independent
All communication via RAM
Only flushed writes visible
  One CPU must write-through
  Other CPU must read-through
Coherency possible but…
  Must always write-through
  Limits CPUs to memory BW
  Limits CPUs to memory latency

## Slide 36: Parallel cores : realistic model
CPUs know each other
  They talk via their caches
Two communication methods:
Long temporal distances
  Communicate via memory
  = 1 CPU over long temporal distance
Short temporal distances
  Communicate via cache
  Either/or:
    Tell each other who owns what line;
    Share lines with each other

## Slide 37: Coherency through locking
Multiple processors are connected through caches

## Slide 38: Coherency through locking
Multiple processors are connected through caches
  Identical data may be found in multiple caches

## Slide 39: Coherency through locking
Multiple processors are connected through caches
  Identical data may be found in multiple caches
  Atomic operations expand into a sequence of smaller operations

## Slide 40: Coherency through locking
Multiple processors are connected through caches
Atomic operations expand to: lock, update, release
  Locking ensures data is only present in one cache

## Slide 41: Coherency through locking
Multiple processors are connected through caches
Atomic operations expand to: lock, update, release
  Locking ensures data is only present in one cache
  While locked, data can be manipulated locally

## Slide 42: Coherency through locking
Multiple processors are connected through caches
Atomic operations expand to: lock, update, release
  Locking ensures data is only present in one cache
  While locked, data can be manipulated locally
  Other CPUs can read the data once it is released

## Slide 43: Coherency through locking
Multiple processors are connected through caches
Atomic operations expand to: lock, update, release
Problem occurs if two CPUs want to modify same memory
  Only one lock will succeed

## Slide 44: Coherency through locking
Multiple processors are connected through caches
Atomic operations expand to: lock, update, release
Problem occurs if two CPUs want to modify same memory
  Only one lock will succeed
  Other CPU will block until it can acquire a lock

## Slide 45: Potential Problems with Atomic Operations
Lock contention : CPUs fight to lock the same location
  Assume CPU performs atomic with probability p per cycle
  Given n processors, probably of conflict per cycle is ~1-(1-p)n
  But eventually progress will be made
Cache thrashing: Locking a variable evicts entire cache line
  Memory traffic increases even if conflicts don’t occur
  Still need to move data from cache to cache
General guidelines for use:
  atomic ops should be a low percentage of total instructions
  try to ensure that each atomic only lives in one cache

## Slide 46: The MSI model
Cache coherency is tricky
  Uses lots of silicon area
  State is distributed throughout the silicon
  Control is distributed throughout the silicon
Formal models and methods are very important here
  Liveness : does the system as a whole make progress
  Fairness : can every CPU eventually make progress
  Correctness : are memory model abstractions maintained
One early model is MSI : Modified, Shared, Invalid

## Slide 47: MSI : Cache block states
Each cache block in each CPU cache has one state:
  Modified : the block is dirty
    Eventually this block must be written back to RAM
    No other CPU’s cache contains the same address
  Shared : the block is clean
    This block can be discarded without writing back
    Other CPUs may contain the same address (also marked as clean)
  Invalid : the block does not contain anything
For any pair of blocks in different CPUS:
 | M | S | I
M | 🗶 | 🗶 | 🗸
S | 🗶 | ✓ | 🗸
I | 🗸 | 🗸 | 🗸

## Slide 48: Interactions using MSI
We have two CPUs, each with their own cache
Each cache is connected to memory and each other

## Slide 49: Interactions using MSI
Store instruction begins on CPU-1

## Slide 50: Interactions using MSI
Store instruction begins on CPU-1
  Write cache miss

## Slide 51: Interactions using MSI
Store instruction begins on CPU-1
  Load contents of M[1] from memory; cache line is Shared
  Notify cache partner just in case

## Slide 52: Interactions using MSI
Store instruction begins on CPU-1
  Perform store into block; state changes to Modified
  Notify partner about state change

## Slide 53: Interactions using MSI
Store instruction completes on CPU-1

## Slide 54: Interactions using MSI
Load instruction begins on CPU-0

## Slide 55: Interactions using MSI
Load instruction begins on CPU-0
  Read miss

## Slide 56: Interactions using MSI
Load instruction begins on CPU-0
  Request line from memory and notify partner
  Partner blocks the operation due to Modified line

## Slide 57: Interactions using MSI
Load instruction begins on CPU-0
  CPU-0 stalls until load can complete
  CPU-1’s cache flushes modified line to memory

## Slide 58: Interactions using MSI
Load instruction begins on CPU-0
  Value for M[1] now only exists in memory
  CPU-1 notifies partners that it no longer owns M[1]

## Slide 59: Interactions using MSI
Load instruction begins on CPU-0
  CPU-1 re-issues load instruction from memory
  It also notifies partners; now there are no conflicts

## Slide 60: Interactions using MSI
Load instruction begins on CPU-0
  CPU finally reads value from cache

## Slide 61: Interactions using MSI

## Slide 62: Interactions using MSI
Add instruction begins on CPU-0

## Slide 63: Interactions using MSI
Add instruction begins on CPU-0
  No memory traffic

## Slide 64: Interactions using MSI

## Slide 65: Interactions using MSI
Store instruction on CPU-0

## Slide 66: Interactions using MSI
Store instruction on CPU-0
  Cache hit; line moves to modified state
  Invalidate any other copies

## Slide 67: Interactions using MSI

## Slide 68: Interactions using MSI
Load on CPU-1

## Slide 69: Interactions using MSI
Load on CPU-1
  Cache read miss

## Slide 70: Interactions using MSI
Load on CPU-1
  Issue read request to memory
  Also notify partners; read blocked due to modified line

## Slide 71: Interactions using MSI
Load on CPU-1
  CPU-1 writes back modified block to memory

## Slide 72: Interactions using MSI
Load on CPU-1
  CPU-1 notifies partner that block is no longer modified

## Slide 73: Interactions using MSI
Load on CPU-1
  CPU-0 issues read again
  Block is stored in Shared state

## Slide 74: Interactions using MSI
Load on CPU-1
  Finally the read completes

## Slide 75: Interactions using MSI

## Slide 76: MSI State Machine

## Slide 77: MSI State Machine
CPURd = CPU load instruction
BusRd = Read transaction over bus

## Slide 78: MSI State Machine
CPUWr = CPU store instruction
BusRdX = Read transaction over bus and take exclusive access

## Slide 79: MSI State Machine
BusUpgr = Tell other caches you’re taking exclusive access

## Slide 80: MSI State Machine

## Slide 81: MSI State Machine

## Slide 82: MSI State Machine
Flush = write data back to memory

## Slide 83: Pros and Cons of MSI
Pro : it ensures coherency for any given address
Pro : un-modified (shared) data can be used in parallel
Pro : it is simple to implement
Con : all traffic goes via the memory bus
  Must evict then re-read, even if data already in another cache
Con : notifications between CPUs are costly
  Gets more expensive with more CPUs

## Slide 84: MESI and MOSI
MESI : Adds an Exclusive state
  Exclusive lines are clean, but only in one cache
  Exclusive -> Modified : if owning CPU writes to line
  Exclusive -> Shared : if another CPU tries to read it
  Allows for transfers of clean data between caches
    Don’t have to write back to memory then read
MOSI : Adds an Owned state
  Owned lines are dirty, but can be read by other CPUs
  Avoids always writing dirty lines back to
  Allows for transfers of dirty data between caches

## Slide 85: The unfortunate details
How do n caches notify each other about memory operations?
Snooping : each cache “listens” to every other cache’s accesses
  Very expensive in area and/or time as n increases
  Full cross-bar: O(n2) area; O(log n) time
  Ring : O(n) area; O(n) time
Directory : shared data structure tracking cache locations
  E.g. hash-table on addresses, or linked-list through caches
  A single directory can become its own bottleneck
Coherency cost is super-linear in number of cores
  But... you can often avoid it in software