## Slide 1: AXI4-Lite GPIO Peripheral and DDR Memory Controller

## Slide 2: Learning Outcomes:
At the end of this module, you will be able to:
Outline AXI4-Lite features and usage of low-power interface.
Describe functionality and properties of General-Purpose Input and Output (GPIO).
Explain the structure and operation of memory access and addressing.
Identify the properties of various types of memory used in a typical SoC including volatile and non-volatile memory.
Describe the structure and read/write operations for SRAM and DRAM.
Describe the role and function of a Memory Controller.

## Slide 3: AMBA AXI4-Lite
AXI4-Lite:
  Suitable for simpler control interfaces, register-style
  Light version of full AXI4
Key features:
  All transactions are of burst length one
  All data accesses are based on full-width data bus (AXI4-Lite supports a data bus of 32-bit width or 64-bit width)
  All accesses are non-modifiable, Non-bufferable
  No support of exclusive accesses
Notes: AXI4-Lite is a subset of the AXI4 protocol intended for communication with simpler control register-style interfaces for systems that do not require the full functionality of AXI4.
AXI4-Lite supports a data bus of 32-bit width or 64-bit width, and all transactions are of one burst length.
In AXI4-Lite, all accesses are Non-modifiable. This means that the characteristics of the transaction cannot be modified. All accesses in AXI4-Lite are also Non-bufferable, which indicates that the interconnect, or any component cannot delay the transaction reaching its final destination by a number of cycles.
Exclusive access mechanisms enable the implementation of atomic operations without requiring the bus to remain locked to a particular Manager for the duration of the operation. The advantage of this is that it does not impact critical bus latency. However, sometimes the Manager may have to make multiple attempts to successfully complete the atomic operation.
Note that there is no exclusive access for AXIF-Lite.
An atomic operation is an operation of transaction that, when initiated by a Manager, must be completed without being interrupted or intercepted by another Manager or transaction. Typically, this applies to a read-modify-write operation, where a Manager wants to read a location, modify it, and write back the results to memory before another Manager has had a chance to modify that location.
Modifiable access indicates that the characteristics of the transaction can be modified.
Bufferable indicates that the interconnect, or any component, can delay the transaction reaching its final destination for any number of cycles. Normally, the bufferable attribute is only relevant to writes.

## Slide 4: AXI4-Lite Signals
Global | Read Address | Read Data | Write Address | Write Data | Write Response
ACLK | ARVALID | RVALID | AWVALID | WVALID | BVALID
ARESETn | ARREADY | RREADY | AWREADY | WREADY | BREADY
 | ARADDR | RDATA | AWADDR | WDATA | BRESP
 | ARPORT | RRESP | AWPORT | WSTRB | 
Notes: This table lists down all the AXI4-Lite Signals.
The signals that are in red are signals that are different compared to AXI in AMBA 3.
ARPORT is a Manager signal that indicates the privilege and security level of the transaction, and whether the transaction is data access or instruction access.
RRESP is a Subordinate signal for Read response. This signal indicates the status of the read transfer. AMBA 3 AXI had the RLAST signal instead to show that the last data item is being transferred.
AWPROT is Protection-type Manager signal. This signal indicates the privilege and security level of the transaction, and whether the transaction is data access or instruction access.
WSTRB is a Write strobes Manager signal. This signal indicates which byte lanes hold valid data. There is one write strobe bit for each eight bits of the write data bus. AMBA 3 AXI had the WLAST signal instead to show that the last data item is being transferred.
The AXI4-Lite protocol supports write strobes. This means multi-sized registers can be implemented, and it also supports memory structures that require support for 8-bit and 16-bit accesses.
All Manager interfaces and interconnect components must provide correct write strobes. Any Subordinate component can choose whether to use the write strobes. The options permitted are:
  to make full use of the write strobes
  to ignore the write strobes and treat all Write-Accesses as being the full data bus width
  to detect write strobe combinations that are not supported and provide an error response

## Slide 5: AXI low-power interface
AXI low-power interface provides control during entry into and exit from a low-power state.
It is an optional extension to the AXI protocol that targets
  Any peripheral without powerdown sequence that can indicate when its clocks can be turned off
  Any peripheral that requires a powerdown sequence and that can have its clocks turned off only after it enters a low-power state
Low-power clock control
  Low-power clock control interface signals:
    One signal from the peripheral indicating when its clocks can be enabled or disabled
    Two handshake signals for the system clock controller to request exit from or entry into a low-power state
  A number of different peripherals can be combined into the same low-power clock domain, to treat that clock domain like a single peripheral.
Notes: The low-power interface is an optional extension to the AXI protocol that targets two different classes of peripherals:
  The first class of peripherals is any peripheral that has no powerdown sequence and that can indicate when its clocks can be turned off.
  The second class of peripherals is any peripheral that requires a powerdown sequence and that can have its clocks turned off only after it enters a low-power state. The peripheral requires an indication from a system clock controller to indicate when to initiate the powerdown sequence and must then signal when it has entered its low-power state.
The low-power clock control interface consists of:
One signal from the peripheral indicating when its clock can be enabled or disabled.
Two handshake signals for the system clock controller to request exit or entry into a low-power state.
Different peripherals can be combined into the same low-power clock domain, and thus treating that clock domain like a single peripheral.
For more information on the AXI low-power interface, see the AMBA AXI Protocol Specification document.
Involved signals are:
CSYSREQ Clock controller: System exit low-power state request. This signal is a request from the system clock controller for the peripheral to exit from a low-power state.
CSYSACK Peripheral device: Exit low-power state acknowledgment. This signal is the acknowledgment from a peripheral to a system exit low-power state request.
CACTIVE Peripheral device: Clock active. This signal indicates that the peripheral requires its clock signal.

## Slide 6: GPIO Overview
General-purpose input/output (GPIO)
  Used for general purpose, no special usage defined
  Widely used for most of the applications
  The direction of input/output is controlled by the direction register.
  A mask register is often used to mask out certain bits.
Direction Register
Bit [0] out
Bit [1] out
Bit [2] out
Bit [0] in
Bit [1] in
Bit [2] in
To external devices
Notes: GPIO is basically a generic pin whose behavior, including whether it is an input or output pin, can be controlled by the user at runtime. GPIO pins have no special purpose defined and go unused by default. They exist because an SoC integrator building a full system with a third-party IP core chip might benefit from a handful of additional digital control lines. Having these available from the chip avoids having to arrange additional circuitry.
GPIO peripherals vary quite widely. In some cases, they are simply a group of pins that can be switched as a group to either input or output. In others, each pin can be set up flexibly to accept or source different logic voltages with configurable drive strengths and pull ups or pull downs. The input and output voltages are typically, though not universally, limited to the supply voltage of the device with the GPIOs on and may be damaged by greater voltages.
The direction of input or output is controlled by the direction register as shown in the diagram in this slide. A mask register is often used to mask out certain bits.
GPIO pins are widely used in embedded applications for reading, from various environmental sensors (IR, video, temperature) to writing output to DC motors (via PWM), audio, LCD displays, or LEDs for status. A GPIO pin's state may be exposed to the software developer through one of a number of different interfaces, such as a memory-mapped peripheral or through dedicated I/O port instructions.

## Slide 7: Basic Concepts
Goal: light either LED1 or LED2 based on switch SW1 position
GPIO
  Input: program can determine if input signal is a 1 or a 0
  Output: program can set output to 1 or 0
Can use this to interface with external devices
  Input: switch
  Output: LEDs
Notes: GPIOs can be used to interface with external devices. For instance, GPIOs can be used as inputs to acquire external control signals (such as from switches and pushbuttons) and as outputs to activate actuators or other devices (such as LEDs). The scheme in this slide shows how GPIOs are used to alternatively switch two LEDs, red and blue, by changing the position of a switch. The GPIO configuration could be controlled by a software application.

## Slide 8: Example GPIO Port Bit Circuitry in MCU
Control
  Direction
  MUX
Data
  Output (different ways to access it)
  Input
Notes: In most devices like MCUs or FPGAs, there is quite a bit of circuitry associated with a GPIO port bit. The connection between the package and the external circuit is a pin or a pad and is shown on the far right of the figure. Usually, there are various properties that can be configured using the control registers. The most common are:
  Data direction (input or output)
  The input/output state (whether it is enabled or disabled)
  Write register value
  Multiplexing, in other words, selecting the peripheral to be connected to the pin
The diagram in this slide shows an example GPIO Port Bit Circuitry in MCU.

## Slide 9: AXI4-Lite GPIO
General-purpose input/output (GPIO) with AXI4-Lite interface
  Used to transmit data between the AXI bus and the GPIO block
  32-bit data transmission with write strobes
AXI4-Lite
Interface
addr
S_AXI
Address
Decoder
Data [31:0]
Output Data
Input Data
Direction
External
Pins
GPIO Block
AXI4-Lite GPIO
Notes: When a GPIO block is to be controlled or accessed through an AXI bus, an AXI interface is needed between the bus and the GPIO block itself. This slide shows the general block diagram of an AXI4-Lite interfaced GPIO.

## Slide 10: Computer Memory
Computer memory: a physical device that is used to store program code or data of a processor on either a temporary or permanent basis
We can distinguish between two types of memory:
  Volatile memory
    Requires power to keep the stored data
  Non-volatile memory
    Can retain stored data after powerdown
Notes: Before examining memory controller implementation, we need to understand what memory is in an SoC. Basically, memory is a physical device that is used to store information, the program code, or data of a processor on either a temporary or permanent basis.
We can categorize memories into two types: volatile memory and non-volatile memory.
Volatile memory requires power to keep the stored data.
Non-volatile memory can retain stored data even after powered off.

## Slide 11: Memory Access
A memory is accessed by presenting it with an address, then writing or reading the data at that address.
For example, a memory architecture with 8-bit width and 8-bit data is shown below:
Address Decoder
Bitline Amplifier
Address [7:0]
Data_In [7:0]
Data_Out [7:0]
Memory Cells
One Word
Address Bus
Notes: In order to obtain data from a memory block and store information in it, we first need to specify the location of the data item we need access to. Each data item in memory has a unique address whose length depends on the size of the memory.
For example, if we have a 256-byte memory, each eight-bit word stored in memory will have an eight-bit address (since 28 = 256). To illustrate the basic operating principles of memory access, we will use the simple architecture of a 256-byte memory that stores 8-bit data words as shown in this slide.
The bit amplifier block is a component of the read/write circuitry that is used when data is read from the memory. To access a specific location in memory, the address is provided to the memory address decoder block through the address bus. The decoder then chooses a specific word to be accessed through the bitline amplifier block. It should be noted here that for larger amounts of memory, the address may be divided into row and column sections.

## Slide 12: Memory Accessing
Present an address:
  Provide an address to the memory address bus
  A particular word is then selected by the address decoder and connected to the bitline amplifier.
  For larger memory, the address may be divided into row and column sections.
Read operation:
  The selected data is connected to the bitline amplifier.
  The amplifier restores the signal to the proper voltage level, then outputs it to the Data_Out port.
Write operation:
  Present the data to the Data_In port
  The amplifier sets the bitlines to the desired values and drives that value from the bitline to the memory cell.
Notes: In order to read from memory, the address of the data item that is to be read is first applied to the address decoder. The address decoder, as explained previously, will choose a specific data item to connect to the bitline amplifier. The bitline amplifier block then senses the low-power signals from a bitline that represents a data bit (1 or 0) stored in a memory cell. It then amplifies the small voltage swing to recognizable logic levels so the data can be interpreted properly by logic outside the memory and then outputs it to the Data_Out port.
In order to write to memory, the address of the memory location that it is to be written to is first applied to the address decoder. At the same time, the data item to be written is presented to the Data_In port. The amplifier sets the bitlines to the desired values and drives that value from the bitline to the memory cell.

## Slide 13: Volatile v Non-volatile Memory
Volatile memory
  Requires power to retain the data information
  Usually faster access speed and less costly
  Used for temporary data storage such as CPU cache, internal memory
  Also known as random access memory (RAM)
Non-volatile memory
  No power is required to retain the data information
  Usually slower access speed and more costly
  Used for secondary storage or long-term persistent storage
Notes: As mentioned previously, there are two types of memory used in the designing of systems on chips (SoCs): volatile memory and non-volatile memory.
Volatile memory retains its contents while powered on, but when power is interrupted, the stored data is lost very rapidly or immediately.
The most widely used form of primary storage today is a volatile form of random access memory (RAM), meaning that when the computer is shut down, anything contained in the RAM is lost.
Non-volatile memory can retain stored information even after having been through a power cycle.
Non-volatile memory is typically used for the task of secondary storage or long-term persistent storage.
However, most forms of non-volatile memory have limitations that make them unsuitable for use as primary storage. Typically, non-volatile memory either costs more or has a poorer performance than volatile RAM.
Examples of non-volatile memory include read-only memory, flash memory, ferroelectric RAM (F-RAM), and most types of magnetic computer storage devices (such as hard disks, floppy disks, and magnetic tape). Optical discs and early computer storage methods such as paper tape and punched cards are also a type of non-volatile memory.

## Slide 14: Types of Memory
Volatile memory
  Static RAM (SRAM)
  Dynamic RAM (DRAM)
Non-volatile memory
  Read-only memory (ROM)
  Erasable programmable ROM (EPROM)
  Electrically erasable programmable ROM (EEPROM)
  Non-volatile random access memory (NVRAM)
  Flash memory
  Mechanical storage
  Hard drive, magnetic tape
Memory
Volatile Memory
Static RAM (SRAM)
Dynamic RAM (DRAM)
Non-Volatile Memory
Read-only Memory (ROM)
Erasable Programmable ROM (EPROM)
Electrically Erasable Programmable ROM (EEPROM)
Mechanical Storage
Hard Drive
Flash memory
Magnetic Tape
Optical Disc
Notes: A detailed list of the different types of memory blocks is shown here.
Volatile memory includes static RAM (SRAM) and dynamic RAM (DRAM), which will be discussed in more detail later on.
Non-volatile data storage can further be categorized into electrically addressed systems (such a as read-only memory) and mechanically addressed systems (such as hard disks, optical discs, magnetic tapes, holographic memory, and so on). Electrically addressed systems are expensive but fast, whereas mechanically addressed systems have a low price per bit but are slow.
In former times, ROM was manufactured with the desired information inside, which cannot be later changed. Later types of ROM allowed data to be reprogramed, but with a degree of effort. Examples include erasable programmable ROM (EPROM) and electrically erasable programmable ROM (EEPROM). The flash memory chip is a close relative to the EEPROM; it differs in that it can only erase one block or “page” at a time. In addition, its capacity is substantially larger than that of an EEPROM, making these chips a popular choice for digital cameras and desktop PC BIOS chips. There are also new emerging memory types, including F-RAM (ferroelectric RAM) and M-RAM (magnetoresistive RAM), which have very promising properties such as non-volatility, infinite endurance, high-speed reading/writing, and low cost.

## Slide 15: Static RAM
Static RAM (SRAM)
  Volatile memory
  Data is retained as long as power is supplied
  Usually uses six transistors to store one-bit data
  Fast data access
  Larger power
  Less density, larger block size
  More expensive
Notes: Static RAM or SRAM is a volatile memory, that is, it retains information as long as it is powered. It is a fast data access technology, but its basic cell is quite large (typically six transistors). Therefore, no high integration density can be achieved, which results in comparatively larger memory block sizes.

## Slide 16: Static RAM Cell
An SRAM cell is typically made up of six MOSFET transistors.
  A single bit is stored on four transistors (M1-M4), which form two inverters that are cross-coupled.
  The access of the bit is controlled by two access transistors (M5 and M6) that are gated by the wordline (select).
Bit
bit'
Select
VDD
M5
M2
M4
M6
M1
M3
Notes: A typical SRAM cell is made up of six MOSFET transistors as shown here.
Each bit in an SRAM is stored on four transistors (indicated by M1, M2, M3, M4 in the diagram) that form two cross-coupled inverters. This storage cell has two stable states that are used to denote 0 and 1. Two additional access transistors serve to control the access to a storage cell during read and write operations. In the diagram, M5 and M6 are the access transistors.
In addition to such six-transistor (6T) SRAM, other kinds of SRAM chips use 4, 6, 10 (4T, 8T, 10T SRAM) or more transistors per bit.
Generally, the fewer transistors needed per cell, the smaller each cell can be. Since the cost of processing a silicon wafer is relatively fixed, using smaller cells and so packing more bits on one wafer reduces the cost per bit of memory.
Compared to 6T or bigger cell SRAM, the principal drawbacks of using 4T SRAM are: (1) its high static power due to the constant current flow through one of the pull-down transistors and (2) that it is not as fast as, say, a 6T cell with CMOS flip-flops.

## Slide 17: Accessing Static RAM
Read operation
  The address is decoded and the desired cell is then selected, in which case the select line is set to one.
  Depending on the value of the four transistors (M1-M4), one of the bitlines will be charged to 1 and the other will be drained to 0.
  The states of the two bitlines (bit and bit’) are then read out as 1-bit data.
  Write operation
  The two bitlines (bit and bit’) are pre-charged to the desired value (e.g., bit = VDD, bit’ = VSS).
  The address is decoded and the desired cell is then selected, in which case, the select line is set to one.
  The four transistors (M1-M4) are then forced to flip their states (either charged or discharged), since the bitlines normally have much higher capacitance than the four transistors.
Notes: When a particular SRAM cell is chosen for a read operation by the address decoder, the desired cell is selected by setting the select line to one. This line controls the two access transistors, M5 and M6. These, in turn, control whether the cell should be connected to the bitlines: bit and bit’. The bitlines are actively driven high and low by the inverters in the SRAM cell.
The states of the two-bit lines (indicated by bit and bit’ in the diagram) are then read out as 1-bit data. Although it is not strictly necessary to have two bitlines, both the signal and its inverse are typically provided in order to improve noise margin.
The start of a write cycle begins by applying the value to be written to the bitlines. If we wish to write a 0, we would apply a 0 to the bitlines, that is, setting bit to 0 and bit’ to 1. This is similar to applying a reset pulse to an SR-latch, which causes the flip-flop to change state. 1 is written by inverting the values of the bitlines. Select signal is then asserted, and the value that is to be stored is latched in.
Because the bitline input-drivers are designed to be much stronger than the relatively weak transistors in the cell itself, they can easily override the previous state of the cross-coupled inverters. In practice, access NMOS transistors M5 and M6 have to be stronger than either bottom NMOS (M1, M3) or top PMOS (M2, M4) transistors. This is easily obtained as PMOS transistors are much weaker than NMOS when they are the same size. Consequently, when one transistor pair (e.g., M3 and M4) is only slightly overridden by the write process, the opposite transistor pair (M1 and M2) gate voltage is also changed. This means that M1 and M2 transistors can be easily overridden, and so on. Thus, cross-coupled inverters magnify the writing process.
Finally, it can be pointed out that there is synchronous and asynchronous SRAM, that is, it can have, or not have, access to memory synchronized through a clock signal.

## Slide 18: Dynamic RAM
Dynamic RAM (DRAM)
  One bit of data can be stored in one transistor and capacitor pair; the status of the capacitor (charged or uncharged) indicates the bit state (1 or 0).
  Needs to be refreshed (or recharged) periodically, since the capacitor leaks its charge, e.g., every 10 ms.
  Higher density, smaller block size
  Less expensive
  DRAM can be categorized according to its data rate and synchronization mode, for example:
    Single data rate (SDR) and double data rate (DDR)
    Synchronous DRAM (SDRAM) and non-synchronous DRAM
Notes: A Dynamic RAM, or DRAM, cell is another type of volatile memory. It stores each bit of data in a separate capacitor within an integrated circuit. The simplest design of a DRAM cell is one transistor and one capacitor, where the status of the capacitor (charged or uncharged) indicates the bit state 1 or 0, and the transistor is used to select a single cell.
Since even “non-conducting” transistors always leak a small current, the capacitors will slowly discharge and the information eventually fades, unless the capacitor charge is refreshed periodically. Because of this refresh requirement, it is a “dynamic” memory (as opposed to “static” memory (SRAM) or other static types of memory).
One of the main advantages of DRAM is its structural simplicity, since typically, only one transistor and capacitor are required per bit, compared to the four or six transistors in SRAM. This allows DRAM to reach very high densities and comparatively smaller block sizes.
DRAM can be categorized according to its data rate and synchronization mode. For example, there are Single Data Rates (SDR) and Double Data Rate (DDR) RAMs. There are also Synchronous DRAM (SDRAM) and non-synchronous DRAMs.
DDR SDRAM: The interface uses double pumping (transferring data on both the rising and falling edges of the clock signal) to lower the clock frequency and reduce signal integrity requirements. The name “double data rate” refers to the fact that a DDR SDRAM with a certain clock frequency achieves nearly twice the bandwidth of a SDR SDRAM running at the same clock frequency due to this double pumping.

## Slide 19: Dynamic RAM
In DRAM, each memory cell requires fewer transistors, e.g., a three-transistor cell or even one-transistor cell.
For example, the one-transistor cell is composed by one transistor and one capacitor.
  One-transistor: a gate transistor used to select a single cell
  One-capacitor: stores the value of a single bit
Bitline
Select
Notes: As mentioned before, the simplest design of a DRAM cell is one transistor and one capacitor, where the status of the capacitor (charged or uncharged) indicates the bit state (1 or 0) and the transistor is used to select a single cell.
A typical DRAM cell is shown here.

## Slide 20: Accessing Dynamic RAM
Read operation
  The address decoder decodes the address and sets the select line to one
  The bitline is then changed according to the state of the capacitor
Write operation
  The single bitline is pre-charged to a desired value (e.g., VDD or VSS)
  The address decoder decodes the address and sets the select line to one
  The capacitor is then either charged or discharged by the bitline
Notes: When a particular DRAM cell is chosen for a read operation by the address decoder, the desired cell is selected by setting the select line to one. This causes the transistor to conduct, transferring charge from the storage cell to the connected bitline (if the stored value is 1) or from the connected bitline to the storage cell (if the stored value is 0). Since the capacitance of the bitline is typically much higher than the capacitance of the storage cell, the voltage on the bitline increases very slightly if the storage cell’s capacitor is discharged and decreases very slightly if the storage cell is charged (around, 0.54V and 0.45 V in the two cases). This change in the voltage level of the bitline is detected by the sense amplifier as seen previously.
The start of a write cycle begins by applying the value to be written to the bitlines. If we wish to write a 0, we would apply a 0 to the bitlines. The address decoder decodes the address and sets the select line to one; this causes the capacitor to be either charged or discharged by the bitline.

## Slide 21: Non-volatile Memory
Read-only memory (ROM)
  In early times, ROM was manufactured with the desired data, which could not be changed.
  Later types allowed data to be reprogramed, but with a degree of effort.
    Erasable programmable ROM (EPROM)
    Electrically erasable programmable ROM (EEPROM)
Non-volatile random access memory (NVRAM)
  Radom access, data can be both read and written
  Best-know form is flash memory
Mechanical storage
  Non-electrically addressed memories, e.g., hard drives, magnetic tapes, optical drives
  Less expensive, but slower
Notes: Formerly, read-only Memory, or ROM, was manufactured with the desired information inside, which could not be later changed. Later types of ROM allowed data to be reprogrammed, but with a degree of effort. Examples include erasable programmable ROM (EPROM) and electrically erasable programmable ROM (EEPROM).
The modern flash memory chip is a close relative to the EEPROM. It differs in that it can only erase one block or “page” at a time. Also, its capacity is substantially larger than that of an EEPROM. Today, it is frequently used as a non-volatile program memory in MCUs and SoCs, desktop PC BIOS chips, and for permanently storing the configuration bitstreams in some FPGAs.
Mechanical storage utilizes a contact structure (“head”) to read and write on a designated storage medium. Since the access time depends on the physical location of the data on the device, mechanically addressed systems may not be “random access” as are electrically addressed semiconductor NVRAM. For example, magnetic tapes store data as a sequence of bits on a long tape; transporting the tape past the read/write head is required to access any part of the storage. Tape media can be removed from the drive and stored, giving indefinite capacity at the cost of the time required to retrieve a dismounted tape. Hard disk drives use a rotating magnetic disk to store data, and optical discs store data by altering a pigment layer on a plastic disk.

## Slide 22: Memory Controller
A piece of hardware that is mainly used for controlling the data flow going to/from the memory block.
Memory controllers facilitate access to heterogeneous physical devices, e.g., SRAM, DRAM, FLASH, hard disk.
Heterogeneous devices
Various data accesses
Electrical supports
Physical maintenance
Memory Controllers
Standard accessing interface
Application/OS
Notes: A memory controller is a piece of hardware that is mainly used for controlling the data flow going to/from the memory block. Some memory controllers can be connected to different kinds of devices at the same time, including SDRAM, SRAM, ROM, and memory mapped I/O. This facilitates memory access by providing a universal interface to the system, for example, to a standard bus interface.
A memory controller is also used to provide electrical support for some types of memory, for example, refreshing a DRAM.

## Slide 23: The Roles of a Memory Controller
The role of a memory controller includes:
  Interfacing with a particular type of memory block
  Facilitating memory access by providing a universal interface to the system, e.g., to a standard bus interface
  Supporting a variety of memory access modes, such as burst mode, memory paging, etc
  May provide electrical support for the memory, e.g., refreshing a DRAM
Notes: A memory controller plays a number of roles.
First, it manages read and write operations to the memory block. It selects the appropriate de-multiplexer circuit for data storage and retrieval.
Think of the memory on RAM block-like houses and the de-multiplexer circuit like a street address: in order to “mail” information to a specific house or to retrieve information from that house, the computer must know what address to use. The memory controller acts as the middleman in these operations, ensuring that the proper information is retrieved from the right locations.
A memory controller typically supports a variety of memory access modes, such as burst mode and memory paging. In the latter access mode, the OS retrieves data from the memory in same-size blocks called pages.
A memory controller is also used to provide electrical support for some types of memories, for example, refreshing a DRAM.

## Slide 24: Signal Description
Name | I/O | Description
Data [15:0] | I/O | 16-bit data input/output bus
Addr [25:0] | I | 26-bit address bus
RamCS | I | Chip select; activates the device when LOW
MemOE | I | Output enable: enables the output buffers when LOW
MemWR | I | Write enable: writes to the memory when LOW
RamLB | I | Lower byte enable
RamUB | I | Upper byte enable
RamClk | I | Additional clock input used to synchronize with the system; can be set to LOW as it is not needed in this teaching material
RamAdv | I | Address valid: indicates that a valid address is given on to the address bus; can be set to LOW as it is not needed in this teaching material
RamCre | I | Control register enable; can be set to LOW as it is not needed in this teaching material
RamWait | O | Provides data-valid feedback in the burst mode; not needed in this teaching material
Notes: This table sums up the signals involved in an AXI DDR interface with a 16-bit data bus and a 26-bit address bus. This interface will enable data transfers between the implemented SoC and an external DDR memory chip.
The twenty-six address bits are a combination of a 15-bit row addressing (32K) and an 11-bit column addressing (2K) for a total of 64M addressing at each memory bank.

## Slide 25: Example: Timing
The off-chip memory supports a variety of transfer modes (basic read and write timing graph below).
Copes with different data width, namely, merging two 16-bit data from the memory to form 32-bit data to be transferred through the AXI bus.
MemWR
Addr [25:0]
RamCS
MemOE
Address Valid
RamLB/UB
Data Valid
Data [15:0]
Address Valid
Data Valid
Notes: In addition to understanding the detailed interface of both the memory block and the bus, the design of the memory controller block requires a good understanding of the data transfer protocols supported by the bus and the target memory block. Most off-chip memories support a variety of transfer modes. The graph in this slide gives a basic read and write timing.
As a designer, you need to give special attention to the timing and values of the control signals during these transfers. This allows you to develop an accurate specification of the memory controller block, which can be modeled using one of the hardware description languages. In our case, the memory controller also has to cope with different data widths, namely merging two 16-bit data from the memory to form a 32-bit data, to be transferred through an AXI bus.