## Slide 1: Armv7-A/R ISA Overview (Part 2)

## Slide 2: Learning Outcomes
At the end of this module, you will be able to:
Outline behaviors of conditional and branch instructions.
Identify operations of coprocessor instructions.
Compute the results of DSP instructions when executed, including saturated math and count lead zero.

## Slide 3: Flow Control
Arm state
  Append a two-letter suffix to the mnemonic (conditional instruction), or
  use a conditional branch instruction.
    Almost all Arm instructions can be executed conditionally on the value of the condition flags in the Application Program Status Register (APSR).
    Using conditional branch instructions can be more efficient when a series of instructions depends on the same condition.
Thumb state
  Use an IT (If-Then) instruction, or
  use a conditional branch instruction.
    IT is a 16-bit instruction that enables almost all Thumb instructions to be conditionally executed, based on the value of the condition flags and the condition code suffix specified.
    Armv6T2 or later processors: instructions can also be conditionally executed by using CBZ and CBNZ.
Notes: To execute Arm instructions conditionally, you can either append a two-letter suffix to the mnemonic or use a conditional branch instruction. Almost all Arm instructions can be executed conditionally on the value of the condition flags in the APSR. You can either add a condition code suffix to the instruction or conditionally skip the instruction using a conditional branch instruction. Using conditional branch instructions to control the flow of execution can be more efficient, when a series of instructions depends on the same condition.
To execute Thumb instructions conditionally, you can use either an IT instruction or a conditional branch instruction. In Thumb state on processors before Armv6T2, the only mechanism for conditional execution is a conditional branch. You can conditionally skip the instruction using a conditional branch instruction.
In Thumb state on Armv6T2 or later processors, instructions can also be conditionally executed by using CBZ and CBNZ instructions. You can also use the IT or “if-then” instruction.

## Slide 4: Branch Instructions
Branch instructions have the following format:
B{<cond>} label
  Might not cause a pipeline flush (branch prediction)
  Branch range depends on instruction set and width.
  A BL instruction additionally generates a return address in r14 (lr).
  Returning is performed by restoring the program counter (pc) from lr.
:
BL func2
:
:
BX lr
func1
func2
void func1 (void)
{ :
func2();
:
}
Notes: There are branch instructions that you can use as well, such as B and BL.
The B instruction causes a branch to a label specified. The branch range depends on the instruction set and the width.
The BL instruction causes a branch to label specified and copies the address of the next instruction into Link Register (R14).
Ranges: Machine-level B instructions have restricted ranges from the address of the current instruction. However, you can use these instructions even if the label is out of range. Often, you do not know where the linker places the label. When necessary, the linker adds code to enable longer branches. The added code is called a veneer.

## Slide 5: Interworking
Interworking can be carried out using the branch exchange instruction.
  BX Rn
  BLX Rn
Bit 0 of Rn determines the exchange behavior.
  Unset : change to (or remain in) Arm state.
  Set: change to (or remain in) Thumb state.
  Branch and link with exchange
  Used to branch to a subroutine, which is known to be in the opposite instruction set
  When branching to imported labels, use BL; the linker will substitute BLX if necessary.
  BLX offset ; Arm/Thumb instruction which always ; changes state (and sets LR)
  All instructions that modify the PC can cause a state change.
  Depending on bit 0 of the result
  For data processing instructions, state changes only if S variant is snot used.
Notes: Interworking enables you to mix Arm and Thumb code so that Arm routines can return to a Thumb state caller and Thumb routines can return to an Arm state caller.
This can be beneficial if you compile or assemble code for interworking because your code can call a routine in a different module without considering which instruction set it uses. The compiler and assembler both use the --apcs=/interwork command-line option to enable interworking. You can freely mix code compiled or assembled for Arm and Thumb, provided that the code conforms to the Arm Architecture Procedure Call Standard (AAPCS).
There are two instructions that allow you to perform interworking: BX and BLX.
BX stands for Branch and Exchange instruction set. If bit 0 of the register Rn is 0, then the processor changes or remains in Arm state. If bit 0 is set to 1, then the processor changes or remains in Thumb state.
BLX stands for Branch with Link and Exchange instruction set. It is used to branch to a subroutine, which is known to be in the opposite instruction set. Specifically, it causes a branch to label, or to the address contained in register Rn. In addition, the BLX instruction copies the address of the next instruction into the Link Register (R14, the link register), and the BLX instruction can change the instruction set.
BLX offset always changes the instruction set.
BLX Rm derives the target instruction set from bit[0] of Rm.
You can use the linker to fix up calls to routines that use a different instruction set from the caller, by using BL to call the routine, or you can write your code to make the instruction set changes explicitly. In some circumstances, you can write smaller or faster code by doing this. You can use BX, BLX, LDR, LDM, and POP instructions to perform the instruction set state changes.
BX: Causes a branch to the address contained in Rn and exchanges the instruction set, if required.
BLX: Causes a branch to label, or to the address contained in Rn. In addition, the BLX instruction copies the address of the next instruction into LR (R14, the link register), and the BLX instruction can change the instruction set.
BLX offset always changes the instruction set.
BLX Rm derives the target instruction set from bit[0] of Rm.

## Slide 6: Compare and Branch if Zero
Replaces a CMP followed by a branch
  BUT does not affect condition code flags
Syntax
  CB{N}Z <Rn>, <label>
    CBZ: If Rn is equal to zero, branch to label
    CBNZ: If Rn is not equal to zero, branch to label
Can only branch forward between 4 and 130 bytes
.
CMP r0, #0
BEQ exit
.
exit
.
CBZ r0, exit
.
.
exit
Notes: The Compare (CMP) and Compare Negative (CMN) are instructions that compare the value in a register with Operand 2. They update the condition flags on the result but do not place the result in any register.
On the other hand, the compare and branch if zero instructions, which are CBZ and CBNZ, basically replaces a CMP followed by BEQ instruction as shown in the diagram in this slide. However, the condition code flags are not affected.
The Compare and Branch on Zero (CBZ) instruction compares and branch on zero,
The Compare and Branch Not Zero (CBNZ) instructions compare and branch on nonzero.
Therefore, you can use the CBZ or CBNZ instructions to avoid changing the condition flags and to reduce the number of instructions, which can be useful for jumping out of a loop.

## Slide 7: Conditional Instructions
Arm and Thumb instructions can execute conditionally on the condition flags set by a previous instruction.
The conditional instruction can occur either:
  Immediately after the instruction that updated the flags
  After any number of intervening instructions that have not updated the flags
The instructions that you can make conditional depends on whether the processor is in Arm state or Thumb state.
To make an instruction conditional, you must add a condition code suffix to the instruction mnemonic.
  The condition code suffix enables the processor to test a condition based on the flags.
  If the condition test of a conditional instruction fails, the instruction:
    Does not execute
    Does not write any value to its destination register
    Does not affect any of the flags
    Does not generate any exception
Notes: Conditional instructions are instructions that can execute if the condition flags are set by a previous instruction.
The conditional instruction can either be executed immediately after the condition flag is updated or after any number of intervening instructions that have not updated the flags.
Note that instructions that you can make conditional depends on which state you are in, whether you are in Arm state or Thumb state.
You can make an instruction conditional by adding a code suffix to the instruction mnemonic. For example, {cond} in BLX{cond}{q} label. The condition code suffix enables the processor to test a condition based on the flags.
If the condition test of a conditional instruction fails, the instruction does not execute, does not write any value to its destination register, does not affect any of the flags, and does not generate any exception.
At this point, you may wonder why use conditional instructions instead of conditional branches.
It can be more efficient to use conditional instructions rather than conditional branches. Conditional execution of Arm instructions reduces the number of branch instructions in your code, and therefore improves code density. As explained later, the IT instruction in Thumb achieves a similar improvement.
Branch instructions are also expensive in processor cycles. On Arm processors without branch prediction hardware, it typically takes three processor cycles to refill the processor pipeline each time a branch is taken. Some Arm processors, for example, the Arm Cortex-R7 processor, have branch prediction hardware. In systems using these processors, the pipeline only has to be flushed and refilled when there is a misprediction.

## Slide 8: Reference: Condition Codes and Flags
The possible condition codes are listed below.
  Note AL is the default and does not need to be specified.
Not equal
Unsigned higher or same
Unsigned lower
Minus
Equal
Overflow
No overflow
Unsigned higher
Unsigned lower or same
Positive or Zero
Less than
Greater than
Less than or equal
Always
Greater or equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N=!V
Status Flag | Meaning
N | Negative
Z | Zero
C | Carry
V | Overflow
By default, data processing instructions do not affect the condition flags but this can be achieved by placing an “S” between the instruction and any condition code.
Notes: The optional condition code is shown in syntax descriptions as {cond}. The optional condition is encoded in Arm instructions and encoded in a preceding IT instruction for Thumb instructions. An instruction with a condition code is only executed if the condition flags in the Application Program Status Register meet the specified condition.
The possible condition codes and the corresponding flags tested are listed in this slide. Note that AL is the default and does not need to be specified.
By default, data processing instructions do not affect the condition flags, but this can be achieved by placing an “S” between the instruction and any condition code.
In Thumb state on processors before Armv6T2, the {cond} field is only permitted on certain branch instructions because there is no IT instruction on these processors.

## Slide 9: If-Then
Thumb only, makes the next one to four instructions conditional
Syntax
IT{T|E}{T|E}{T|E} <cond>
  Any condition code may be used.
  Doesn’t affect condition flags
  16-bit instructions in the IT block do not affect condition flags (except CMP, CMN, & TST).
  32-bit instructions do affect condition flags (normal rules apply).
  No need to write this instruction: the assembler will insert it for you where necessary.
Current if-then status stored in CPSR
  Conditional block may be safely interrupted and returned to.
  Not recommended to branch into or out of if-then block
; if (r0 == 0) ; r0 = *r1 + 2; ; else ; r0 = *r2 + 4;
; if CMP r0, #0 ITTEE EQ
; then LDREQ r0, [r1] ADDEQ r0, #2
; else LDRNE r0, [r2] ADDNE r0, #4
Notes: The IT or “If Then” instruction makes up to four following instructions (the IT block) conditional. The conditions can be all the same, or some of them can be the logical inverse of the others.
The syntax of the IT instruction is shown in this slide. It has three “fields” {T|E} and a condition. In each field, T stands for “Then”, and E stands for “Else”. The first field specifies the condition switch for the second instruction in the IT block, the second field is for the third instruction, and the third field is for the fourth instruction. The condition in the syntax specifies the condition for the first instruction in the IT block.
The instructions, including branches, in the IT block, except the BKPT instruction, must specify the condition in the {cond} part of their syntax. Any condition code may be used.
With the exception of CMP, CMN, and TST, the 16-bit instructions that normally affect the condition flags do not affect them when used inside an IT block. 32-bit instructions do affect condition flags, normal rules apply.
You are not required to write IT instructions in your code because the assembler generates them for you automatically according to the conditions specified in the following instructions. However, if you do write IT instructions, the assembler validates the conditions specified in the IT instructions against the conditions specified in the following instructions.
The current “if-then” status is stored in the CPSR. Conditional block may be safely interrupted and returned to, but it is not recommended to branch into or out of the if-then block.
That is, if you write:
MOVNE r0, r1
the assembler will generate
IT NE
MOVNE r0, r1
Note that writing the IT instructions ensures that you consider the placing of conditional instructions, and the choice of conditions, in the design of your code. When assembling to Arm code, the assembler performs the same checks but does not generate any IT instructions.
A BKPT instruction in an IT block is always executed, so it does not require a condition in the {cond} part of its syntax. The IT block continues from the next instruction.

## Slide 10: Example: Conditional Execution
if (r0 == 0)
{
r1 = r1 + 1;
}
else
{
r2 = r2 + 1;
}
pseudocode
CMP r0, #0
IT NE
BNE else
ADD r1, r1, #1
B end
else
ADD r2, r2, #1
end
...
assembler instructions
inefficient branching
CMP r0, #0
ITE EQ
ADDEQ r1, r1, #1
ADDNE r2, r2, #1
...
no branching
Notes: This slide shows an example of conditional code execution.
The code on the left is a C code with an if-else condition.
The code in the middle is the assembler instructions corresponding to the C code. It uses inefficient branching.
The code on the right is the assembler instructions, and it uses no branching. Notice that the assembly code for this is shorter.
Some other examples:
if (a==0) func(1); if (a==0) x=0; if (a==4 || a==10) x=0;
CMP r0,#0 if (a>0) x=1; CMP r0,#4
MOVEQ r0,#1 CMP r0,#0 CMPNE r0,#10
BLEQ func MOVEQ r1,#0 MOVEQ r1,#0

## Slide 11: Supervisor Call (SVC)
Syntax
SVC{<cond>} <SVC number>
  Causes an SVC exception
  The SVC handler can examine the SVC number to decide what operation has been requested.
    But the core ignores the SVC number.
  By using the SVC mechanism, an OS can implement a set of privileged operations, which applications running in user mode can request.
Notes: The Supervisor Call or SVC instruction causes an exception. This means that the processor mode changes to supervisor, the CPSR is saved to the supervisor mode SPSR, and execution branches to the SVC vector. In effect, an SVC is a user-defined instruction. This is used for calling the OS (switches to privileged mode).
In this slide, the syntax for the SVC instruction is shown. The SVC number field can be used to specify the operation code. For example, SVC 1 starts a new task, SVC 2 allocates memory, and so on. The SVC handler can examine the SVC number to decide what operation has been requested. However, the SVC number is ignored by the processor.
The advantage of using a number is that the OS can have different revisions, and the same application code will work on each OS revision.

## Slide 12: Coprocessor Instructions
The instructions for each coprocessor occupy a fixed part of the Arm instruction set.
  If the appropriate coprocessor is not present in the system, an Undefined Instruction exception occurs.
There are three types of coprocessor instruction:
  Data processing
    CDP: Initiate a coprocessor data processing operation.
  Register transfer
    MRC: Move to Arm register from coprocessor register.
    MCR : Move to coprocessor register from Arm register.
  Memory transfers
    LDC: Load coprocessor register from memory.
    STC: Store from coprocessor register to memory.
Multiple register and other variants of these instructions are also available.
Notes: The instruction set distinguishes up to sixteen coprocessors with a 4-bit field in each coprocessor instruction, so each coprocessor is assigned a particular number. The encoding for each coprocessor instruction includes the number of the coprocessor in the system that should execute that particular instruction.
There are three types of coprocessor instruction, and there are for data processing, register transfer, and memory transfers.
The CPD instruction initiates a coprocessor data processing operation. This means that the coprocessor performs some processing on its own (e.g., read from coprocessor registers, perform calculation, and write back to coprocessor registers). Arm does not have to stall to wait for this operation to complete, which allows parallel processing. Coprocessor needs to interlock or stall any further operations.
The coprocessor instructions for register transfers include the MRC and MCR instructions. These instructions transfer register value between coprocessor and Arm registers. Arm does not perform any processing, but the coprocessor can (e.g., convert floating point reg to integer during the transfer). Arm partially decodes the instruction and sends or receives a 32-bit register value over the coprocessor interface.
The coprocessor instructions for memory transfers include LDC and STC. These instructions load or store between memory and coprocessor registers. Arm performs the addressing (Arm register + offset), and the data is transferred to or from the coprocessor. It is possible to load multiple words into coprocessors as the coprocessors would signal when to stop. Coprocessor could also perform an operation while words are loaded.
There are other variants of these instructions too. For more information, see the Arm Compiler armasm User Guide and the Armv7 Architecture Reference Manual.
Examples are MOVE coprocessor and VFP coprocessor. MOVE is loaded with an 8×8 pixel block from one frame and then performs sum of absolute differences, while an 8×8 pixel block is loaded in from various positions in the second frame.

## Slide 13: PSR Access
MRS and MSR allow contents of CPSR to be transferred to/from a general-purpose register or take an immediate value.
  MSR allows the whole status register, or just parts of it, to be updated.
  MRS r0,CPSR ; read CPSR into r0
  BIC r0,r0,#0x80 ; clear bit 7 to enable IRQ
  MSR CPSR_c,r0 ; write modified value to ‘c’ byte only
CPS can be used to directly modify some bits in the CPSR.
SETEND instruction selects the endianness of data accesses (BE8 or LE).
  For use in systems with mixed-endian data (e.g., peripherals)
SETEND BE LDR r0, [r7], #4 ; big-endian SETEND LE LDR r1, [r7], #4 ; little-endian
Notes: In this slide, we will look at accessing Program Status Registers.
The MRS and MSR instructions move the contents of the Current Program Status Register (also known as CPSR) to or from an Arm core register. For example, MSR allows the whole status register or a part of it to be updated. See the example code shown in the slide, where MRS, BIC, and MSR are used to modify the control bits of the CPSR (bit A, I, F, T, and mode bits of the CPSR, bottom eight bits of CPSR).
To directly modify the bits in the CPSR, use the CPS instruction.
You can also set the endianness bit in the CPSR, without affecting any other bits in the CPSR by using the SETEND instruction.
  MRS: Moves the contents of a program status register (PSR) to a general-purpose register
  MSR: Loads an immediate value, or the contents of a general-purpose register, into the specified fields of a PSR
  CPS (change processor state): Changes one or more of the modes, A, I, and F bits in the CPSR, without changing the other CPSR bits. CPS is only permitted in privileged software execution and has no effect in user mode.
  SETEND: Sets the endianness bit in the CPSR, without affecting any other bits in the CPSR
The condition flags in the APSR are normally set by executing data-processing instructions and normally control the execution of conditional instructions. However, software can set the condition flags explicitly using the MSR instruction and can read the current state of the condition flags explicitly using the MRS instruction.
At the system level, software can also use these instructions to access the SPSR of the current mode or use the CPS instruction to change the CPSR.M field and the CPSR.{A, I, F} interrupt mask bits.

## Slide 14: Miscellaneous Instructions
Breakpoint instruction - BKPT <bkpt number>
  Immediate value is ignored by the processor.
  Execution of this instruction will either cause a Prefetch Abort or cause the processor to enter Debug state (depends on the core design and configuration).
  Used by debug agents
Wait for interrupt: WFI
  Puts the core into Standby mode
  Woken by an interrupt or debug event
  Previously implemented as a CP15 operation
No operation: NOP
  Can be used as padding to align following instructions
  May or may not take time to execute
Wait for event (WFE) and send event (SEV)
  Covered elsewhere in the course
Notes: There are several miscellaneous instructions that you might find useful, for example, the breakpoint instruction, the WFI instruction, the No operation instruction, WFE instruction, and set event instruction.
The Breakpoint (BKPT) instruction causes the processor to enter Debug state. Debug tools can use this to investigate system state when the instruction at a particular address is reached. With a similarity to the SVC instruction, the breakpoint is fully user (debugger) defined and allows a debugger interface to allow information to be carried with every breakpoint.
The architecture allows the instruction to either force a Prefetch Abort (for Real-Time debugging) or to pass directly into Debug state.
BKPT instructions are unconditional.
RVI allows you to choose whether to use BKPT or a magic number (0xEEEEEEEE/0xEEEE) for software interrupts.
WFI is a hint instruction. It puts the processor into a Standby mode. The processor can be woken up from Standby mode by an interrupt or debug event. It is optional whether this instruction is implemented or not. If this instruction is not implemented, it executes as an NOP. The assembler produces a diagnostic message if the instruction executes as an NOP on the target. WFI suspends execution until one of the following events occur:
  An IRQ interrupt, regardless of the CPSR I-bit
  An FIQ interrupt, regardless of the CPSR F-bit
  An imprecise Data Abort, unless masked by the CPSR A-bit
  A debug entry request, regardless of whether debug is enabled
NOP instruction does nothing. It can be used as padding to align instructions. If NOP is not implemented as a specific instruction on your target architecture, the assembler treats it as a pseudo-instruction and generates an alternative instruction that does nothing, such as MOV r0, r0 (Arm) or MOV r8, r8 (Thumb).
NOP is not necessarily a time-consuming NOP. The processor might remove it from the pipeline before it reaches the execution stage.
WFE instruction is a hint instruction that permits the processor to enter a low-power state until one of a number of events occurs, including events signaled by executing the SEV instruction on any processor in the multiprocessor system.
SEV is a hint instruction. It causes an event to be signaled to all processors in the multiprocessor system.

## Slide 15: DSP Instructions Overview
These DSP instructions are single instruction multiple data (SIMD).
  They operate on 8- or 16-bit quantities packed into words.
  They allow more efficient access to packed structure types.
Instruction groups
  Data packing/unpacking
  Data processing
  Saturated maths
  Addition/subtraction
  Multiplication
  Sum of absolute differences
Notes: The DSP instructions are Single Instruction Multiple Data, or SIMD, instructions. SIMD technology uses a single instruction to perform the same operation in parallel on multiple data elements of the same type and size. In this way, the hardware that normally adds two 32-bit values instead performs four parallel additions of 8-bit values in the same amount of time.
The DSP instructions operate on 8- or 16-bit quantities packed into words and allow more efficient access to packed structure types.
The DSP instructions consist of instructions for data packing and processing, saturated maths, addition, subtraction, multiplication, and sum of absolute differences.

## Slide 16: Saturated Maths and CLZ
Support for saturated mathematics
  Targeted at DSP and control applications
  Overflow sets Q flag (sticky) not V, and sets result to +/- max value.
  QSUB{cond} Rd, Rm, Rn ; Rd = saturate(Rm - Rn)
  QADD{cond} Rd, Rm, Rn ; Rd = saturate(Rm + Rn)
  QDSUB{cond} Rd, Rm, Rn ; Rd = saturate(Rm - saturate(Rn2))
  QDADD{cond} Rd, Rm, Rn ; Rd = saturate(Rm + saturate(Rn2))
  Count leading zeros
  CLZ{cond} Rd, Rm
  Returns number of unset bits before the most significant set bit
0x0
0x7FFFFFFF
0x80000000
-ve
+ve
0
31
0
0
0
0
0
0
0
0
0
0
1
0
1
1
0
0
0
1
0
0
1
1
1
0
0
1
1
1
0
1
0
0
CLZ returns 10 in this case
Notes: What is saturated maths?
Saturated maths is integer arithmetic in which a result that would be greater than the largest representable number is set to the largest representable number, and a result that would be less than the smallest representable number is set to the smallest representable number. Signed saturated arithmetic is often used in DSP algorithms. It contrasts with the normal signed integer arithmetic used in Arm processors, in which overflowing results wrap around from +2^31–1 to –2^31 or vice versa.
Saturating instructions recognize this type of event and saturate the result at either the most negative value for subtract or the most positive value for addition.
Note that the overflow sets the Q flag and not the V flag.
The QADD/QDADD/QSUB/QDSUB instructions, which are also shown in this slide, do not affect the N, Z, C, or V flags. These instructions all saturate their results.
For the QDSUB instruction, saturation can occur on the doubling operation, on the subtraction, or on both. If saturation occurs on the doubling but not on the subtraction, the Q flag is set but the final result is unsaturated.
The Count Leading Zeros, or CLZ, instruction counts the number of leading zeros and returns the result. In other words, it returns the number of unset bits before the most significant set bit. So, if bit 31 is set in a 32-bit register, the result is zero.

## Slide 17: Saturation
Saturate a value to a specified bit position (effectively saturating to any power of 2).
  USAT: Unsigned saturate 32-bit
  Syntax: USAT Rd, #sat, Rm {shift}
  Operation: Rd = Saturate(Shift(Rm), #sat)
  Variants
  SSAT
  signed saturation
  USAT16
  saturates two 16-bit unsigned halfwords (no rotation allowed)
  SSAT16
  signed saturation of two 16-bit halfwords (no rotation allowed)
  #sat is specified as an immediate value in the range 0 to 31.
  {shift} is optional and is limited to LSL or ASR.
  Q flag is set if saturation occurs.
0
0
0
1
1
max
1
1
1
0
0
min
0
0
1
1
1
saturation position
max
(unsigned saturation)
(signed saturation)
Notes: There are also instructions you can use to saturate a value to a specified bit position, effectively saturating to any power of 2.
The USAT instruction applies a specified shift to a signed value and then saturates to an unsigned range (0 ≤ x ≤ 2^sat – 1).
The syntax for the USAT instruction is shown in the slide:
The #sat field is specified as an immediate value in the range 0 to 31.
The {shift} field is optional and is limited to LSL or ASR operations.
Rm is the register containing the operand and Rd is the destination register.
The Q flag is set if saturation happens.
There are also other variations such as SSA, USAT16, and SSAT16. For more information, see the Arm Compiler armasm User Guide and the Armv7 Architecture Reference Manual.
SSAT: Signed saturate to any bit position, with optional shift before saturating
The SSAT instruction applies the specified shift and then saturates a signed value to the signed range –2sat–1 ≤ x ≤ 2^(sat–1) –1.
So, the effect of this operation would be
Rm = 0x00450FFF
Using SSAT Rd, #23, Rm would return Rd as 0x003FFFFF with the Q flag set.
Using USAT16 Rd, #10, Rm would return Rd as 0x004507FF with the Q flag set (will be set by either halfword saturating).

## Slide 18: SIMD
Armv6 added a number of instructions that perform SIMD operations using Arm registers.
  Includes instructions for addition, subtraction, multiplication, and sum of absolute differences
  Instructions can work on four 8-bit quantities or two 16-bit quantities.
  Signed/unsigned and saturating versions of many instructions available
  CPSR GE bits used instead of normal ALU flags
  There are instructions for packing (PKHBT and PKHTB) and unpacking (UXTH & UXTB) registers.
+
Rs
+
Rm
UADD16 Rd, Rm, Rs
Rd
GE[3:2]
GE[1:0]
Notes: The Armv6 architecture introduced a small set of SIMD instructions, operating on multiple 16-bit or 8-bit values packed into standard 32-bit general-purpose registers. This permits certain operations to execute twice or four times as quickly, without implementing additional computation units. The mnemonics for these instructions are recognized by having 8 or 16 appended to the base form, indicating the size of data values operated on.
For the SIMD instruction, the CPSR GE bits are used instead of the normal ALU flags.
The UADD16 instruction is a SIMD instruction that does unsigned parallel halfword-wise addition. In other words, this instruction performs two unsigned integer additions on the corresponding halfwords of the operands and writes the results into the corresponding halfwords of the destination as shown in the slide. The results are modulo of 2^16. It sets the CPSR GE flags.
Some examples of the SIMD instructions are UADD16, UQADD8, and QSUB16. There are also instructions for packing and unpacking registers.
UQADD8: Unsigned saturating parallel byte-wise addition. This instruction performs four unsigned integer additions on the corresponding bytes of the operands and writes the results into the corresponding bytes of the destination. It saturates the results to the unsigned range 0 ≤ x ≤ 2^8 –1. The Q flag is not affected even if this operation saturates.
QSUB16: Signed saturating parallel halfword-wise subtraction. This instruction subtracts each halfword of the second operand from the corresponding halfword of the first operand and writes the results into the corresponding halfwords of the destination. It saturates the results to the signed range –2^15 ≤ x ≤ 2^15 –1. The Q flag is not affected even if this operation saturates.

## Slide 19: Appendix: Encoding Choice
When assembling for a Thumb-2 processor, there is often a choice of 16-bit and 32-bit instruction encodings.
  The assembler will normally generate 16-bit instructions.
Thumb-2 instruction width specifiers
  Allow you to determine which instruction width the assembler will use
  Can be placed immediately after instruction mnemonics
  .W: Forces a 32-bit instruction encoding
  .N: Forces a 16-bit instruction encoding
  Assembler will raise an error if the selected encoding is not possible.
Disassembly rules
  One-to-one mapping is defined to ensure correct reassembly.
  .W or .N suffix used for cases when a bit pattern that doesn’t follow the above rules is disassembled.
Notes: Disassembly sometimes will not match what you wrote in the first place because the rules for disassembly force the choice of one of the number of options. The disassembler will append .W or .N to an instruction that does not follow the normal assembly rules to ensure that reassembly will produce the same result as the original. 2-operand Thumb ADD is disassembled using the 2-operand form (rather than the default 3-operand form) to ensure that it will reassemble to the same bit pattern.
The assembler is not 100% WYSIWYG. Some warnings exist, which are suppressed by default:
  “—diag_warning 1645” will warn when armasm has changed one instruction to another (e.g., ADD to equivalent SUB).
  “—diag_warning 1763” warns when armasm generates an IT block (SP1 only).
sp/lr/pc should be used in preference to register names to reflect the fact that the syntax attaches special significance to these particular registers.