## Slide 1: The Arm Cortex-M33 Processor Architecture

## Slide 2: Learning Objectives
At the end of this lecture, you should be able to:
Outline the features and benefits of the Arm Cortex-M33 processor.
Outline the functions of the Cortex-M33 processor components including Nested Vectored Interrupt Controller (NVIC), Wakeup Interrupt Controller (WIC), Memory Protection Unit (MPU), Bus Interconnect and Debug System.
Describe the Cortex-M33 processor core registers including their functions.

## Slide 3: Module syllabus
Cortex-M33 Memory Map
  Cortex-M33 Memory Map
  Bit-band Operations
  Cortex-M3 Program Image and endianness
Arm Cortex-M33 processor instruction set
  Arm and Thumb instruction set
  Cortex-M33 instruction set

## Slide 4: Arm Cortex-M33 memory map
The Cortex-M33 processor has 4GB of memory address space
  Support for bit-band operation (detailed later)
The 4GB memory space is architecturally defined with a number of regions
  Each region is designed for particular recommended uses
  Easy for software programmer to port between different devices
Note that, despite the default definitions, the actual usage of the memory map can also be flexibly defined by the user, apart from some fixed memory addresses such as the internal private peripheral bus.
An address can have security level associated with it when the Armv8‑M Security Extension is included. This is determined by either the internal Secure Attribution Unit (SAU) or an external Implementation Defined Attribution Unit (IDAU) in the system.
Notes: The Arm Cortex-M33 memory map describes the organization of the processor’s address space. The address space contains data sources and sinks such as internal and external RAM and ROM as well as buses, peripherals, and further parts and equipment.
The total memory space of a 32bit system, like the Cortex-M33, is 2^32 = 4GB. It is split and separated into regions with different functionality which can be individually changed, apart from some fixed assigned addresses, e.g., of the internal private peripheral bus of the processor.

## Slide 5: Arm Cortex-M33 memory map
Private peripherals
e.g. NVIC, SCS
Mainly used for external peripherals
e.g. SD card
Mainly used for external memories
e.g. external DDR, FLASH, LCD
Mainly used for on-chip peripherals
e.g. AHB, APB peripherals
Mainly used for data memory
e.g. on-chip SRAM, SDRAM
Mainly used for program code
e.g. on-chip FLASH. Instruction and data accesses on C-AHB
Vendor specific
Memory
External device
External RAM
Peripherals
SRAM
Code
0xFFFFFFFF
0xE0000000
Private Peripheral Bus
(PPB)
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE0100000
Reserved for other purposes
ROM table
External PPB
Embedded Trace Macrocell
Trace Port Interface Unit
Reserved
System Control Space, including
Nested Vectored Interrupt
Controller (NVIC)
Reserved
Fetch patch and breakpoint unit
Data Watchpoint and Trace unit
Instrumentation Trace Macrocell
External PPB
Internal PPB
Notes: The Arm architecture uses a single flat address space of 2^(32) 8bit bytes. Byte addresses are treated as unsigned numbers running from 0 to 2^(32) - 1 The above figure shows the memory regions of ARMv8-M architecture. Each region has a defined memory type, and some regions have additional memory attributes. The memory type and attributes determine the behavior of accesses to the region.

## Slide 6: Arm Cortex-M33 memory map
Code region
  Primarily used to store program code
  Can also be used for data memory
  On-chip memory, such as on-chip FLASH
SRAM region
  Primarily used to store data, such as heaps and stacks
  Can also be used for program code
  On-chip memory; despite its name “SRAM”, the actual device could be SRAM, SDRAM, etc
Peripheral region
  Primarily used for peripherals, such as Advanced High-performance Bus (AHB) or Advanced Peripheral Bus (APB) peripherals
  On-chip peripherals
Notes: The Code region with 0x00000000- 0x1FFFFFFF address range is the executable region for the program core. Data can also be put here.
The SRAM region with 0x20000000- 0x3FFFFFFF address range is the executable region for data. Code can also be put here. This region includes the bit band and bit band alias areas.
The Peripheral region with 0x40000000- 0x5FFFFFFF address range is used for peripherals attached to the core on the address and data bus. This region includes bit band and bit band alias areas.

## Slide 7: Arm Cortex-M33 memory map
External RAM region
  Primarily used to store large data blocks or memory caches
  Off-chip memory, slower than on-chip SRAM region
External device region
  Primarily used to map to external devices
  Off-chip devices, such as SD card
Private Peripheral Bus (PPB)
  Provides access to internal and external processor resources
Notes: The External region 0x60000000 - 0x9FFFFFFF address range is the executable region for data.
The External device region with 0xA0000000 - 0xDFFFFFFF address range is the external device memory, which is primarily used to map external devices.
The Private Peripheral Bus region with 0xE0000000 - 0xE00FFFFF address range provides access to internal and external processor resources.

## Slide 8: Bit-band operations
Bit-band operations allow a single load/store operation to access a single bit in the memory, for example, to change a single bit of one 32-bit data:
  Normal operation without bit-band (read-modify-write)
          Read the value of 32-bit data
          Modify a single bit of the 32-bit value (keep other bits unchanged)
          Write the value back to the address
  Bit-band operation
          Directly write a single bit (0 or 1) to the “bit-band alias address” of the data
Bit-band alias address
  Each bit-band alias address is mapped to a real data address
  When writing to the bit-band alias address, only a single bit of the data will be changed
Notes: For bit-wise data manipulations with 32-bit operations, Arm has introduced an alternative: the bit band operations.
The standard operation without bit-band is read-modify-write: First, we load a full 32bit word into the registers. Then, we manipulate the corresponding bit with AND, OR, XOR instructions in full word length, and, finally, we write the word back. If this operation (read-modify-write) is interrupted, there can be a data loss. One way to avoid data loss is the interrupt disabling using a supervisor mode or by using bit banding operations.
Using bit-band operation, the corresponding data word is bitwise aliased into bit-band-memory area. So every original bit has now the aliased size of a word. The bits to be manipulated can be directly accessed with word wise operating instructions. Because of the aliasing, everything modified within the “linked copy” of the data will directly be changed in the original data.

## Slide 9: Bit-band operation example
For example, in order to set bit[3] in word data in address 0x20000000:
Read-modify-write operation
  Reads the data (0x21) from the address 0x20000000
  The interrupt changes the data of 0x20000000 address to 0x79 and then returns
  Writes back the modified old data back
  0x79 has been lost!
;Read-Modify-Write Operation
LDR R1, =0x20000000 ;Setup address
LDR R0, [R1] ;Read 0x21
ORR.W R0, #0x8 ;Set bit[3]
STR R0, [R1] ;Write back 0x29
Interrupt!
...
LDR R1, =0x20000000 ;Setup address
STR R2,[R1] ;Write back 0x79
...
Return!
Notes:   Let’s say that we want to set bit[3] in word data in address 0x20000000.
  Usually we read the data from the address, then modify them and, finally, we write back the new value.
  In this example, you can see that the read-modify-write cycle is interrupted, and the value of the address 0x20000000 is changed by the ISR right after reading the data from the address.
  After returning from the routine, the application continues its normal execution but the modification and write back will be done based on the old value. Consequently, the change that was made by the ISR will be lost.

## Slide 10: Bit-band operation example
Bit-band operation
  Directly set the bit by writing ‘1’ to address 0x2200000C, which is the alias address of the fourth bit of the 32-bit data at 0x20000000
  In effect, this single instruction is mapped to 2 bus transfers: read data from 0x20000000 to the buffer, and then write to 0x20000000 from the buffer with bit [3] set
;Bit-band Operation
LDR R1, =0x2200000C ;Setup address
MOV R0, #1 ;Load data
STR R0, [R1] ;Write
Notes: Alternatively, using the bit band operation you can see that we set the desired bit by writing ‘1’ to the alias address and, with a single instruction, we can set the desired bit of the 0x20000000 address to 1, thereby avoiding any data loss.

## Slide 11: Bit-band alias address
Each bit of the 32-bit data is one-to-one mapped to the bit-band alias address
  For example, the fourth bit (bit [3]) of the data at 0x20000000 is mapped to the bit-band alias address at 0x2200000C
  Hence, to set bit [3] of the data at 0x20000000, we only need to write ‘1’ to address 0x2200000C
  In Cortex-M33, there are two pre-defined bit-band alias regions: one for SRAM region, and one for peripherals region
0x20000000
0x20000004
0x20000008
Real 32-bit data address
0x22000000
0x22000080
0x22000100
0x2200000C
0x22000018
Bit-band alias address
Notes: The SRAM-area 0x20000000-0x200FFFFF may be directly accessed and manipulated by 32-Bit-instructions in the bit-band alias area 0x22000000-0x23FFFFFF, simulating and bitwise manipulation as every original bit is mapped to a byte:
0x22000000 equals Bit 0 of 0x20000000
0x22000004 equals Bit 1 of 0x20000000
0x22000008 equals Bit 2 of 0x20000000
0x22000020 equals Bit 0 of 0x20000001
...
bit-band-address = bit-band-basis-address + (byte-offset × 32) + bit[0-7] × 4)
0x22000020 = 0x22000000 + 1 × 32 + 0 × 4

## Slide 12: Bit-band alias address
SRAM region
  32MB memory space (0x22000000 – 0x23FFFFFF) is used as the bit-band alias region for 1MB data (0x20000000 – 0x200FFFFF)
Peripherals region
  32MB memory space (0x42000000 – 0x43FFFFFF) is used as the bit-band alias region for 1MB data (0x40000000 – 0x400FFFFF)
External RAM
Peripherals
SRAM
Code
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1MB Bit-band region
32MB Bit-band alias
31MB non-bit-band region
0x20000000
0x20100000
0x22000000
0x23FFFFFF
0x21FFFFFF
1MB Bit-band region
32MB Bit-band alias
31MB non-bit-band region
0x40000000
0x40100000
0x42000000
0x43FFFFFF
0x41FFFFFF
Notes: SRAM and Peripheral regions include bit band and bit band alias areas.

## Slide 13: Benefits of bit-band operations
Faster bit operations
Fewer instructions
Atomic operation, avoid hazards
  For example, if an interrupt is triggered and served during the read-modify-write operations, and the interrupt service routine modifies the same data, a data conflict will occur
Interrupt occurs
Read data at 0x00
Modify bit [1]
Read data at 0x00
Modify bit [1]
Write data back
Write data back
Interrupt returns
Bit [1] modified by ISR is overwritten
by the main program
Interrupt Service Routine
Main program
Notes: Bit-band operations require fewer (in fact, only one) instruction, and therefore are called “atomic” because they cannot be split further.
This also protects them from data corruptions by interrupts that could modify the just read memory. If the bit manipulation is performed in the traditional way, the memory block is read first, and directly after the reading an interrupt occurs. Such an interrupt could theoretically modify the just read data in their original destination. After the interrupt releases the processor again, the bit manipulation continues and writes the modified, but not out dated, data back; therefore, a data corruption has occurred.
This cannot happen with bit band operations, because they modify the data within one single step.

## Slide 14: Cortex-M33 program image
The program image in Cortex-M33 contains
  Vector table – includes the starting addresses of exceptions (vectors) and the value of the main stack point (MSP)
  C start-up routine
  Program code – application code and data
  C library code – program codes for C library functions
0x00000000
Code region
Start-up routine &
Program code &
C library code
Vector table
Program
Image
Initial MSP value
Reset vector
NMI vector
Hard fault vector
MemManage fault
Reserved
PendSV
SysTick
External Interrupts
Bus fault
Usage fault
Reserved
SVCall
Debug monitor
Notes: A program starting at 0x00000000 is subdivided into the following parts. First, the vector tables are located. Vector tables are created because many overarching features of a controller bitwise features – such as interrupts. To save memory space, they are consolidated to bytes or words, so-called bit vectors. Therefore, a vector needs to be evaluated bitwise to interpret the meaning or origin of the change. The size of the vector table is 64Byte + 4 byte for each used interrupt vector. The start-up routine, the program code, and static libraries are located beyond the vector table.

## Slide 15: Cortex-M33 program image
After reset, the processor:
  First reads the initial MSP value
  Then reads the reset vector
  Then branches to the start of the program execution address (reset handler)
  Subsequently executes program instructions
Reset
Fetch initial value for MSP
(Read address 0x00000000)
Fetch reset vector
(Read address 0x00000004)
Fetch 1st instruction
(Read address of reset vector)
Fetch 2nd instruction
(Read subsequent instructions)
Notes: After reset, the MSP initializes the address of the beginning of the stack. Then, the reset vector defines the address of the first line of executable code and is located at address 0x00000004. From now on, the program can be started and executed line by line.

## Slide 16: Cortex-M33 endianness
Endian refers to the order of bytes stored in memory
  Big-endian: lowest byte of a word-size data is stored in bit 0 to bit 7
  Big-endian: lowest byte of a word-size data is stored in bit 24 to bit 31
Cortex-M33 supports both little-endian and big-endian
However, endianness only exists in the hardware level
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
0x00000000
0x00000004
0x00000008
Address
[7:0]
[15:8]
[23:16]
[31:24]
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
[7:0]
[15:8]
[23:16]
[31:24]
Word 1
Word 2
Word 3
Word 1
Word 2
Word 3
Little-endian 32-bit memory
Big-endian 32-bit memory
Notes: Endianness describes the order in which bytes have to be combined in halfwords or words. For Arm architectures, the endianness has little significance as either word wise operations (4 bytes) are performed automatically in the correct order by the instruction set, or the information is stored in single bytes regardless of any endianness.
Endianness is only important if halfwords (2 bytes) are manually stored byte wise. In this case, we must consider whether the most significant byte is stored first or last. If the most significant byte is stored at the highest bit positions, this is called “little endianness”. On the other hand, if the most significant byte is stored at the lowest bit positions, this is called “big endianness”.

## Slide 17: Arm Cortex-M33 processor instruction set and Thumb instruction set
Early Arm instruction set
  32-bit instruction set, called the Arm instructions
  Powerful and good performance
  Larger program memory compared to 8-bit and 16-bit processors
  Larger power consumption
Thumb-1 instruction set
  16-bit instruction set, first used in ARM7TDMI processor in 1995
  Provides subset of Arm instructions, with better code density compared to 32-bit RISC architecture
  Code size is reduced by ~30%, but performance is also reduced by ~20%
Notes: The Arm standard instruction set is 32 bits long with three operand formats for load and store operations, where most instructions can be executed conditionally and in a single cycle. One side effect of the early Arm instruction set is that is required larger program memory than 8-bit or 16-bit processors, and larger power consumption as more information needed to be moved.
By comparison, Thumb-1 is a 16‐bit instruction set which is optimized for code density from C code. It is a subset of the Arm instruction set functionality with better code density, but worse performance. Thumb instructions are executed unconditionally, and many of the data processing instructions use a 2‐address format. As a result of the dense encoding, Thumb instruction formats are less regular than Arm instruction formats.

## Slide 18: Arm and Thumb instruction set
Mix of Arm and Thumb-1 Instruction sets
  Benefit from both 32-bit Arm (high performance) and 16-bit Thumb-1 (high code density)
  A multiplexer is used to switch between two states: Arm state (32-bit) and Thumb state (16-bit), which requires a switching overhead
Thumb-2 instruction set
  Consists of both 32-bit Thumb instructions and original 16-bit Thumb-1 instruction sets
  Compared to 32-bit Arm instructions set, code size is reduced by ~26%, with similar performance
  Capable of handling all processing requirements in one operation state
Incoming
Instructions
Thumb remap
to Arm
Arm
Instruction
decoder
Instructions
Executing
T bit, 0: select Arm,
1: select Thumb
0
1
Notes: In earlier processor architectures, Arm and Thumb 1 instructions could be mixed, but required switching a multiplexer between the two instruction sets. That reduces the speed due to the switching overhead.
Thumb-2 is a superset of the Thumb instruction set. Thumb-2 introduces 32-bit instructions that are mixed with the 16-bit instructions. The Thumb-2 instruction set covers almost all the functionality of the Arm instruction set. Thumb-2 is backwards compatible with the ARMv6 Thumb instruction set.
The most important difference between the Thumb-2 instruction set and the Arm instruction set is that most Thumb-2 instructions are unconditional, where as almost all Arm instructions can be conditional.
Thumb-2’s performance is close to or better than that of the Arm instruction set, and has the code density of the original Thumb 1.

## Slide 19: Cortex-M33 instruction set
Cortex-M33 processor
  ARMv8-M architecture
  Supports 32-bit Thumb-2 instructions
  Can handle all processing requirements in one operation state (Thumb state)
  Compared with traditional Arm processors (which use state switching), advantages include:
          No state switching overhead – both execution time and instruction space are saved
          No need to separate Arm code and Thumb code source files, which makes the development and maintenance of software easier
          Easier to get optimized efficiency and performance
Notes: The Cortex-M33 implements the ARMv8-M instruction set. ARMv8-M supports a large number of 32-bit instructions that Thumb-2 technology introduced into the Thumb instruction set. The Floating-point (FP) extension adds single-precision floating-point instructions to the Thumb instruction set.
The Thumb instruction stream is a sequence of halfword-aligned halfwords. Each Thumb instruction is either a single 16-bit halfword in that stream, or a 32-bit instruction consisting of two consecutive halfwords in that stream.

## Slide 20: Cortex-M33 instruction set
Arm assembly syntax:
  label
    mnemonic operand1, operand2, … ; Comments
  Label is used as a reference to an address location
  Mnemonic is the name of the instruction
  Operand1 is the destination of the operation
  Operand2 is normally the source of the operation
  Comments are written after “ ; ”, which does not affect the program, e.g.:
  MOVS R3, #0x11 ;Set register R3 to 0x11
  Assembly code can be assembled by either Arm assembler (armasm) or assembly tools from a variety of vendors (e.g. GNU toolchain). When using the GNU toolchain, the syntax for labels and comments is slightly different.
Notes: Labels are symbolic representations of addresses. You can use labels to mark specific addresses that you want to refer to from other parts of the code.
Mnemonic is the name of the instruction. Most data processing instructions can optionally update the condition flags according to the result of the operation. You can also execute an instruction conditionally, based on the condition flags set in another instruction, either immediately after the instruction that updated the flags, or after any number of intervening instructions that have not updated the flags.
Conditional execution is available by using conditional branches or by adding condition code suffixes to instructions. The condition code suffix enables the processor to test a condition based on the flags. If the condition test of a conditional instruction fails, then the instruction does not execute, does not write any value to its destination register, does not affect any of the flags and does not generate any exception.
An instruction operand can be an Arm register, a constant, or another instruction-specific parameter.
Instructions act on the operands and often store the result in a destination register.
When there is a destination register in the instruction, it is usually specified before the operands.
Note that instruction mnemonics, pseudo-instructions, directives, and symbolic register names can be written in all uppercase or all lowercase, but not mixed. Labels and comments can be in uppercase or lowercase, or mixed.

## Slide 21: Arm Cortex-M33 Instruction Set - Overview
Instructions supported by the Cortex-M33 processor can be grouped as follows:
  Memory access instructions
  General data processing instructions
  Multiply and divide instructions
  Saturating instructions
  Packing and unpacking instructions
  Bitfield instructions
  Branch and control instructions
  Miscellaneous instructions
  Floating-point instructions
Notes: Memory access instructions:
Addresses can be accessed directly by indicating the explicit or relative address to which the content is stored. It can also be accessed indirectly, by pointing to an address where the address for the content is stored. Indirect addressing is a particular advantage if large fields need to be manipulated, e.g. sorted, and the data of one element are not limited to a single memory cell, but are a structure of many memory elements. In this case, the addresses of the root elements are sorted, which is less effort than sorting the elements themselves.
General data processing instructions:
The instructions for general data processing contain everything for mathematical operations, bit manipulation and comparison.
  Multiply and divide instructions:
There are two ways to multiply and divide. The first is to right- and left-shift the bits of a number (division by two and multiplication by two, respectively) and the second is bitwise multiplication and addition.
  Saturating instructions:
Saturating instructions cover data-range over- and underflow for different kinds of integer and floating-point additions and subtractions.
  Packing and unpacking instructions:
  Packing and unpacking contain range and precision changing operations.
  Bitfield instructions:
Bitfield instructions are designed for a similar purpose as packing and unpacking instructions. If two bitfields of different length have to be processed for logical operation, then their sizes have to be aligned.
  Branch and control instructions:
Control structures are used if the control must be transferred to another part of the instruction space, or when the next PC must not be executed.
Branches are conditional transfers of control, when the target address is close to the current PC location.
Jumps are unconditional transfers of control with unpredictable distance of jump.
  Miscellaneous instructions:
Further, unclassified instructions are mainly used for superordinate actions like debugging, interrupting, and synchronization.
Floating-point instructions:
Floating point instructions are instructions that deal with floating point registers and operations.

## Slide 22: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
ADCS | {Rd,} Rn, Op2 | Add with Carry | N,Z,C,V
ADD, ADDS | {Rd,} Rn, Op2 | Add | N,Z,C,V
ADD, ADDW | {Rd,} Rn, #imm12 | Add | -
ADR | Rd, label | Address to Register | -
AND, ANDS | {Rd,} Rn, Op2 | Logical AND | N,Z,C
ASR, ASRS | Rd, Rm, <Rs¦#n> | Arithmetic Shift Right | N,Z,C
B {cond} | label | Branch {conditionally} | -
BFC | Rd, #lsb, #width | Bit Field Clear | -
BFI | Rd, Rn, #lsb, #width | Bit Field Insert | -
BIC, BICS | {Rd,} Rn, Op2 | Bit Clear | N,Z,C
BKPT | #imm8 | Breakpoint | -
BL | label | Branch with Link | -
BLX | Rm | Branch indirect with Link and Exchange | -

## Slide 23: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
BLXNS | Rm | Branch indirect with Link and Exchange, Non-secure | -
BX | Rm | Branch and Exchange | -
BXNS | Rm | Branch and Exchange, Non-secure | -
CBNZ | Rn, label | Compare and Branch on Non Zero | -
CBZ | Rn, label | Compare and Branch on Zero | -
CDP, CDP2 | {cond} coproc, #op1, Rt, CRn, CRm{, #op2} | Coprocessor Data Processing | -
CLREX | - | Clear Exclusive | -
CLZ | Rd, Rm | Count Leading Zeros | -
CMN | Rn, Op2 | Compare Negative | N,Z,C,V
CMP | Rn, Op2 | Compare | N,Z,C,V
CPSID | i | Change Processor State, Disable Interrupts | -
CPSIE | i | Change Processor State, Enable Interrupts | -
DMB | {opt} | Data Memory Barrier | -

## Slide 24: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
DSB | {opt} | Data Synchronization Barrier | -
EOR, EORS | {Rd,} Rn, Op2 | Exclusive OR | N,Z,C
FLDMDBX ,FLDMIAX | Rn | FLDMX (Decrement Before, Increment After) loads | -
FSTMDBX,FSTMIAX | Rn | FSTMX (Decrement Before, Increment After) stores | -
ISB | {opt} | Instruction Synchronization Barrier | -
IT | - | If Then condition block | -
LDA | Rd, [Rn] | Load-Acquire Word | 
LDAB | Rd, [Rn] | Load-Acquire Byte | 
LDAEX | Rd, [Rn] | Load-Acquire Exclusive Word | -
LDAEXB | Rd, [Rn] | Load-Acquire Exclusive Byte | -
LDAEXH | Rd, [Rn] | Load-Acquire Exclusive Halfword | -
LDAH | Rd, [Rn] | Load-Acquire Halfword | -
LDM | Rn{!}, reglist | Load Multiple | -

## Slide 25: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
LDMDB, LDMEA | Rn{!}, reglist | Load Multiple Decrement Before | -
LDMIA, LDMFD | Rn{!}, reglist | Load Multiple, Increment After | -
LDR | Rt, [Rn, Rm {, LSL #shift}] | Load Register Word (register offset) | -
LDR | Rt, label | Load Register Word (literal) | -
LDR, LDRT | Rt, [Rn, #offset] | Load Register Word (immediate offset, unprivileged) | -
LDRB | Rt, [Rn, Rm {, LSL #shift}] | Load Register Byte (register offset) | -
LDRB | Rt, label | Load Register Byte (literal) | -
LDRB, LDRBT | Rt, [Rn, #offset] | Load Register Byte (immediate offset, unprivileged) | -
LDRD | Rt, Rt2, [Rn, #offset] | Load Register Dual (immediate offset) | -
LDRD | Rt, Rt2, label | Load Register Dual (PC- relative) | -
LDREX | Rt, [Rn, #offset] | Load Register Exclusive | -
LDREXB | Rt, [Rn] | Load Register Exclusive Byte | -
LDREXH | Rt, [Rn] | Load Register Exclusive Halfword | -
LDRH | Rt, [Rn, Rm {, LSL #shift}] | Load Register Halfword (register offset) | -

## Slide 26: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
LDRH | Rt, label | Load Register Halfword (literal) | -
LDRH, LDRHT | Rt, [Rn, #offset] | Load Register Halfword (immediate offset, unprivileged) | -
LDRSB | Rt, [Rn, Rm {, LSL #shift}] | Load Register Signed Byte (register offset) | -
LDRSB | Rt, label | Load Register Signed Byte (PC-relative) | -
LDRSB, LDRSBT | Rt, [Rn, #offset] | Load Register Signed Byte (immediate offset, unprivileged) | -
LDRSH | Rt, [Rn, Rm {, LSL #shift}] | Load Register Signed Halfword (register offset) | -
LDRSH | Rt, label | Load Register Signed Halfword (PC-relative) | -
LDRSH, LDRSHT | Rt, [Rn, #offset] | Load Register Signed Halfword (immediate offset, unprivileged) | -
LSL, LSLS | Rd, Rm, <Rs¦#n> | Logical Shift Left | N,Z,C
LSR, LSRS | Rd, Rm, <Rs¦#n> | Logical Shift Right | N,Z,C
MCR,MCR2 | {cond} coproc, #opc1, Rt, CRn, CRm{, #opc2} | Move to Coprocessor from Register | -
MCRR,MCRR2 | {cond} coproc, #opc1, Rt, Rt2, CRm | Move to Coprocessor from two Registers | -
MLA | Rd, Rn, Rm, Ra | Multiply Accumulate | -

## Slide 27: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
MLS | Rd, Rn, Rm, Ra | Multiply and Subtract | -
MOV, MOVS | Rd, Op2 | Move | N,Z,C
MOV, MOVS | Rd, Rm | Move (register) | N,Z
MOVT | Rd, #imm16 | Move Top | -
MOVW | Rd, #imm16 | Move 16-bit constant | N,Z,C
MRC,MRC2 | {cond} coproc, #opc1, Rt, CRn, CRm{, #opc2} | Move to Register from ¦Coprocessor | -
MRRC,MRRC2 | {cond} coproc, #opc1, Rt, Rt2, CRm | Move to two Registers from Coprocessor. | -
MRS | Rd, spec_reg | Move from Special Register to general register | -
MSR | spec_reg, Rn | Move from general register to Special Register | -
MUL, MULS | {Rd,} Rn, Rm | Multiply | N,Z
MVN, MVNS | Rd, Op2 | Bitwise NOT | N,Z,C
NOP | - | No Operation | -
ORN, ORNS | {Rd,} Rn, Op2 | Logical OR NOT | N,Z,C

## Slide 28: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
ORR, ORRS | {Rd,} Rn, Op2 | Logical OR | N,Z,C
PKHTB, PKHBT | {Rd,} Rn, Rm, {, Op2} | Pack Halfword | -
PLD | [Rn {, #offset}] | Preload Data | -
POP | reglist | Pop registers from stack | -
PUSH | reglist | Push registers onto stack | -
QADD | {Rd,} Rn, Rm | Saturating Add | Q
QADD16 | {Rd,} Rn, Rm | Saturating Add 16 | -
QADD8 | {Rd,} Rn, Rm | Saturating Add 8 | -
QASX | {Rd,} Rn, Rm | Saturating Add and Subtract with Exchange | -
QDADD | {Rd,} Rn, Rm | Saturating Double and Add | Q
QDSUB | {Rd,} Rn, Rm | Saturating Double and Subtract | Q
QSAX | {Rd,} Rn, Rm | Saturating Subtract and Add with Exchange | -
QSUB | {Rd,} Rn, Rm | Saturating Subtract | Q

## Slide 29: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
QSUB16 | {Rd,} Rn, Rm | Saturating Subtract 16 | -
QSUB8 | {Rd,} Rn, Rm | Saturating Subtract 8 | -
RBIT | Rd, Rn | Reverse Bits | -
REV | Rd, Rn | Reverse byte order in a word | -
REV16 | Rd, Rn | Reverse byte order in each halfword | -
REVSH | Rd, Rn | Reverse byte order in bottom halfword and sign extend | -
ROR, RORS | Rd, Rm, <Rs¦#n> | Rotate Right | N,Z,C
RRX, RRXS | Rd, Rm | Rotate Right with Extend | N,Z,C
RSB, RSBS | {Rd,} Rn, Op2 | Reverse Subtract | N,Z,C,V
SADD16 | {Rd,} Rn, Rm | Signed Add 16 | GE
SADD8 | {Rd,} Rn, Rm | Signed Add 8 | GE
SASX | {Rd,} Rn, Rm | Signed Add and Subtract with Exchange | GE
SBC, SBCS | {Rd,} Rn, Op2 | Subtract with Carry | N,Z,C,V

## Slide 30: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
SBFX | Rd, Rn, #lsb, #width | Signed Bit Field Extract | -
SDIV | {Rd,} Rn, Rm | Signed Divide | -
SEL | {Rd,} Rn, Rm | Select bytes | GE
SEV | - | Send Event | -
SG | - | Secure Gateway | -
SHADD16 | {Rd,} Rn, Rm | Signed Halving Add 16 | -
SHADD8 | {Rd,} Rn, Rm | Signed Halving Add 8 | -
SHASX | {Rd,} Rn, Rm | Signed Halving Add and Subtract with Exchange | -
SHSAX | {Rd,} Rn, Rm | Signed Halving Subtract and Add with Exchange | -
SHSUB16 | {Rd,} Rn, Rm | Signed Halving Subtract 16 | -
SHSUB8 | {Rd,} Rn, Rm | Signed Halving Subtract 8 | -
SMLABB, SMLABT, SMLATB, SMLATT | Rd, Rn, Rm, Ra | Signed Multiply Accumulate halfwords | Q
SMLAD, SMLADX | Rd, Rn, Rm, Ra | Signed Multiply Accumulate Dual | Q

## Slide 31: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
SMLAL | RdLo, RdHi, Rn, Rm | Signed Multiply Accumulate Long (32 × 32 + 64), 64-bit result | -
SMLALBB, SMLALBT, SMLALTB, SMLALTT | RdLo, RdHi, Rn, Rm | Signed Multiply Accumulate Long, halfwords | -
SMLALD, SMLALDX | RdLo, RdHi, Rn, Rm | Signed Multiply Accumulate Long Dual | -
SMLAWB, SMLAWT | Rd, Rn, Rm, Ra | Signed Multiply Accumulate, word by halfword | Q
SMLSD, SMLSDX | Rd, Rn, Rm, Ra | Signed Multiply Subtract Dual | Q
SMLSLD, SMLSLDX | RdLo, RdHi, Rn, Rm | Signed Multiply Subtract Long Dual | -
SMMLA, SMMLAR | Rd, Rn, Rm, Ra | Signed Most Significant Word Multiply Accumulate | -
SMMLS, SMMLSR | Rd, Rn, Rm, Ra | Signed Most Significant Word Multiply Subtract | -
SMMUL, SMMULR | Rd, Rn, Rm | Signed Most Significant Word Multiply | -
SMUAD, SMUADX | {Rd,} Rn, Rm | Signed Dual Multiply Add | Q.
SMULBB, SMULBT, SMULTB, SMULTT | {Rd,} Rn, Rm | Signed Multiply (halfwords) | -
SMULL | RdLo, RdHi, Rn, Rm | Signed Multiply Long (32 × 32), 64-bit result | -
SMULWB, SMULWT | {Rd,} Rn, Rm | Signed Multiply word by halfword | -

## Slide 32: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
SMUSD, SMUSDX | {Rd,} Rn, Rm | Signed Dual Multiply Subtract | -
SSAT | Rd, #n, Rm {,shift #s} | Signed Saturate | Q
SSAT16 | Rd, #n, Rm | Signed Saturate 16 | Q
SSAX | {Rd,} Rn, Rm | Signed Subtract and Add with Exchange | GE
SSUB16 | {Rd,} Rn, Rm | Signed Subtract 16 | GE
SSUB8 | {Rd,} Rn, Rm | Signed Subtract 8 | GE
STL | Rt, [Rn] | Store-Release Word | -
STLB | Rt, [Rn] | Store-Release Byte | -
STLEX | Rt, Rt [Rn] | Store-Release Exclusive Word | -
STLEXB | Rt, Rt [Rn] | Store-Release Exclusive Byte | -
STLEXH | Rt, Rt [Rn] | Store-Release Exclusive Halfword | -
STLH | Rt, [Rn] | Store-Release Halfword | -
STM | Rn{!}, reglist | Store Multiple | -

## Slide 33: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
STMDB, STMEA | Rn{!}, reglist | Store Multiple Decrement Before | -
STMIA, STMFD | Rn{!}, reglist | Store Multiple Increment After | -
STR | Rt, [Rn, Rm {, LSL #shift}] | Store Register Word (register offset) | -
STR, STRT | Rt, [Rn, #offset] | Store Register Word (immediate offset, unprivileged) | -
STRB | Rt, [Rn, Rm {, LSL #shift}] | Store Register Byte (register offset) | -
STRB, STRBT | Rt, [Rn, #offset] | Store Register Byte (immediate offset, unprivileged) | -
STRD | Rt, Rt2, [Rn, #offset] | Store Register Dual two words | -
STREX | Rd, Rt, [Rn, #offset] | Store Register Exclusive | -
STREXB | Rd, Rt, [Rn] | Store Register Exclusive Byte | -
STREXH | Rd, Rt, [Rn] | Store Register Exclusive Halfword | -
STRH | Rt, [Rn, Rm {, LSL #shift}] | Store Register Halfword (register offset) | -
STRH, STRHT | Rt, [Rn, #offset] | Store Register Halfword (immediate offset, unprivileged) | -
SUB, SUBS | {Rd,} Rn, Op2 | Subtract | N,Z,C,V

## Slide 34: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
SUB, SUBW | {Rd,} Rn, #imm12 | Subtract | -
SVC | #imm | Supervisor Call | -
SXTAB | {Rd,} Rn, Rm {,ROR #n} | Sign extend 8 bits to 32 and Add | -
SXTAB16 | {Rd,} Rn, Rm {,ROR #n} | Sign extend two 8-bit values to 16 and Add | -
SXTAH | {Rd,} Rn, Rm {,ROR #n} | Sign extend 16 bits to 32 and Add | -
SXTB | Rd, Rm {,ROR #n} | Sign extend 8 bits to 32 | -
SXTB16 | {Rd,} Rm {,ROR #n} | Sign extend 8 bits to 16 | -
SXTH | {Rd,} Rm {,ROR #n} | Sign extend a Halfword to 32 | -
TBB | [Rn, Rm] | Table Branch Byte | -
TBH | [Rn, Rm, LSL #1] | Table Branch Halfword | -
TEQ | Rn, Op2 | Test Equivalence | N,Z,C
TST | Rn, Op2 | Test | N,Z,C
TT | Rd, [Rn] | Test Target | -

## Slide 35: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
TTA | Rd, [Rn] | Test Target Alternate Domain | -
TTAT | Rd, [Rn] | Test Target Alternate Domain Unprivileged | -
TTT | Rd, [Rn] | Test Target Unprivileged | -
UADD16 | {Rd,} Rn, Rm | Unsigned Add 16 | GE
UADD8 | {Rd,} Rn, Rm | Unsigned Add 8 | GE
UASX | {Rd,} Rn, Rm | Unsigned Add and Subtract with Exchange | GE
UBFX | Rd, Rn, #lsb, #width | Unsigned Bit Field Extract | -
UDF | {c}{q} {#}imm | Permanently Undefined. | -
UDIV | {Rd,} Rn, Rm | Unsigned Divide | -
UHADD16 | {Rd,} Rn, Rm | Unsigned Halving Add 16 | -
UHADD8 | {Rd,} Rn, Rm | Unsigned Halving Add 8 | -
UHASX | {Rd,} Rn, Rm | Unsigned Halving Add and Subtract with Exchange | -
UHSAX | {Rd,} Rn, Rm | Unsigned Halving Subtract and Add with Exchange | -

## Slide 36: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
UHSUB16 | {Rd,} Rn, Rm | Unsigned Halving Subtract 16 | -
UHSUB8 | {Rd,} Rn, Rm | Unsigned Halving Subtract 8 | -
UMAAL | RdLo, RdHi, Rn, Rm | Unsigned Multiply Accumulate Accumulate Long (32 × 32 + 32 + 32), 64-bit result | -
UMLAL | RdLo, RdHi, Rn, Rm | Unsigned Multiply Accumulate Long (32 × 32 + 64), 64-bit result | -
UMULL | RdLo, RdHi, Rn, Rm | Unsigned Multiply Long (32 × 32), 64-bit result | -
UQADD16 | {Rd,} Rn, Rm | Unsigned Saturating Add 16 | -
UQADD8 | {Rd,} Rn, Rm | Unsigned Saturating Add 8 | -
UQASX | {Rd,} Rn, Rm | Unsigned Saturating Add and Subtract with Exchange | -
UQSAX | {Rd,} Rn, Rm | Unsigned Saturating Subtract and Add with Exchange | -
UQSUB16 | {Rd,} Rn, Rm | Unsigned Saturating Subtract 16 | -
UQSUB8 | {Rd,} Rn, Rm | Unsigned Saturating Subtract 8 | -
USAD8 | {Rd,} Rn, Rm | Unsigned Sum of Absolute Differences | -
USADA8 | Rd, Rn, Rm, Ra | Unsigned Sum of Absolute Differences and Accumulate | -

## Slide 37: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
USAT | Rd, #n, Rm{,shift #s}, Ra | Unsigned Saturate | Q
USAT16 | Rd, #n, Rm | Unsigned Saturate 16 | Q
USAX | {Rd,} Rn, Rm | Unsigned Subtract and Add with Exchange | GE
USUB16 | {Rd,} Rn, Rm | Unsigned Subtract 16 | GE
USUB8 | {Rd,} Rn, Rm | Unsigned Subtract 8 | GE
UXTAB | {Rd,} Rn, Rm {,ROR #n} | Rotate, unsigned extend 8 bits to 32 and Add | -
UXTAB16 | {Rd,} Rn, Rm {,ROR #n} | Rotate, unsigned extend two 8-bit values to 16 and Add | -
UXTAH | {Rd,} Rn, Rm {,ROR #n} | Rotate, unsigned extend and Add Halfword | -
UXTB | Rd, Rm {,ROR #n} | Unsigned zero-extend Byte | -
UXTB16 | {Rd,} Rm {,ROR #n} | Unsigned zero-extend Byte 16 | -
UXTH | Rd, Rm {,ROR #n} | Unsigned zero-extend Halfword | -
VABS | .F32 Sd, Sm | Floating-point Absolute | -
VADD | .F32 {Sd,} Sn, Sm | Floating-point Add | -

## Slide 38: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
VCMP | .F32 Sd, <<Sm¦ #0.0> | Compare two floating-point registers, or one floating-point register and zero | N,Z,C,V
VCMPE | .F32 Sd, <<Sm¦ #0.0> | Compare two floating-point registers, or one floating-point register and zero with Invalid Operation check | N,Z,C,V
VCVT | .F32.Tm <Sd>, Sm | Convert from floating-point to integer | -
VCVT | .Td.F32 Sd, Sd, #fbits | Convert from floating-point to fixed point | -
VCVTA | .Tm.F32 <Sd>, Sm | Convert from floating-point to integer with directed rounding to nearest with Ties Away | -
VCVTB VCVTT | .F32.F16 Sd, Sm | Convert half-precision value to single-precision or double-precision | -
VCVTB VCVTT | .F16.F32 Sd, Sm | Convert single-precision or double-precision register to half-precision | -
VCVTM | .Tm.F32 <Sd>, Sm | Convert from floating-point to integer with directed rounding towards Minus infinity | -
VCVTN | .Tm.F32 <Sd>, Sm | Convert from floating-point to integer with directed rounding to nearest with Ties to even | -
VCVTP | .Tm.F32 <Sd>, Sm | Convert from floating-point to integer with directed rounding towards Plus infinity | -

## Slide 39: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
VCVTR | .Tm.F32 <Sd>, Sm | Convert between floating-point and integer with rounding. | -
VDIV | .F32 {Sd,} Sn, Sm | Floating-point Divide | -
VFMA | .F32 {Sd,} Sn, Sm | Floating-point Fused Multiply Accumulate | -
VFMS | .F32 {Sd,} Sn, Sm | Floating-point Fused Multiply Subtract | -
VFNMA | .F32 {Sd,} Sn, Sm | Floating-point Fused Negate Multiply Accumulate | -
VFNMS | .F32 {Sd,} Sn, Sm | Floating-point Fused Negate Multiply Subtract | -
VLDM | {mode}{.size} Rn{!}, list | Floating-point Load Multiple extension registers | -
VLDR | .F32 Sd, [<Rn> {, #offset}] | Floating-point Load an extension register from memory (immediate) | -
VLDR | .F32 Sd, <label> | Load an extension register from memory | -
VLDR | .F32 Sd, [PC,#-0] | Load an extension register from memory | -
VLLDM | <c> Rn | Floating-point Lazy Load multiple | -
VLSTM | <c> Rn | Floating-point Lazy Store multiple | -
VMAXNM | .F32 Sd, Sn, Sm | Maximum of two floating-point numbers with IEEE754-2008 NaN handling | -

## Slide 40: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
VMINNM | .F32 Sd, Sn, Sm | Minimum of two floating-point numbers with IEEE754-2008 NaN handling | -
VMLA | .F32 Sd, Sn, Sm | Floating-point Multiply Accumulate | -
VMLS | .F32 Sd, Sn, Sm | Floating-point Multiply Subtract | -
VMOV | <Sn¦Rt>, <Rt¦Sn> | Copy core register to single-precision | -
VMOV | <Sm¦Rt>, <Sm1¦Rt2>, <Rt¦Sm>, <Rt2¦Sm1> | Copy two core registers to two single-precision | -
VMOV | {.size} Dd[x], Rt | Copy core register to scalar | -
VMOV | {.dt} Rt, Dn[x] | Copy scalar to core register | -
VMOV | .F32 Sd, #immm | Floating-point Move immediate | -
VMOV | .F32 Sd, Sd, Sm | Copies the contents of one register to another | -
VMOV | <Dm¦Rt>, <Rt¦Rt2>, <Rt2¦Dm> | Floating-point Move transfers two words between two core registers and a doubleword register | -
VMRS | Rt, FPSCR | Move to core register from floating-point Special Register | N,Z,C,V
VMSR | FPSCR, Rt | Move to floating-point Special Register from core register | -

## Slide 41: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
VMUL | .F32 {Sd,} Sn, Sm | Floating-point Multiply | -
VNEG | .F32 Sd, Sm | Floating-point Negate | -
VNMLA | .F32 Sd, Sn, Sm | Floating-point Multiply Accumulate and Negate | -
VNMLS | .F32 Sd, Sn, Sm | Floating-point Multiply, Subtract and Negate | -
VNMUL | .F32 {Sd,} Sn, Sm | Floating-point Multiply and Negate | -
VPOP | {.size} list | Load multiple consecutive floating-point registers from the stack | -
VPUSH | {.size} list | Store multiple consecutive floating-point registers to the stack | -
VRINTA | .F32 Sd, Sm | Float to integer in floating-point format conversion with directed rounding to Nearest with Ties Away | -
VRINTM | .F32 Sd, Sm | Float to integer in floating-point format conversion with directed rounding to Minus infinity | -
VRINTN | .F32 Sd, Sm | Float to integer in floating-point format conversion with directed rounding to Nearest with Ties to even | -
VRINTP | .F32 Sd, Sm | Float to integer in floating-point format conversion with directed rounding to Plus infinity | -

## Slide 42: Cortex-M33 instruction set
Mnemonic | Operands | Brief description | Flags
VRINTR | .F32 Sd, Sm | Float to integer in floating-point format conversion with rounding towards value specified in FPSCR | -
VRINTX | .F32 Sd, Sm | Float to integer in floating-point format conversion with rounding specified in FPSCR | -
VRINTZ | .F32 Sd, Sm | Float to integer in floating-point format conversion with rounding towards Zero | -
VSEL | .F32 Sd, Sn, Sm | Select register, alternative to a pair of conditional VMOV | -
VSQRT | .F32 Sd, Sm | Calculates floating-point Square Root | -
VSTM | {mode}{.size} Rn{!}, list | Floating-point Store Multiple | -
VSTR | .F32 Sd, [Rn{, #offset}] | Floating-point Store Register stores an extension register to memory | -
VSUB | F32 {Sd,} Sn, Sm | Floating-point Subtract | -
WFE | - | Wait For Event | -
WFI | - | Wait For Interrupt | -
YIELD | - | Suspend task | -

## Slide 43: Cortex-M33 instruction set
Cortex-M33 suffix
  Some instructions can be followed by suffixes to update processor flags or execute the instruction on a certain condition
Suffix | Description | Example | Example explanation
S | Update APSR (flags) | ADDS R1, #0x21 | Add 0x21 to R1 and update APSR
EQ, NE, CS, CC, MI, PL, VS, VC, HI, LS, GE, LT, GT, LE | Condition execution e.g. EQ= equal, NE= not equal, LT= less than | BNE label | Branch to the label if not equal

## Slide 44: Data insertion and alignment
Insert data inside programs
  DCD: insert a word-size data
  DCB: insert a byte-size data
  ALIGN:
    used before inserting a word-size data
    Uses a number to determine the alignment size
For example:
  …
  ALIGN 4 ; Align to a word boundary
  MY_DATA DCD 0x12345678 ; Insert a word-size data
  MY_STRING DCB “Hello”, 0 ; Null terminated string
  …
Notes: DCB and DCD define the initial runtime contents of the memory. A DCB directive allocates one or more bytes of memory, whereas a DCD directive allocates one or more words of memory, aligned on 4-byte boundaries.
The ALIGN directive aligns the current location to a specified boundary, by padding with zeros or NOP instructions to ensure that the data and code is aligned to appropriate boundaries.

## Slide 45: Useful resources
Architecture Reference Manual:
  https://developer.arm.com/documentation/ddi0553/bp/
Cortex-M33 Technical Reference Manual:
  https://developer.arm.com/documentation/100230/latest
Cortex-M33 Devices Generic User Guide:
  https://developer.arm.com/documentation/100235/latest