## Slide 1: Timer Peripherals

## Slide 2: Learning Objectives
At the end of this lecture, you should be able to:
Describe the mode of operation and function of the interrupt timer.
Explain the three modes of operation of the standard timer including ‘compare mode’, capture mode’ and pulse width modulation mode.

## Slide 3: Outline
Types of Timer Peripherals
  Interrupt Timer
  PWM Module
  Low-Power Timer
  Real-Time Clock
  SYSTICK

## Slide 4: Types of Timer Peripherals
Interrupt Timer
  Can generate periodically generate interrupts or trigger DMA (direct memory access) transfers
PWM Module
  Connected to I/O pins, has input capture and output compare support
  Can generate PWM signals
  Can generate interrupt requests
Low-Power Timer
  Can operate as timer or counter in all power modes
  Can wake up system with interrupt
  Can trigger hardware
Real-Time Clock
  Powered by external 32.768 kHz crystal
  Tracks elapsed time (seconds) in register
  Can set alarm
  Can generate 1Hz output signal and/or interrupt
  Can wake up system with interrupt
SysTick
  Part of CPU core’s peripherals
  Can generate periodic interrupt

## Slide 5: Timer/Counter Peripheral Introduction
Common peripheral for microcontrollers
Based on presettable binary counter, enhanced with configurability
  Count value can be read and written by MCU
  Count direction can often be set to up or down
  Counter’s clock source can be selected
          Counter mode: count pulses which indicate events (e.g. odometer pulses)
          Timer mode: clock source is periodic, so counter value is proportional to elapsed time (e.g. stopwatch)
  Counter’s overflow/underflow action can be selected
          Generate interrupt
          Reload counter with special value and continue counting
          Toggle hardware output signal
Events
Clock
Current Count
Reload Value
Presettable Binary Counter
PWM
Interrupt
Reload
or

## Slide 6: Interrupt Timer

## Slide 7: Interrupt Timer
Load start value from register
Counter counts down with each clock pulse
When timer value reaches zero
  Generates interrupt
  Reloads timer with start value
Write 1000 to timer
max
Enabling timer loads counter with 1000, starts counting
Timer counts down to 0
Interrupt generated, counter reloads with 1000, starts counting
Write 700 to timer
max
Interrupt generated, counter reloads with 700, starts counting
Interrupt generated, counter reloads with 700, starts counting
Interrupt generated, counter reloads with 700, starts counting
Interrupt
Clock
Read current timer value
Presettable Binary Counter
Interrupt
Reload
Start Value
Read/write timer start value

## Slide 8: Calculating Max Value
Goal: generate an interrupt every T seconds
Max value = round(T * Freq)
  Round since register is an integer, not a real number
    Rounding provides closest integer to desired value, resulting in minimum timing error
Example: Interrupt every 137.41ms, assuming clock frequency 24MHz
  137.41ms * 24MHz = 3297840
Example: Interrupt with a frequency of 91Hz with a 12MHz clock
  (1/91 Hz) * 12MHz = round (131868.1318) = 131868
Use macros, interrupt 1000 times per second:
  CLK_FREQ / 1000

## Slide 9: Configuring the Interrupt Timer
Setup timer, set to tick at 10Hz
  timer_init(CLK_FREQ / 10);
Set interrupt
  timer_set_callback(timer_isr);
Enable module
  timer_enable();
Disable module
  timer_disable();

## Slide 10: Example: Stopwatch
Measure time with 100 us resolution
Display elapsed time, updating screen every 10ms
Controls
  S1: toggle start/stop
Use interrupt timer
  Counter increment every 100 us
          Set to timer to expire every 100 us
          Calculate max value, e.g. at 24 MHz = round (100 us * 24MHz -1) = 2399
  LCD Update every 10 ms
          Update LCD every nth ISR
          n = 10 ms/100us = 100
          Don’t update LCD in ISR! Too slow.
          Instead set flag in ISR, poll it in main loop

## Slide 11: Timer / PWM Module

## Slide 12: Timer / PWM Module
Core Counter
  Clock options - external or internal
  Prescaler to divide clock
  Can reload with set value, or overflow and wrap around
N channels
  3 modes
          Capture Mode: Capture timer’s value when input signal changes
          Output Compare: Change an output signal when timer reaches certain value
          PWM: Generate pulse-width-modulated signal. Width of pulse is proportional to specified value.
  Possible triggering of interrupt, hardware trigger on overflow
  One I/O pin per channel

## Slide 13: Major Channel Modes
Input Capture Mode
  Capture timer’s value when input signal changes
          Rising edge, falling edge, both
  How long after I started the timer did the input change?
          Measure time delay
Output Compare Mode
  Modify output signal when timer reaches specified value
          Set, clear, pulse, toggle (invert)
  Make a pulse of specified width
  Make a pulse after specified delay
Pulse Width Modulation
  Make a series of pulses of specified width and frequency

## Slide 14: Input Capture Mode
I/O pin operates as input on edge
When valid edge is detected on pin…
  Current value of counter is stored
  Interrupt is called
External Signal
Internal Counter
Value
Enable the module
Event on external signal
Fire interrupt with value saved
Fire interrupt with value saved

## Slide 15: Wind Speed Indicator (Anemometer)
Rotational speed (and pulse frequency) is proportional to wind velocity
Two measurement options:
  Frequency (best for high speeds)
  Width (best for low speeds)
Can solve for wind velocity v
How can we use the timer for this?
  Use Input Capture Mode to measure period of input signal

## Slide 16: TPM Capture Mode for Anemometer
Configuration
  Set up module to count at given speed from internal clock
  Set up channel for input capture on rising edge
Operation: Repeat
  First interrupt - on rising edge
          Reconfigure channel for input capture on falling edge
          Clear counter, start it counting
  Second interrupt - on falling edge
          Read capture value, save for later use in wind speed calculation
          Reconfigure channel for input capture on rising edge
          Clear counter, start it counting

## Slide 17: Output Compare Mode
Action on match
    Toggle
    Clear
    Set
When counter matches value …
  Output signal is generated
  Interrupt is called (if enabled)
Enable timer
Overflow
Overflow
Timer
Value
Toggle
Clear
Set
Output
Pin
Value
Compare Value

## Slide 18: Pulse-Width Modulation
Uses of PWM
  Digital power amplifiers are more efficient and less expensive than analog power amplifiers
          Applications: motor speed control, light dimmer, switch-mode power conversion
          Load (motor, light, etc.) responds slowly, averages PWM signal
  Digital communication is less sensitive to noise than analog methods
          PWM provides a digital encoding of an analog value
          Much less vulnerable to noise
PWM signal characteristics
  Modulation frequency – how many pulses occur per second (fixed)
  Period – 1/(modulation frequency)
  On-time – amount of time that each pulse is on (asserted)
  Duty-cycle – on-time/period
  Adjust on-time (hence duty cycle) to represent the analog value

## Slide 19: PWM Mode
PWM duty cycle proportional to compare value
  Period = max timer value
  Pulse width = compare value
Enable timer
Overflow
Overflow
Timer
Value
Output
Pin
Compare Value

## Slide 20: PWM to Drive Servo Motor
Servo PWM signal
  20 ms period
  1 to 2 ms pulse width

## Slide 21: Low Power Timer

## Slide 22: Low Power Timer Overview
Features
  Count time or external pulses
  Generate interrupt when counter matches compare value
  Interrupt wakes MCU from any low power mode
Current draw can be reduced to microamps or even nanoamps!
Use the WFI instruction (Wait For Instruction)
  Puts CPU in low power mode until interrupt request
Current
Time
Interrupt routine
Sleeping mode
Average
Current
Processor Always On
With Low-Power Timer