## Slide 1: Serial Communications

## Slide 2: Learning Objectives
At the end of this lecture, you should be able to:
Outline the concepts of both serial and parallel communication and give examples of their applications.
Explain the difference between synchronous and asynchronous serial communication.
Compare serial and parallel communication including their advantages and disadvantages.
Outline the difference between synchronous half-duplex and full-duplex serial buses
Describe UART and its communication protocol.
Describe SPI communication protocol.
Describe I2C communication protocol.

## Slide 3: Overview
Serial communications
  Concepts
  Tools
  Software: polling, interrupts, and buffering
Protocols:
  UART
  SPI
  I2C

## Slide 4: Why Communicate Serially?
Native word size is multi-bit (8, 16, 32, etc.)
Often it’s not feasible to support sending all the word’s bits at the same time
  Cost and weight: more wires needed, larger connectors needed
  Mechanical reliability: more wires => more connector contacts to fail
  Timing Complexity: some bits may arrive later than others due to variations in capacitance and resistance across conductors
  Circuit complexity and power: may not want to have 16 different radio transmitters + receivers in the system

## Slide 5: Example System: Voyager Spacecraft
Launched in 1977
Constraints: Reliability, power, size, weight, reliability, reliability, etc.
“Uplink communications are via S-band (16-bits/sec command rate) while an X-band transmitter provides downlink telemetry at 160 bits/sec normally and 1.4kbps for playback of high-rate plasma wave data. All data are transmitted from and received at the spacecraft via the 3.7 meters high-gain antenna (HGA).” http://voyager.jpl.nasa.gov/spacecraft/index.html
  Uplink – to spacecraft
  Downlink – from spacecraft
???

## Slide 6: Example System
Dedicated point-to-point connections
  Parallel data lines, read and write lines between MCU and each peripheral
Fast, allows simultaneous transfers
Requires many connections, PCB area, scales badly

## Slide 7: Parallel Buses
All devices use buses to share data, read, and write signals
MCU uses individual select lines to address each peripheral
MCU requires fewer pins for data, but still one per data bit
MCU can communicate with only one peripheral at a time

## Slide 8: Synchronous Serial Data Transmission
Use shift registers and a clock signal to convert between serial and parallel formats
Synchronous: an explicit clock signal is along with the data signal
Transmitting Device
Receiving Device
Clock
Serial Data
Data Sampling Time at Receiver

## Slide 9: Synchronous Full-Duplex Serial Data Bus
Now can use two serial data lines - one for reading, one for writing.
  Allows simultaneous send and receive full-duplex communication

## Slide 10: Synchronous Half-Duplex Serial Data Bus
  Share the serial data line
  Doesn’t allow simultaneous send and receive - is half-duplex communication

## Slide 11: Asynchronous Serial Communication
Eliminate the clock line!
Transmitter and receiver must generate clock locally
Transmitter must add start bit (always same value) to indicate start of each data frame
Receiver detects leading edge of start bit, then uses it as a timing reference for sampling data line to extract each data bit N at time Tbit*(N+1.5)
Stop bit is also used to detect some timing errors
Tbit*1.5
Data bits
Data Sampling Time at Receiver
Tbit*2.5
Tbit*3.5
Tbit*4.5
Tbit*5.5
Tbit*6.5
Tbit*7.5
Tbit*8.5
Tbit*9.5
Time Zero
Start bit
Stop bit

## Slide 12: Serial Communication Specifics
Data frame fields
  Start bit (one bit)
  Data (LSB first or MSB, and size – 7, 8, 9 bits)
  Optional parity bit is used to make total number of ones in data even or odd
  Stop bit (one or two bits)
All devices must use the same communications parameters
  E.g. communication speed (300 baud, 600, 1200, 2400, 9600, 14400, 19200, etc.)
Sophisticated network protocols have more information in each data frame
  Medium access control – when multiple nodes are on bus, they must arbitrate for permission to transmit
  Addressing information – for which node is this message intended?
  Larger data payload
  Stronger error detection or error correction information
  Request for immediate response (“in-frame”)
Message
Data bits
Start bit
Stop bit

## Slide 13: Error Detection
Can send additional information to verify data was received correctly
Need to specify which parity to expect: even, odd or none.
Parity bit is set so that total number of “1” bits in data and parity is even (for even parity) or odd (for odd parity)
  01110111 has 6 “1” bits, so parity bit will be 1 for odd parity, 0 for even parity
  01100111 has 5 “1” bits, so parity bit will be 0 for odd parity, 1 for even parity
Single parity bit detects if 1, 3, 5, 7 or 9 bits are corrupted, but doesn’t detect an even number of corrupted bits
Stronger error detection codes (e.g. Cyclic Redundancy Check) exist and use multiple bits (e.g. 8, 16), and can detect many more corruptions.
  Used for CAN, USB, Ethernet, Bluetooth, etc.

## Slide 14: Tools for Serial Communications Development
Tedious and slow to debug serial protocols with just an oscilloscope
Instead use a logic analyzer to decode bus traffic
Worth its weight in gold!
Saelae 8-Channel Logic Analyzer
  $150 (www.saelae.com)
  Plugs into PC’s USB port
  Decodes SPI, asynchronous serial, I2C, 1-Wire, CAN, etc.
Build your own: with Logic Sniffer or related open-source project

## Slide 15: Software Structure – Handling asynchronous Communication

## Slide 16: Software Structure
Communication is asynchronous to program
  Don’t know what code the program will be executing …
          when the next item arrives
          when current outgoing item completes transmission
          when an error occurs
  Need to synchronize between program and serial communication interface somehow
Options
  Polling
          Wait until data is available
          Simple but inefficient of processor time
  Interrupt
          CPU interrupts program when data is available
          Efficient, but more complex

## Slide 17: Serial Communications and Interrupts
Want to provide multiple threads of control in the program
  Main program (and subroutines it calls)
  Transmit ISR – executes when serial interface is ready to send another character
  Receive ISR – executes when serial interface receives a character
  Error ISR(s) – execute if an error occurs
Need a way of buffering information between threads
  Solution: circular queue with head and tail pointers
  One for tx, one for rx
Serial Interface
tx_isr
rx_isr
get_string
send_string
Main Program or other threads

## Slide 18: Code to Implement Queues
Enqueue at tail: tail is the index of the next free entry
Dequeue from head: head is the index of the item to remove
Queue size is initialized and stored in size
One queue per direction
  tx ISR unloads tx_q
  rx ISR loads rx_q
Other threads (e.g. main) load tx_q and unload rx_q
Need to wrap pointer at end of buffer to make it circular,
  Use % (modulus, remainder) operator if queue size is not power of two
  Use & (bitwise and) if queue size is a power of two
Queue is empty if tail == head
Queue is full if (tail + 1) % size == head
write data to tail
read data from head
older data
newer data
Serial
Interface
tx_isr
rx_isr
get_string
send_string

## Slide 19: Defining the Queues
typedef struct {
uint8_t *data; //!< Array of data, stored on the heap.
uint32_t head; //!< Index in the array of the oldest element.
uint32_t tail; //!< Index in the array of the youngest element.
uint32_t size; //!< Size of the data array.
} Queue;

## Slide 20: Initialization and Status Inquiries
int queue_init(Queue *queue, uint32_t size) {
queue->data = (uint8_t*)malloc(sizeof(uint8_t) * size);
queue->head = 0;
queue->tail = 0;
queue->size = size;
// If malloc returns NULL (0) the allocation has failed.
return queue->data != 0;
}
int queue_is_full(Queue *queue) {
return ((queue->tail + 1) % queue->size) == queue->head;
}
int queue_is_empty(Queue *queue) {
return queue->tail == queue->head;
}

## Slide 21: Enqueue and Dequeue
int queue_enqueue(Queue *queue, uint8_t item) {
if (!queue_is_full(queue)) {
queue->data[queue->tail++] = item;
queue->tail %= queue->size;
return 1;
} else {
return 0;
}
}
int queue_dequeue(Queue *queue, uint8_t *item) {
if (!queue_is_empty(queue)) {
*item = queue->data[queue->head++];
queue->head %= queue->size;
return 1;
} else {
return 0;
}
}

## Slide 22: Using the Queues
Sending data:
queue_enqueue(…, c)
Receiving data:
queue_dequeue(…, &c)

## Slide 23: Software Structure – Parsing Messages

## Slide 24: Decoding Messages
Two types of messages
  Actual binary data sent
    First identify message type
    Second, based on this message type, copy binary data from message fields into variables
          May need to use pointers and casting to get code to translate formats correctly and safely
  ASCII text characters representing data sent
          First identify message type
          Second, based on this message type, translate (parse) the data from the ASCII message format into a binary format
          Third, copy the binary data into variables

## Slide 25: Example Binary Serial Data: TSIP
switch (id) {
case 0x84:
lat = *((double *)(&msg[0]));
lon = *((double *)(&msg[8]));
alt = *((double *)(&msg[16]));
clb = *((double *)(&msg[24]));
tof = *((float *)(&msg[32]));
break;
case 0x4A: …
default:
break;
}
Type | sizeof(Type) | Item | Units
Double | 8 | Latitude | Radians; + for north, - for south
Double | 8 | Lonitude | Radians; + for east, - for west
Double | 8 | Altitude | Meters
Double | 8 | Clock Bias | Meters
Single | 4 | Time-of-fix | Seconds
Report Packet (0x84) Data Structure

## Slide 26: Example ASCII Serial Data: NMEA-0183
$IDMSG,D1,D2,D3,D4,…,Dn*CS\r\n
$ denotes the start of a message
ID is a two letter mnemonic to describe the source of data, e.g. GP signifies GPS
MSG is a three letter mnemonic to describe the message content.
Commas are used to delaminate the data fields.
Dn represents each of the data fields.
* is used to separate the data from the checksum.
CS contains two ASCII characters representing the hex value of the checksum.
\r\n is the carriage return character followed by the new line character to denote the end of a message.

## Slide 27: State Machine for Parsing NMEA-0183
Start
Talker + Sentence Type
Sentence Body
Checksum 1
Checksum 2
$ Append char to buf.
Any char. except *, \r or \n
Append char to buf. Inc. counter
*, \r or \n, non-text, or counter>6
buf==$SDDBT, $VWVHW, or $YXXDR
Enqueue all chars. from buf
Any char. except *
Enqueue char
*
Enqueue char
Any char.
Save as checksum1
/r or /n
Any char.
Save as checksum2

## Slide 28: Parsing
switch (parser_state) {
case TALKER_SENTENCE_TYPE:
switch (msg[i]) {
‘*’:
‘\r’:
‘\n’:
parser_state = START;
break;
default:
if (Is_Not_Character(msg[i]) || n>6) {
parser_state = START;
} else {
buf[n++] = msg[i];
}
break;
}
if ((n==6) & … ){
parser_state = SENTENCE_BODY;
}
break;
case SENTENCE_BODY:
break;

## Slide 29: Asynchronous serial (UART) Communications

## Slide 30: Transmitter Basics
If no data to send, keep sending 1 (stop bit) – idle line
When there is a data word to send
  Send a 0 (start bit) to indicate the start of a word
  Send each data bit in the word (use a shift register for the transmit buffer)
  Send a 1 (stop bit) to indicate the end of the word
Tbit
Data
bits
Data Sampling Time at Receiver
Time Zero
Tbit
Tbit
Tbit
Tbit
Tbit
Tbit
Tbit
Tbit
Tbit
Tbit

## Slide 31: Receiver Basics
Wait for a falling edge (beginning of a Start bit)
  Then wait ½ bit time
  Do the following for as many data bits in the word
          Wait 1 bit time
          Read the data bit and shift it into a receive buffer (shift register)
  Wait 1 bit time
  Read the bit
          if 1 (Stop bit), then OK
          if 0, there’s a problem!
Tbit*1.5
Data
bits
Data Sampling Time at Receiver
Tbit*2.5
Tbit*3.5
Tbit*4.5
Tbit*5.5
Tbit*6.5
Tbit*7.5
Tbit*8.5
Tbit*9.5
Tbit*10.5
Time Zero

## Slide 32: For this to work…
Transmitter and receiver must agree on several things (protocol)
  Order of data bits
  Number of data bits
  What a start bit is (1 or 0)
  What a stop bit is (1 or 0)
  How long a bit lasts
          Transmitter and receiver clocks must be reasonably close, since the only timing reference is the start of the start bit

## Slide 33: Input Data Oversampling
When receiving, UART oversamples incoming data line
  Extra samples allow voting, improving noise immunity
  Better synchronization to incoming data, improving noise immunity
Configurable oversampling from 8x to 32x
  Put desired oversampling factor minus one into SCB_CTRL, SCB_OVS bits.

## Slide 34: Baud Rate
Need to divide high frequency clock down to desired baud rate * oversampling factor
Example
  24MHz -> 4800 baud with 16x oversampling
  Division factor = 24E6/(4800*16) = 312.5. Must round to closest integer value ( 312 or 313), will have a slight frequency error.

## Slide 35: Using the UART
When can we transmit?
  Transmit peripheral must be ready for data
  Can poll the status register
  Or we can use an interrupt, in which case we will need to queue up data
When can we receive a byte?
  Receive peripheral must have data
  Can poll the status register
  Or we can use an interrupt, and again we will need to queue the data

## Slide 36: Software for Polled Serial Comm.
void test_polled() {
uart_init(9600);
uart_enable();
while(1) {
uart_tx(uart_rx()); // echoes the received character back
}
}

## Slide 37: Example Receiver: Display Data on LCD
line = col = 0;
while (1) {
c = uart_rx();
lcd_set_cursor(col, line);
lcd_put_char(c);
col++;
if (col > 7) {
col = 0;
line++;
if (line > 1) {
line = 0;
}
}
}

## Slide 38: Software for Interrupt-Driven Serial Comm.
Use interrupts
First, initialize peripheral to generate interrupts
Second, create single ISR with for the receive callback
Third, enable the peripheral

## Slide 39: Interrupt Handler
Queue rx_queue;
void uart_rx_isr(uint8_t rx) {
// Store the received character
queue_enqueue(&rx_queue, rx);
}
int main() {
queue_init(&rx_queue, 128);
uart_init(9600);
uart_set_rx_callback(uart_rx_isr);
uart_enable();
…
}

## Slide 40: USB to UART Interface
PCs haven’t had external asynchronous serial interfaces for a while, so how do we communicate with a UART?
USB to UART interface
  USB connection to PC
  Logic level (0-3.3V) to microcontroller’s UART (not RS232 voltage levels)
USB01A USB to serial adapter
  http://www.pololu.com/catalog/product/391
  Can also supply 5V, 3.3V from USB
PC
USB to UART bridge
MCU
D+ / D-
TX
RX
RX
TX
USB
UART

## Slide 41: Building on Asynchronous Comm.
Problem #1
  Logic-level signals (0 to 1.65V, 1.65V to 3.3V) are sensitive to noise and signal degradation
Problem #2
  Point-to-point topology does not support a large number of nodes well
          Need a dedicated wire to send information from one device to another
          Need a UART channel for each device the MCU needs to talk to
          Single transmitter, single receiver per data wire

## Slide 42: Solution to Noise: Higher Voltages
Use higher voltages to improve noise margin: +3 V to +15 V, -3 V to -15 V
Example IC (Maxim MAX3232) uses charge pumps to generate higher voltages from 3.3V supply rail

## Slide 43: Solution to Noise: Differential Signaling
Use differential signaling
  Send two signals: Buffered data (A), buffered complement of data (B)
  Receiver compares the two signals to determine if data is a one (A > B) or a zero (B > A)
Data into transmitter
Data out of transmitter, on bus
Data out of receiver

## Slide 44: Solutions to Poor Scaling
Approaches
  Allow one transmitter to drive multiple receivers (multi-drop)
  Connect all transmitters and all receivers to same data line (multi-point network). Need to add a medium access control technique so all nodes can share the wire
Example Protocols
  RS-232: higher voltages, point-to-point
  RS-422: higher voltages, differential data transmission, multi-drop
  RS-485: higher voltages, multi-point

## Slide 45: SPI Communications

## Slide 46: Hardware Architecture
All chips share bus signals
  Clock SCK
  Data lines MOSI (master out, slave in) and MISO (master in, slave out)
Each peripheral has its own chip select line (CS)
  Master (MCU) asserts the CS line of only the peripheral it’s communicating with

## Slide 47: Serial Data Transmission
Use shift registers and a clock signal to convert between serial and parallel formats
Synchronous: an explicit clock signal is along with the data signal
Transmitting Device
Receiving Device

## Slide 48: SPI Example: Secure Digital Card Access
SD cards have two communication modes
  Native 4-bit
  Legacy SPI 1-bit
VDD from 2.7 V to 3.6 V
CS: Chip Select (active-LOW)
Host sends a six-byte command packet to card
  Index, argument, CRC
Host reads bytes from card until card signals it is ready
  Card returns
          0xff while busy
          0x00 when ready without errors
          0x01-0x7f when error has occurred
DAT2 /
X
DAT3 /
CS
CMD /
DI
GND
VDD
CLK /
SCLK
DAT0/
DO
DAT1/
X
GND

## Slide 49: I2C Communications

## Slide 50: I2C Bus Overview
“Inter-Integrated Circuit” bus
Multiple devices connected by a shared serial bus
Bus is typically controlled by master device, subordinates respond when addressed
I2C bus has two signal lines
  SCL: Serial clock
  SDA: Serial data
Full details available in “The I2C-bus Specification”
Author: Colin M.L. Burnett, Source: Wikimedia

## Slide 51: I2C Bus Connections
Resistors pull up lines to VDD
Open-drain transistors pull lines down to ground
Master generates SCL clock signal
  Can range up to 400 kHz, 1MHz, or more
Author: Colin M.L. Burnett, Source: Wikimedia

## Slide 52: Master Writing Data to Subordinate
Start
Address
Write
ACK
Data
Repeated Start
ACK

## Slide 53: Master Reading Data from Subordinate
Start
Address
Read
ACK
Data
ACK
Data
NACK
Stop
SDA
SCL

## Slide 54: I2C Addressing
Each device (IC) has seven-bit address
  Different types of device have different default addresses
  Sometimes can select a secondary default address by tying a device pin to a different logic level
What if we treat the first byte of data as a register address?
  Can specify registers within a given device: 8 bits

## Slide 55: Enabling i2c
void temperature_init(void) {
i2c_init();
i2c_enable();
}
void temperature_enable(void) {
// Start conversion.
i2c_start();
i2c_tx(subordinate_ADDRESS | WRITE);
i2c_tx(START_CONVERT_T);
i2c_stop();
}

## Slide 56: Reading 12 bits from a temperature sensor
float temperature_read(void) {
short temp;
i2c_start();
i2c_tx(subordinate_ADDRESS | WRITE);
i2c_tx(READ_TEMPERATURE);
i2c_start();
i2c_tx(subordinate_ADDRESS | READ);
temp = i2c_rx() << 8;
i2c_ack();
temp |= i2c_rx();
i2c_nack();
i2c_stop();
// Sign extend from 16-bit to 12-bit.
temp >>= 4;
// Convert from fixed-point to floating point.
return temp / (float)16;
}

## Slide 57: Protocol Comparison

## Slide 58: Factors to Consider
How fast can the data get through?
  Depends on raw bit rate, protocol overhead in packet
How many hardware signals do we need?
  May need clock line, chip select lines, etc.
How do we connect multiple devices (topology)?
  Dedicated link and hardware per device - point-to-point
  One bus for manager transmit/subordinate receive, one bus for subordinate transmit/manager receive
  All transmitters and receivers connected to same bus – multi-point
How do we address a target device?
  Discrete hardware signal (chip select line)
  Address embedded in packet, decoded internally by receiver
How do these factors change as we add more devices?

## Slide 59: Protocol Trade-Offs
Protocol | Speed | Signals Req. for Bidirectional Communication with N devices | Device Addressing | Topology
UART (Point to Point) | Fast – Tens of Mbit/s | 2*N (TxD, RxD) | None | Point-to-point full duplex
UART (Multi-drop) | Fast – Tens of Mbit/s | 2 (TxD, RxD) | Added by user in software | Multi-drop
SPI | Fast – Tens of Mbit/s | 3+N for SCLK, MOSI, MISO, and one SS per device | Hardware chip select signal per device | Multi-point full-duplex, multi-drop half-duplex buses
I2C | Moderate – 100kbit/s, 400 kbit/s, 1Mbit/s, 3.4Mbit/s. Packet overhead. | 2 (SCL, SDA) | In packet | Multi-point half-duplex bus