## Slide 1: Cortex-M4 Analog Peripherals Lecture 4
EN3544 Embedded System
By: Ghalib Janjua

## Slide 2: Contents
Analog to Digital Converter (ADC)
    Reference
Digital to Analog Converter (DAC)
    Reference
Comparator (COMP) - Optional
    Reference
Operational Amplifier (OPAMP) - Optional
    Reference
Q&A

## Slide 3: Analog to Digital Converter - ADC
Number of ADC = 3
  16-24 input through GPIO (Single or differential ended)
  Three WDG timer per ADC
12bit resolution, 16bit with oversampling
5.33 Msample/s (12bit) when fADC_CLK=80MHz
  210uA per 1Msample/s
Mode
  Single, Continuous, Scan, Discontinuous/injected
Data
  DMA request generation
  Interrupt request

## Slide 4: ADC – Advance feature
Interleave mode can support up to 10 MSamples/s
Auto calibration to reduce offset
Deep power down mode
  When not in use the internal power supply is disconnected
Auto-delayed Conversion
  Make ADC to wait until last data is read before starting new conversion
Sampling time in Cycles
  2.5, 6.5, 12.5, 24.5, 47.5, 92.5, 247.5, 640.5
Clock sources – HCLK or independent clock

## Slide 5: ADC - Interrupts

## Slide 6: ADC - Power Modes

## Slide 7: Digital to Analog Converter - DAC
2 DAC module
  Can be Buffered output
  Synchronised output
8bit or 12bit resolution
  Right & left aligned
DMA – Interrupt event: Underrun and request
Tigger
  Timer OR External I/O OR Software
Sample & Hold mode
  Duty cycle
Noise generator and Triangular wave generator

## Slide 8: DAC

## Slide 9: Comparator - COMP
Ultra low power comparator
Two comparator with binary output
  Independent and Combine for window operation
Continuously monitor voltage (Speed vs Power consumption)
  Can be connected to I/Os using alternate function
  Can be redirected to various internal peripherals
Wakeup from sleep, stop and low power sleep
  Can generate timer break signal
Can generate EXTI interrupt

## Slide 10: COMP

## Slide 11: Operational Amplifier - OPAMP
Rail to rail output OPAMP with low offset voltage
  Inverting
  Non-inverting
  Low/High pass filter
Operation mode
  Normal mode (120uA)
  Lower mode (45uA)
On chip mode
  Standalone mode
  Programable gain amplifier
  Voltage follower

## Slide 12: OPAMP

## Slide 13: Q&A