## Slide 1: Cortex-M4 Timers and PWM Lecture 6
EN3544 Embedded System

## Slide 2: Contents
General Purpose Timers (GPTIM)
    Reference
    Application note
PWM
Q&A
Notes: Handle timing related events, generate waveform and measure timing characteristic of input signal.

## Slide 3: Timer
A timer (sometimes referred to as a counter) is a special piece of hardware inside many microcontrollers.
Their function is simple: they count (up or down, depending on the configuration--we'll assume up for now).
For example, an 8-bit timer will count from 0 to 255. Most timers will “roll over” once they reach their max value.

## Slide 4: Common hardware functions with timers
Output compare (OC): toggle a pin when a timer reaches a certain value
Input capture (IC): measure the number of counts of a timer between events on a pin
Pulse width modulation (PWM): toggle a pin when a timer reaches a certain value and on rollover. By adjusting the on versus off time (duty cycle), you can effectively control the amount of electrical power going to another device.

## Slide 5: Timer feature
Time critical operation and unloading CPU
Software tasks
  Time base, timeout and trigger
Hardware tasks
  Waveform, measure signal timing and react to event
Interconnection of timer
  Monitoring/trigger
Merging of timers
Application
  Motor control and Digital power conversion

## Slide 6: Contd…
Architecture
  Number of inputs/outputs (1 to 9)
  Resolution 16 or 32 bit
  PWM, DMA, synchronization, up/down courting
Independent configuration
  Capture
  PWM
Default clock derived from APB domain and/or external clocks
Auto-reload and 16-bit pre-scaler
Update event
  Interrupt or DMA

## Slide 7: Prescaler
How fast do timers run? Well, that depends on how fast you tell them to run.
All timers require a clock of some sort.
Most will be connected to the microcontroller’s main CPU clock (others, like real time clocks, have their own clock sources).
A timer will tick (increment by one) each time it receives a clock pulse.

## Slide 8: Prescalar (Example)
For a default main clock (HCLK) of 80 MHz, We could have a timer tick at 80 MHz, but that might be too fast for many of our applications.
A 16-bit timer can count to 65,535 before rolling over, which means we can measure events no longer than about 819 microseconds! (1/80M x 65535 = 819 us)
If we wish to measure longer events, we need to use a prescaler, which is a piece of hardware that divides the clock source.

## Slide 9: Prescalar (Example)
A prescaler of 80 would turn an 80 MHz clock into a 1 MHz clock.
Timer would tick once every 1 microsecond(1/1M = 1us)
A 16-bit timer, be able to time events up to a maximum of about 65.5 milliseconds (65535/1M = 65.5 ms )

## Slide 11: Pulse Width Modulation (PWM
PWM is a method to reduce the average power delivered by signal
PWM in an idealized inductor driven by a ■ voltage source modulated as a series of pulses, resulting in a ■ sine-like current in the inductor.

## Slide 12: Pulse Width Modulation (PWM)
Parameters
  Frequency
  Duty cycle
Application
  Servo motor control
  Telecommunication
  Voltage regulation
Figure : PWM

## Slide 13: Counting period: PWM

## Slide 14: Low Power Modes

## Slide 15: Q&A