## Slide 1: Performance Evaluation and OS-Aware Debugging
Operating System Lab-in-a-Box
Notes: In this module we learn about performance evaluation and debugging a program created to run on the microcontroller with an operating system.

## Slide 2: Previous
Sharing Data in RTX
Lab
Notes: In the last module we learnt about sharing data in RTX.

## Slide 3: After you code…
Now you have built your MCU programs based on RTOS, what next?
Assume it is functionally sound (no functional bugs)
  Optimize your program
  Based on its performance
  Tweak your program/configuration of the OS until optimal or you are satisfied
Debugging terminology
  Functional debugging
  Performance debugging
  Modular debugging
  Tracing
  Profiling
  Terms are sometimes used interchangeably and mostly overlapping
Intrusiveness – notice that almost all debugging techniques will affect performance
Watchdog – commonly used recovery mechanism in embedded systems
Notes: After we write the program to run with RTOS, we need to make sure that the program is functionally correct, optimized, and has good performance. We need to tweak the operating system parameters to get optimal performance for our program. The program needs to be tested and debugged for functional correctness. Every program maps the inputs to outputs, just like a function. We need to debug so that the output matches the input as desired in our requirement.
We can debug in a number of ways:
debug the program for performance (speed of execution, accuracy, correctness, safe etc).
divide the program into modules and debug every module.
tracing and profiling can be used to debug a program.
All debugging techniques insert some code or steps in the original program and this may affect the performance of the program.
Watchdog monitors the program and makes sure that there is a recovery mechanism. For example, a watchdog timer can monitor the memory and if the memory does not respond within a certain time, instead of making the processor going into an infinite wait, retry the memory operation or enter a recovery routine.

## Slide 4: Functional Debugging
Focus on the functional property of your program
Does the result match your expectation?
Stepping through your program
Tracing
Breakpoints
Print statements
LED heartbeat debugging
Beware of some of the concurrency bugs – hard to identify and recover from:
  Deadlock
  Livelock
  Not releasing mutexes
Notes: Functional debugging involves checking the outputs for various expected inputs. To test we can do the following:
Stepping through your program - Execute one instruction at a time and looking at the variable and register values.
Tracing - Tracing the program behaviour for a few instructions at a time
Breakpoints - Inserting break points at any place in the program and looking at the behaviour.
Print statements - Inserting print statements in different places in the program to print the values of variable or status.
LED heartbeat debugging– Insert at different places in the program LED blinking statement so that we can know that the program executed up to that point.

## Slide 5: Performance Evaluation
Or performance debugging
What are the performance metrics for your application?
  Throughput: number of tasks completed in a time unit
  Latency/response time: delay between request and the response to the request
  Turnaround time: delay between request and completion of the request
  CPU utilization
  Variation: does your program fluctuate a lot?
  Deadline
  Priority
  Memory: may not be obvious for this course as the board has plenty of ROM/RAM space and RTX is relatively lightweight
  Power: OS will induce power consumption overhead
Really varies and affected by architecture, compilers, boards and applications.
Trade-off: good design demands good compromises
Tune your OS configuration

## Slide 6: Performance Evaluation
We will mainly focus on the timing behaviour of our system
Worst case execution time (WCET) analysis
Simulation
  Difficult but sometimes necessary
Static timing analysis
  Examine the source code
  State space exploration and modelling
Measure directly
  Experimental and accurate
  Can be time consuming
*Wilhelm, Reinhard, et al. "The worst-case execution-time problem—overview of methods and survey of tools." ACM Transactions on Embedded Computing Systems (2008).
Notes: Here we will consider timing analysis.
Worst case execution analysis refers to the maximum time taken by a program to execute under different conditions. For example, a program may execute a longer subroutine when the input value is the highest allowed.
This can be analyzed via simulation of the program or by examining the source code or state space exploration and modeling.
Another way is to measure the WCET by experiment – running the program through the longest execution routine path. This may require running the program with various input or intermediate values to check for the longest execution time.

## Slide 7: Prediction of Execution Time
What aspects of execution time do we care about?
  Average – what’s the typical performance?
  Worst-case – must meet deadlines
  Best-case – too fast might cause race conditions or other problems
  Distribution and variability
"Prediction is extremely difficult. Especially about the future.” – Niels Bohr
Prediction Techniques
  Manual estimate based on databook – shortcomings are obvious
  Use a processor simulator
  Measure a real system
Notes: Prediction of execution time is difficult and we may be interested depending on the application about:
  Average – what’s the typical performance?
  Worst-case – must meet deadlines
  Best-case – too fast might cause race conditions or other problems
  Distribution and variability
Prediction techniques are:
Manual – counting the code/instruction cycle and computing the timing
Simulation– using a processor simulator on a PC and running the code on the simulated processor. It is not accurate, but gives an approximate value
Best thing is to run the program on the real board with RTOS. This is time consuming, but accurate.

## Slide 8: Finding the WCET
Need WCET for all tasks and ISRs to perform scheduling analysis
Sources of execution time variations
  Software
    Different input data may trigger different control flow behaviour
  Hardware
    Some instruction execution times may depend on input data
    Pipelines may stall
    Caches may miss
    Branch target buffers may miss
    DMA activity may slow or delay task execution
Notes: We need to compute WCET for all the tasks. For example a typical real time controller may be executing 20 tasks. Each one of them may have different WCET. This computing needs the scheduling analysis of the tasks and the ISR routine running time.
Sources of execution time variations:
  Software-- Different input data may trigger different control flow behaviour.
  Hardware--
    Some instruction execution times may depend on input data
    Pipelines may stall
    Caches may miss
    Branch target buffers may miss
    DMA activity may slow or delay task execution
and combination of the above factors.

## Slide 9: Examining Object Code
C and other high-level languages hide implementation details and allow programming at a higher level
This abstraction means that it isn’t always obvious what assembly code will be generated for a C statement, and (for example) how long it will take to execute
  a = b*c[i+j] depends on:
    data types of a, b, c, i, j: int? float? double? long?
    Instruction Set Architecture (ISA) and MCU implementation
          Multiply instruction for the data type
          Advanced addressing modes suitable for array indexing
Examining the object code generated by the compiler is the only way to get an accurate picture of what will happen
  It gets ugly very quickly (“does not scale well”).
We need representations which reflect the program’s structure in order to simplify the analysis
Also, compilers and other tools use these representations to analyze and optimize the code automatically
Notes: Programs written in C or C++ etc. hide the lower level details and timing analysis is difficult at this level.
Some compilers and other tools found in the development platform allow timing analysis. Example: Code Composer Studio is a development platform from Texas Instruments for DSP processors. This allows timing analysis at C level.
Examining the assembly code generated by the compiler will give a good timing analysis. Some compilers have optimizing capability, i.e. you can choose optimized compiling to generate optimized assembly code.

## Slide 10: Control Flow Graphs and Call Graphs
Control flow graph (CFG)
  A flow chart which shows the execution sequence of the program
  Each node is a basic block (sequence of instructions, potentially with conditional jump at end)
  Create one CFG per subroutine or interrupt service routine
Call graph
  A hierarchical (tree) form which shows the nesting of subroutine calls
  Each node is a subroutine
    Going down an arrow indicates calling a subroutine
    Going up an arrow (backwards) indicates returning from that subroutine
  Create one call graph per program
_timer_isr
L0
L1
_timer_isr_0
main
Init_MCU
Read_ Switches
Process
Refresh_ Display
Linearize
Resample
Notes: Control Flow Graphs and Call Graphs as shown in the slide show the flow of the program. We need to create these graphs to analyze the timing.

## Slide 11: CFG Formation Rules
A CFG consists of basic blocks (BB) joined by edges
Basic block: a sequence of consecutive instructions such that each instruction is executed exactly once if the basic block is executed.
This implies
  the flow of control begins at the entry and leaves at the exit
  there is no conditional branching except potentially at the end.
    no instructions can be skipped within a basic block
  conditional branch (+skip) instruction effectively ends the basic block
  a jump/branch into a BB will split it into two
  a subroutine call ends the basic block
Relationships with other BBs
  Predecessors: all basic blocks which can execute immediately before the given basic block
  Successors: all basic blocks which can execute immediately after the given basic block.
For our purposes, a new label starts a new basic block (except in the case of consecutive labels, in which case the basic block is assigned the first label)
Notes: A CFG consists of basic blocks (BB) and its edges. In BB, each instruction is executed only once. If there is a jump/branch, the BB will be split into two. A subroutine call ends the basic block.
There can be relations with other BBs such as: Predecessors and Successors.

## Slide 12: Call Graph Details
Each subroutine is represented by a node
Each potential call from subroutine A to B is represented by a directed edge from A to B
Each ISR has a node, but it is not called by any other code (except if software interrupts are supported)
Operations not supported by ISA (e.g. modulo (%)) may be implemented with subroutine linked in from a C library, leading to a deeper call graph than expected
Notes: Each subroutine is represented by a node. A subroutine call from A to B is represented by an edge.
Each ISR is a node.

## Slide 13: Static Timing Analysis Procedure
Compile source code
Examine assembly code
Form basic blocks
Form control flow graph from basic blocks
Determine duration per basic block by adding instruction durations
Evaluate paths through function
  Best and worst-case times for function
  Deal with control-flow complexity
    For code in conditional region (if-then-else),
      If control-flow path is known, calculate exact time for path
      If control-flow path is unknown, bound the time: choose the larger time for WCET, the smaller for BCET
    For code in loop, use the exact number of iterations (if known) or else try to derive a bound (minimum and maximum)
Notes: Static timing analysis procedure involves:
Examining the source code, assembly code
Forming BB and CFG graph with basic BB
Computing the timing for each BB by adding the instruction cycle time.
Evaluate the various paths of execution to compute:
  Best and worst-case times for function
  Deal with control-flow complexity
  For code in conditional region (if-then-else),
      If control-flow path is known, calculate exact time for path
      If control-flow path is unknown, bound the time: choose the larger time for WCET, the smaller for BCET
    For code in loop, use the exact number of iterations (if known) or else try to derive a bound (minimum and maximum)

## Slide 14: How Long Does An Instruction Take?
As a guideline for Cortex-M cores:
Most instructions
  1 cycle
Loads and stores
  Usually 2 cycles: to AHB interface or SCS
  1+N cycles: load multiple, store multiple, push, pop (N registers)
Any instruction writing to PC
  2 Cycles
Conditional branch
  Not taken: 1 cycle
  Taken: 2 cycles
Other branches
  Unconditional, exchange, link & exchange: 2 cycles
  Link: 3 cycles
See the Technical Reference Manual of your core for more details
Notes: The technical reference manual gives the instruction cycle time for the Cortex- M, most instructions take 1 cycle.

## Slide 15: Measure a Real System
If simple enough, can count instruction cycles. But not scalable as nowadays program flow and program inputs can easily spin out of control.
In most cases, directly measure the timing behaviours of your system is more intuitive and direct
Use external analysis tools
  Logic analyzer looks for start and end addresses of routine in question
  Oscilloscope looks for special events (e.g. on debug pins)
    Set up GPIO port to set output bit upon entering routine, clear it upon exiting
Use a high-resolution timer in the circuit
  Configure as cycle counter
    Most MCUs have counter peripherals
    Can select prescaled clock source if needed to increase time range
    Make it increment a counter variable when it overflows
Notes:   The Cortex-M series provides an internal timer SysTick, many experienced programmers will use this to measure the timing behaviour of the system. This is however incorrect if your programs are based on RTX as SysTick is used as the OS timer. Instead, use U32 os_time_get (void);!
  For simple programs, counting the instruction cycles will be enough to compute total execution time.
  One can use external analysis tools like logic analyzer, oscilloscope, using GPIO pin to trigger output at the start and end.
  One can also use high resolution timer in the processor, except when the RTOS is using the counter/timer.

## Slide 16: Example – Measuring Execution Time
void clear_ticks(void) {
ta0s = 0; // stop counting
overflow_count = 0;
ta0 = 0xffff;
ta0s = 1; // restart counting
}
void main (void) {
unsigned long t;
mcu_init();
init();
clear_ticks();
// do processing to be timed
t = get_ticks();
while (1);
}
Notes: An example program for measuring execution time is shown here.

## Slide 17: Timing Data Analysis
Statistics are informative
  Minimum, maximum
  Mean: sum total time and divide by number of measurements
#define MIN(a,b) (((a)<(b))? (a):(b))
#define MAX(a,b) (((a)>(b))? (a):(b))
#define NUM_TESTS (300)
unsigned long t=0, min, max;
float sum=0.0;
min = 0xffffffffl;
max = 0;
for (i=0; i<NUM_TESTS; i++) {
Clear_Ticks();
f = tan(i/100.0);
t = Get_Ticks();
min = MIN(t, min);
max = MAX(t, max);
sum += t;
}
Notes: The timing data can be analyzed for minimum, maximum and mean values.

## Slide 18: Repeatability
Does the same input lead to the same output, or are other factors in the system affecting the computation?
min = 0xffffffffl;
max = 0;
for (i=0; i<3000; i++) {
Clear_Ticks();
f = sqrt(37/100.0);
t = Get_Ticks();
min = MIN(t, min);
max = MAX(t, max);
}
Notes: One can also check the running time for various inputs.

## Slide 19: Histogram Showing Distribution of Execution Times
Horizontal axis: range of values of measured variable (bins)
Vertical axis: number of times (frequency) variable had that value
Measured Value
Count
#define HIST_SIZE 10
int hist[HIST_SIZE];
for (i=0; i<HIST_SIZE; i++)
hist[i] = 0;
for (i=0; i<300; i++) {
Clear_Ticks();
f = sqrt(i/100.0);
t = Get_Ticks();
min = MIN(t, min);
max = MAX(t, max);
n = (unsigned) (t/250);
hist[min(n, HIST_SIZE-1)]++;
}
Notes: A histogram can be drawn for execution time distribution.

## Slide 20: Evaluating Responsiveness
Three important types of critical path
  From interrupt request to ISR running
  From interrupt request to user task (signalled by ISR) running
  From one user task to another user task (signalled by first task)
First two most critical for RT embedded systems
How to measure?
  Use embedded instruction trace capability – many Cortex M MCUs have ETM or MTB
  Instrument program to send out trace information (e.g. debug signals) to view with oscilloscope or logic analyzer
Notes: There are 3 important types of critical paths:
  From interrupt request to ISR running
  From interrupt request to user task (signalled by ISR) running
  From one user task to another user task (signalled by first task)
  We can measure the critical path time by using the embedded instruction trace capability like, ETM or MTB of the Cortex M processor.

## Slide 21: OS Aware Debugging
Performance evaluation for OS can be slightly different:
  “Useful” tasks do not really terminate
  Either sleep for a while or wait for some events
Preemption and interrupts
How can you detect deadlock
You actually need to know more than just the timing
  Task states
  Priorities
  Visit times (profiler’s job)
  OS overhead
The lab session will introduce some OS aware debugging features of Arm MDK
Notes: Operating system aware debugging needs more information on the tasks. We can learn more from the lab.

## Slide 22: Optimizations
Minimize interrupt lock-out time
  Application
  OS
If response time is more important than CPU utilization, then adjust task priorities accordingly
Which part of the code uses the most time?
  Profiler – sampling
  That’s the best place to start optimization for speed
Notes: Optimization of interrupt context switching time, response time is necessary.
We need to set the priorities correctly for critical tasks.
We also need to optimize the longest executing part of the program.

## Slide 23: Next
Lab