## Slide 1: FIR Filters Moving Average Filters

## Slide 2: Moving Average Filter
Moving
average
filter
x(n)
y(n)
Input
Output
Five point moving average filter
Notes: The moving average filter is, arguably, the simplest discrete-time (digital) filter of all.
Here is a block diagram representation intended to emphasize that the filter is a (linear time invariant) system and that its input and output are discrete-time signals (or sequences) x(n) and y(n).
For the purposes of illustration, we will consider a five point moving average filter.
The nth value of the output signal y(n) is formed by taking the arithmetic mean, or average, of the five most recent values of the input signal x(n).
Here are two slightly different ways of expressing this. The second highlights that the nth value of the output signal is a weighted sum of previous values of the input signal.
Finally, here is a generic expression for an N-point moving average filter.

## Slide 3: Moving Average Filter
Input x(n) x
Output y(n) ●
Notes: So what does the moving average do to an input signal.
Here’s an example.
The graph shows the discrete values of hypothetical input signal (blue crosses). Without quantitatively analyzing this signal, we can observe that over time (as sample number increases), the value of the signal steadily and slowly decreases. This represents a low frequency component in the signal.
From one sample to the next, the value of the input signal jumps up and down. This represents a high-frequency component in the signal.
Now let’s apply a five point moving average filter to this signal.
First of all, using the expression on the previous slide, and the information provided here, we cannot “properly” compute values of the output signal y(n) until the sampling instant at which n=5. That value of the output signal will be equal to the arithmetic mean of the first five input signal sample values (the first five blue crosses) on the figure.

## Slide 4: Moving Average Filter
Input x(n) x
Output y(n) ●
Notes: The next value of the output signal y(6) will be equal to the arithmetic mean of input signal sample values x(2), x(3), x(4), x(5), and x(6) as shown in the next slide.

## Slide 5: Moving Average Filter
Input x(n) x
Output y(n) ●
Notes: and so on ...

## Slide 6: Moving Average Filter
Input x(n) x
Output y(n) ●
Notes: and so on ...

## Slide 7: Moving Average Filter
Input x(n) x
Output y(n) ●
Notes: Without analyzing it quantitatively, we can observe that as time progresses, the value of the output signal (red blobs) gradually decreases, corresponding to a low-frequency component in the output signal.
The value of the output signal from one sample to the next does not “jump about.” Compared to the input signal, the output signal is “smooth” and does not contain a high-frequency component.
In these terms, the moving average filter has acted as a low pass filter.

## Slide 8: Moving Average Filter
Moving average filter smooths input signal.
Filters out or blocks high-frequency signal components
Allows low-frequency signal components to pass
It is a low pass filter.
Notes: To summarize...

## Slide 9: Finite Impulse Response (FIR) Filter
N point moving average filter
Compare this with the conventional representation of an N point FIR filter.
h(i) are referred to as the coefficients of the filter
and as the impulse response of the FIR filter.
Notes: The moving average filter is one example of a finite impulse response filter. We’ve seen the first expression on this slide before. It describes an N-point moving average filter.
Conventionally, the coefficients, or weights, of a finite impulse response filter are given the symbol h.
Each output sample value in a finite impulse response filter is computed from a number of previous input values.
FIR filters are non-recursive.

## Slide 10: FIR Filter Coefficients
The coefficients, h(i), of an N point moving average
filter each have a value of 1/N .
Graphical representation of the coefficients of a 5 point
moving average filter, also known as its impulse response
Notes: Here, the coefficients of the five point moving average filter are plotted graphically.
The coefficients may also be referred to as the impulse response of the filter.
For i<0 and i>4, the impulse response is assumed to be zero.
Hence, the impulse response is a finite impulse response.

## Slide 11: FIR Filter Impulse Response
x(n) x(n-1) x(n-2) x(n-3) x(n-4)
h(0)x(n) h(1)x(n-1) h(2)x(n-2) h(3)x(n-3) h(4)x(n-4)
Notes: Here is a block diagram representation of the five point moving average filter.
Its component parts are a delay line in which input sample values are stored.
At each sampling instant, the contents of the delay line are shifted by one position and a new input sample value is added.
The coefficients of the filter appear as the gains of the blocks in the middle of the diagram. The output of a block labeled h(i) is equal to its input x(n-i) multiplied by h(i).
A summing junction combines the outputs of the coefficient blocks to form one output sample value, y(n) per sampling instant.

## Slide 12: FIR Filter Impulse Response
1 0 0 0 0
Notes: We have stated previously that the impulse response of an FIR filter is equal to its coefficients.
Let’s look at this in a block diagram form, by applying an impulse as an input. All values of x(n) are zero except for x(0).
We are assuming here that the values representing previous input samples, stored in the delay line, are initially all equal to zero.

## Slide 13: FIR Filter Impulse Response
1 0 0 0 0
h(0) 0 0 0 0
y(n) = h(0)
Notes: The filter output is a sum of products. However, since all but one value stored in the delay line is equal to zero, all but one of the product terms is equal to zero.
Initially, the output is equal to the first filter coefficient h(0).

## Slide 14: FIR Filter Impulse Response
0 1 0 0 0
0 h(1) 0 0 0
y(n) = h(1)
Notes: At each sampling instant, the contents of the delay line are shifted one position (to the right in this diagram).
Here, n is equal to 1 and the output of the filter is y(1) = h(1).

## Slide 15: FIR Filter Impulse Response
0 0 1 0 0
0 0 h(2) 0 0
y(n) = h(2)
Notes: And so on ...

## Slide 16: FIR Filter Impulse Response
0 0 0 1 0
0 0 0 h(3) 0
y(n) = h(3)

## Slide 17: FIR Filter Impulse Response
0 0 0 0 1
0 0 0 0 h(4)
y(n) = h(4)
Output sequence h(0) h(1) h(2) h(3) h(4)
Notes: The output of the FIR filter has been formed by convolving the input sequence x with the filter coefficients h.
Convolution is sometimes (correctly) described in terms of “sliding” one sequence across another, forming sums (or integrals) of products along the way.
In the context of this block diagram, the input sequence x has slid across the delay line from left to right while the filter coefficients h have remained stationary with respect to the delay line.

## Slide 18: FIR Filter Frequency Response
Frequency response is the (complex) gain of the filter at different
(individual) frequencies.
The FIR filter is described by
If input x(n) comprises samples of a continuous complex exponential
(1)
i.e.
Notes: We have seen qualitatively that the moving average filter is a low pass filter.
What are the quantitative characteristics of the filter in the frequency domain?

## Slide 19: Frequency Response of the Moving Average Filter
where
and we consider
or
Then, substituting for x(n-i) in (1)
(2)
(3)

## Slide 20: Frequency Response of the Moving Average Filter
Comparing equations (2) and (3), we see that if the input x[n]
represents a complex exponential with frequency ω, phase phi,
and amplitude A.
Then, the output
represents that input multiplied by a complex gain
that is a continuous, periodic function of ω.
That gain H(ω) represents the frequency response of the filter.
(2)
(3)
(4)

## Slide 21: FIR Filter Impulse Response
Expression for complex frequency response of the filter
Hence, the (continuous) frequency response of an FIR filter is found
by taking the DTFT of its coefficients.
is similar in form to the discrete time Fourier transform (DTFT)
(4)
Notes: Comparing the expression for the frequency response of the filter with that of the discrete time Fourier transform (DTFT), we can see that these are equivalent, given that for an FIR filter h(i) = 0 for i<0 and for i>(N-1)

## Slide 22: FIR Filter Frequency Response
In this case, the filter coefficients are given by
Take the DTFT of h(n)
Hence,
Example: The frequency response of the five point moving average filter
(5)
Notes: Balancing the exponents of the terms in the frequency response enables the sum of complex exponentials to be converted (using Euler’s formula) into a real-valued trigonometric expression. This makes it relatively simple to envisage, or to plot, the magnitude frequency response.
The complex exponential term corresponds to a linear phase response (in this case -2ω), although you need to remember that the real-valued trigonometric expression is equal to the magnitude of the frequency response only when it is positive. Where it is negative, an extra 180 degrees of phase shift is implied.

## Slide 23: Five Point Moving Average Filter
Notes: Here are the (continuous) magnitude and phase components of the frequency response plotted over one period (2 pi radians of normalized frequency).
The trigonometric, real-valued part of the frequency response expression is not equal to the magnitude frequency response since it is negative for values
of normalized frequency between -0.8 pi and -0.4 pi, and between 0.4 pi and 0.8 pi. Correcting for this introduces phase shifts of pi/2 (in those frequency
ranges) to the linear phase response of -2ω corresponding to the complex exponential term in equation (). (It’s more straightforward than it looks!)