## Slide 1: IIR Filters Impulse Invariant and Bilinear Transform Methods of Design

## Slide 2: Recursive Filters
Unlike non-recursive FIR filters, Infinite Impulse Response (IIR) filters use previous output samples as well as previous input samples in order to calculate their output.
FIR filter
FIR filter
FIR filter
IIR filter
IIR filter
IIR filter
Notes: The defining characteristic of an Infinite Impulse Response (IIR filter is that it uses both previous input and previous output samples in order to calculate its output. Here are block diagram, difference equation, and z-transfer function representations of a recursive IIR filter. In each, it is possible to identify the part that is equivalent to a non-recursive FIR filter. Setting the value of each, a coefficient to zero will reduce the IIR filter to a FIR filter. By convention, the a0 coefficient is made equal to 1.

## Slide 3: Impulse Response
FIR filter | IIR filter
stable | potentially unstable
impulse response equal to filter coefficients | impulse response computed recursively from filter coefficients
Notes: Whereas an FIR filter is unconditionally stable and its impulse response is readily discernible from its coefficients, the feedback inherent in an IIR filter introduces the possibility of instability, and its impulse response is computed recursively from its coefficients.

## Slide 4: Stable Impulse Response Example
Recursive calculation of impulse response
n | x(n) | x(n-1) | y(n) | y(n-1) | y(n-2)
0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0.5 | 0 | 0
2 | 0 | 0 | 0.35 | 0.5 | 0
3 | 0 | 0 | -0.155 | 0.35 | 0.5
4 | 0 | 0 | -0.3885 | -0.155 | 0.35
5 | 0 | 0 | -0.148 | -0.3885 | -0.155
6 | 0 | 0 | 0.207 | -0.148 | -0.3885
Notes: Here is an example of the calculation of the impulse response of an IIR from its difference equation. Columns are provided for the discrete sample values of the input x(n), for the discrete output y(n), and for each of the previous input and output values used in the difference equation.
The columns x(n) and x(n-1) may be populated straight away – the input sequence is an impulse. At sampling instant n = 0, it is assumed that the filter has zero initial conditions, represented by zeros in the y(n-1) and y(n-2) columns. The value of y(n-2) for n = 1 may be initialized also.
Calculation of the values in the y(n) column proceeds as follows. Use the values of x(n-1), y(n-1), and y(n-2) in the same row to evaluate the difference equation. Enter the result in the y(n) column. Fill in the values of y(n-1) and y(n-2) in the next row of the table by propagating down and to the right, and repeat.
The filter in this example has a decaying, oscillatory impulse response that (if rounding errors are discounted) will continue as n tends to infinity. In contrast to the impulse response of an FIR filter, the length of the impulse response is not equal to the number of filter coefficients used in its calculation.

## Slide 5: Stable Impulse Response Example
Exponentially decaying impulse response
Notes: The response of this filter to a unit impulse is an exponentially decaying oscillation. Theoretically, it will never decay to zero. It will continue as n tends to infinity.

## Slide 6: Finite Impulse Response Example
Recursive calculation of impulse response
n | x(n) | x(n-1) | x(n-2) | y(n) | y(n-1)
0 | 1 | 0 | 0 | 0.5 | 0
1 | 0 | 1 | 0 | 0.5 | 0.5
2 | 0 | 0 | 1 | 0 | 0.5
3 | 0 | 0 | 0 | 0 | 0
4 | 0 | 0 | 0 | 0 | 0
5 | 0 | 0 | 0 | 0 | 0
6 | 0 | 0 | 0 | 0 | 0
Notes: However, the response of an IIR need not extend to infinite n. This example demonstrates how (in theory at least) the impulse response of a recursive IIR filter may be finite. Here, a two-point moving average filter has been implemented. In order for this example to work in practice, rounding error would have to be zero.

## Slide 7: Finite Impulse Response Example
Finite impulse response computed recursively
Notes: Graphical representation of filter impulse response.

## Slide 8: Unstable Impulse Response Example
Recursive calculation of impulse response
n | x(n) | x(n-1) | y(n) | y(n-1) | y(n-2)
0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0.5 | 0 | 0
2 | 0 | 0 | 0.25 | 0.5 | 0
3 | 0 | 0 | -0.875 | 0.25 | 0.5
4 | 0 | 0 | -0.9375 | -0.875 | 0.25
5 | 0 | 0 | 1.2813 | -0.9375 | -0.875
6 | 0 | 0 | 2.5156 | 1.2813 | -0.9375
7 | 0 | 0 | -1.3 | 2.5156 | 1.2813
Notes: Here is an example of an unstable IIR filter. Its impulse response is oscillatory and increases in amplitude exponentially. These few computed output samples don’t prove instability. For the moment, just accept that these are the initial sample values in an unstable impulse response.

## Slide 9: Unstable Impulse Response Example
Unstable impulse response computed recursively
Notes: Graphical representation of filter impulse response.

## Slide 10: Design of IIR Filters
Traditionally, IIR filters are based on analogue filter designs described by continuous-time s-transfer functions H(s).
A vast amount of knowledge about analogue filter design exists.
Once an analogue filter prototype has been chosen, the design of an IIR filter comprises transforming to the discrete-time or z-domain.
More recently, iterative computer-based techniques for finding the coefficients of an IIR filter that will satisfy a particular specification have taken over.
Notes: Despite the existence of computer-based design packages, consideration of the more traditional methods of design can give valuable insight into the characteristics of IIRs.
Many computer-based design packages automate the “traditional” design methods, offering the user a choice of analogue filter designs, e.g., Butterworth, Chebyshev, Bessel, etc.

## Slide 11: Impulse Invariance Method
Based on mapping of s-plane poles into the z-plane.
Partial fraction expansion of H(s) separates it into terms corresponding to poles.
Replace each denominator term in H(s) with a term in H(z).
Alternatively, use Laplace and z-transform tables.
Discrete impulse response of resulting IIR filter comprises samples of the continuous impulse response of the analogue prototype (scaled by Ts).
Frequency response of IIR filter may not match that of analogue prototype.
Notes: Conceptually, the impulse invariance method is based on transforming each pole of the s-transfer function of the analogue prototype into a corresponding z-transfer function pole. This may involve a significant amount of algebraic manipulation.
An alternative is to make use of tables of Laplace and z-transform pairs.
The term impulse invariance refers to the characteristic that the discrete impulse response of the IIR filter is equal to (scaled) samples of the continuous impulse response of the prototype analogue filter.
However, it does not follow that the frequency response of the IIR filter is identical to that of the prototype analogue filter.

## Slide 12: Aliasing in the Impulse Invariant Design Method
Continuous
impulse response
h(t)
Discrete
impulse response
h(n)
Time-domain
Frequency-domain
-fs
fs
Multiply Convolve
Notes: Consider that the frequency domain representation (found by taking the Fourier transform) of the continuous impulse response of a prototype filter is not necessarily band limited. Then, consider that the discrete impulse response of the impulse invariant IIR filter (which is equal to samples of h(t)) might in theory be found by sampling h(t), i.e., by multiplying h(t) by an infinite sequence of impulses. The corresponding operation in the frequency domain, to yield the frequency response of the IIR filter, is convolution of the prototype filter’s frequency response with an infinite sequence of impulses. If copies of the prototype filter’s frequency response, spaced fs apart, overlap, then the frequency response of the IIR filter will not equal to that of the prototype filter.
In general, for a low pass filter, the roll-off of gain with frequency will not be as steep for the IIR filter as for the analogue prototype.

## Slide 13: Impulse Invariance Method
Simple concept
Lots of algebra
Aliasing problems
Notes: Summary of the characteristics of the impulse invariance method of transforming an analogue filter into an IIR filter.

## Slide 14: Bilinear Transform Method
Substitute for s in H(s)
Effectively, the s-plane is mapped into the z-plane such that the imaginary axis in the s-plane is mapped onto the unit circle in the z-plane and the left hand half of the s-plane is mapped inside the unit circle in the z-plane.
Notes: An alternative is to use the bilinear transform. This involves a relatively straightforward algebraic substitution for s in H(s).

## Slide 15: Bilinear Transform Method
0
0.5
1
1.5
2
0.0
0.1
0.2
0.3
0.4
0.5
Normalized analog frequency (wa/ws)
Normalized digital frequency (wd/ws)
Notes: One important result of this is that effectively the frequency response of the analogue prototype filter across the range zero to infinite frequency is compressed into the effective frequency range of the digital IIR filter, i.e., zero to half the sampling frequency, according to a nonlinear (tangent) function.

## Slide 16: Bilinear Transform Method
Notes: In the example illustrated here, notice that the cutoff (-3 dB) frequency of the analogue prototype filter is moved in the digital implementation.

## Slide 17: Bilinear Transform Method
Simple algebra
No aliasing problems
Warped frequency response
Notes: Summary of the characteristics of the bilinear transform method.