## Slide 1: Fast Fourier Transform (FFT) Review of Fourier Analysis
Notes: The fast Fourier transform (FFT) is one of the most important and widely used algorithms in digital signal processing.

## Slide 2: Fourier Analysis
Fourier analysis describes transformation of signal representation between time and frequency domains.
Different forms of Fourier analysis are applicable to different classes of signal.
Signals may be classified according to whether they are continuous or discrete and according whether they are periodic or aperiodic.
Notes: Fourier analysis is concerned with the transformation of signals between time and frequency domain representations. The term Fourier analysis refers to this in general. According to the nature of the signals involved, whether they are continuous or discrete and whether they are periodic or aperiodic, the specific form of Fourier analysis applicable is different.

## Slide 3: Fourier Analysis
Time domain Frequency domain
Fourier analysis provides
the link between time
and frequency domain
representations of a signal
We classify signals according to whether they are continuous or discrete (sampled) and periodic (finite) or aperiodic.
continuous, aperiodic
continuous, periodic
discrete, aperiodic
discrete, periodic
Discrete signals in one domain correspond to periodic signals in the other.
Continuous signals in one domain correspond to aperiodic signals in the other.
continuous, aperiodic
discrete, aperiodic
continuous, periodic
discrete, periodic
Fourier series (FS)
Notes: It is instructive to consider the four different classifications of signal (according to discrete/continuous and periodic/aperiodic) and the corresponding forms of Fourier analysis.
Armed with a couple of rules about the properties of signal representations in either domain, you can complete this table.
There is a different form of Fourier analysis applicable to each of the four pairs of signal type listed here.
Fourier series is perhaps the most intuitive and easily understood form of Fourier analysis. Continuous periodic waveforms may be synthesized from weighted sums of harmonically related sinusoids. It’s not difficult to see that only sinusoids at frequencies that are integer multiples of the fundamental frequency of the synthesized periodic waveform may be used. This corresponds to the frequency domain representation of a periodic, continuous-time waveform being discrete in nature. There is no reason for the (discrete) frequency domain representation to be periodic.

## Slide 4: Fourier Series (FS)
Synthesis:
Analysis
In the time domain, x(t) is complex, continuous, and periodic.
In the frequency domain, X(k) is complex, discrete, and aperiodic k runs from -∞ to + ∞.
A periodic continuous-time waveform is formed from the weighted sum of a potentially infinite numbers of complex exponentials at integer multiples of its fundamental frequency.
Fundamental period T seconds
Fundamental frequency 1/T hertz
Analyze one cycle of x(t) over period T
Synthesize using an infinite number of weights X(k)
Notes: The expressions describing the Fourier series comprise an infinite weighted summation of individual frequency components (complex exponentials) (synthesis) and an integral evaluated over one period of the continuous-time waveform. This integral effectively correlates different individual frequency components (complex exponentials) with the continuous-time waveform x(t). If correlation represents determining the degree of similarity between two signals, it is possible to consider each correlation result, X(k) as representing how much of that component should appear in the synthesis.

## Slide 5: Fourier Analysis
Time domain Frequency domain
continuous, aperiodic
continuous, periodic
discrete, aperiodic
discrete, periodic
continuous, aperiodic
discrete, aperiodic
continuous, periodic
discrete, periodic
Fourier series (FS)
Fourier transform (FT)
Notes: The Fourier transform is the most generally applicable form of Fourier analysis.

## Slide 6: Fourier Transform (FT)
Synthesis:
Analysis:
Both x(t) and X(ω) are complex, continuous, and aperiodic t and ω are evaluated from -∞ to + ∞.
Notes: Both synthesis and analysis are implemented by integration with limits +/- infinity.

## Slide 7: Fourier Analysis
Time domain Frequency domain
continuous, aperiodic
continuous, periodic
discrete, aperiodic
discrete, periodic
continuous, aperiodic
discrete, aperiodic
continuous, periodic
discrete, periodic
Fourier series (FS)
Fourier transform (FT)
discrete time Fourier transform (DTFT)
Notes: The discrete time Fourier transform is applicable to aperiodic discrete-time signals. One way of gaining insight into this form of Fourier analysis is to consider the relationship between the coefficients of a finite impulse response filter (its impulse response) and its frequency response. As considered in module 3, that frequency response is continuous (a digital filter has a gain at any frequency, not just at a discrete set of frequencies) and is periodic (sampling theory)

## Slide 8: Discrete Time Fourier Transform (DTFT)
Synthesis:
Analysis:
x(n) is complex, discrete, and aperiodic. Analyze x(n) for n from -∞ to + ∞
X(ω) is complex, continuous, and periodic. Synthesize using one cycle of ω over period 2π
Notes: Analysis, i.e., determining frequency response from a set of discrete time domain values, is possible (it’s a finite summation) in the case of a FIR filter. In general, x(n) might be infinite, and in that case, computation of a value X(w) is impractical.

## Slide 9: Fourier Analysis
Time domain Frequency domain
continuous, aperiodic
continuous, periodic
discrete, aperiodic
discrete, periodic
continuous, aperiodic
discrete, aperiodic
continuous, periodic
discrete, periodic
Fourier series (FS)
Fourier transform (FT)
discrete time Fourier transform (DTFT)
discrete Fourier transform (DFT)
Notes: The discrete Fourier transform (DFT) is a form of Fourier analysis used into digital signal processing. In practice, time-domain and frequency-domain representations of signals in a digital computer are necessarily discrete and finite. Think about it.
There is a correspondence between such signal representations being finite and periodicity. Periodic signals are characterized completely by just one cycle, and if a signal is periodic and discrete, then it is characterized completely by a finite set of samples. This correspondence between finite signal representations and periodicity can be a bit philosophical.

## Slide 10: Discrete Fourier Transform (DFT)
Synthesis:
Analysis:
x(n) is complex, discrete, and periodic. Analyze one cycle of x(n) comprising N values 0≤n<N
X(k) is complex, discrete, and periodic. Synthesize x(n) from one cycle of X(k) comprising N values 0≤k<N
Notes: Analysis, i.e., determining frequency response from a set of discrete time domain values, is possible (it’s a finite summation) in the case of a FIR filter. In general, x(n) might be infinite, and in that case, computation of a value X(w) is impractical.

## Slide 11: Discrete Fourier Transform
The discrete Fourier transform (DFT) is particularly important in digital signal processing.
It transforms a periodic, discrete representation of a signal in one domain into a periodic, discrete representation in the other.
In this context, the term periodic is closely associated with the term finite.
Forward and inverse transformations are described by finite summations.
Notes: Summary of why we are interested in the DFT.

## Slide 12: Fast Fourier Transform
The term Fast Fourier transform (FFT) refers to a computationally efficient algorithm for calculating the DFT.
It requires fewer multiplications and additions than a more straightforward implementation of the DFT, and its relative advantage increases with the length of the sample sequences involved.
Based on symmetries in the structure of the DFT calculations and on the periodic nature of twiddle factors.
Notes: So where does the FFT fit into all of this? It’s not a further form of Fourier analysis.
Many slightly different variations of the FFT may be derived from the DFT.
In later slides, the radix-2 version will be described in detail.

## Slide 13: Discrete Fourier Transform
The N-point DFT of a discrete-time signal x(n) is:
It is often expressed
Where
Simplified notation
WN is referred to as a twiddle factor
Notes: The expression for the DFT (analysis or forward DFT in this case) may be simplified by the introduction of twiddle factors.

## Slide 14: Discrete Fourier Transform
The FFT takes advantage of :
and the symmetry (where N is even)
of the twiddle factors
The Periodicity
Notes: Each of the N different values of X(k) that make up the DFT of x(n) is computed from a sum of N products, and each of those products involves a twiddle factor W^kn. On the face of it, there are N^2 possible kn as 0<=k<N and 0<=n<N. Okay, some of these, e.g., n=1, k=3, and n=3, k=1, clearly imply the same value of twiddle factor – but what this slide is pointing out is that, in fact, there are only N possible different values of twiddle factor.

## Slide 15: Discrete Fourier Transform
Complex plane
imaginary
real
Evaluation of the N-point DFT involves nested summations over 0<k<N and 0<n<N, and hence many different values of kn in WNkn but recall that WN(k+N) = WNk
N=8
Notes: Graphical representation of twiddle factors as vectors in the complex plane (a twiddle factor is a constant, complex quantity). Note that a twiddle factor is a vector, not a phasor.
In this case, twiddle factors for an N=8 point DFT are shown. As the N=8 point DFT is evaluated, the exponent of the twiddle factor kn will take on a number of different values in the range 0 through N xN . This diagram illustrates that there will actually be only N distinct twiddle factor values.