## Slide 1: Adaptive Filters Prediction and System Identification

## Slide 2: Adaptive Filters
Adaptation - the ability of a system to cope with unexpected disturbances of the environment
Adaptive System - a system whose characteristics are alterable or adjustable in such a way that its behavior or performance improves according to some measure

## Slide 3: Characteristics of Adaptive Systems
Self-adjusting in the face of non-stationary environments and changing system requirements
Trained, rather than synthesized, to perform particular filtering operations
Non-linear systems with time-varying parameters
Notes: For non-stationary environment, read (stochastic) signals with time-varying statistical properties.

## Slide 4: Characteristics of Adaptive Systems
Inherently difficult to analyze
Have the potential to outperform non-adaptive systems

## Slide 5: Characteristics of Adaptive Systems
In general, the design of non-adaptive filters requires a priori knowledge of the characteristics of the signals involved.
Given this knowledge, optimal filters may be designed.
However, as signal characteristics change, these filters may be rendered sub-optimal.
Notes: For example, if a signal is corrupted by the addition of a sinusoid at a known frequency, we can design a notch filter to eliminate that sinusoid.

## Slide 6: Characteristics of Adaptive Systems
If knowledge of signal characteristics is inaccurate, incomplete, or unavailable, optimal filter design may not be possible.
In such cases, adaptive filters that continually seek optimum performance may be of use.

## Slide 7: Characteristics of Adaptive Systems
In general, adaptive systems must be considered non-linear.
We will consider so-called linear adaptive filters - if adaptation is disabled, they become linear filters.
These are useful. They are mathematically tractable and relatively easy to design.
Notes: Non-linear systems are, in general, difficult to analyze.
The LMS FIR (Least Mean Square Finite Impulse Response) filters that will be presented later are linear adaptive filters.

## Slide 8: Characteristics of Adaptive Systems
Adaptive filtering is at the core of much digital signal processing.
Adaptive filters do not rely on prior knowledge of signal statistics or characteristics to the same extent as non-adaptive filters.

## Slide 9: Closed Loop Configurations
Define the following signals.
filter
x
y
d
e
error
desired
output
output
adaptive
algorithm
input
Notes: We will concentrate on closed, as opposed to open, loop configurations. Desired output is usually derived in some way from the input. The error (difference between filter output and desired output) will be our performance indicator.

## Slide 10: Closed Loop Configurations
Alternatively, represent adaptive filter as a single block.
adaptive
filter
x
y
d
e
error
desired
output
output
input

## Slide 11: Closed Loop Configurations
Different closed loop configurations are concerned primarily with how desired output d is derived.
adaptive
filter
x
y
d
e
error
desired
output
output
input

## Slide 12: Closed Loop Configurations
In each case, however, the adaptive algorithm attempts to minimize error e in some sense.
adaptive
filter
x
y
d
e
error
desired
output
output
input
Notes: We don’t need to know how adaptation works in order to analyze the following configurations – just that it will seek to minimize the variance (average power) of the error signal e.

## Slide 13: a) Prediction
A delayed version of the desired signal s is fed to the adaptive filter, which tries to predict the current value of the desired signal.
adaptive
filter
x
y
d
e
delay
s
Notes: y is the predicted value of desired signal s, e is prediction error, x is a delayed version of the desired signal s.
The adaptive filter attempts to predict the current value of s based on its previous values.

## Slide 14: a) Prediction
A delayed version of the desired signal s is fed to the adaptive filter, which tries to predict the current value of the desired signal.
adaptive
filter
x
y
d
e
delay
s
Notes: Generic adaptive filter block is embedded in the diagram.

## Slide 15: a) Prediction
Prediction is used in signal encoding and noise reduction.
adaptive
filter
x
y
d
e
delay
s

## Slide 16: a) Prediction
Filter learns about the process by which the signal s is produced.
adaptive
filter
x
y
d
e
delay
s

## Slide 17: a) Prediction
Once filter has been trained, disable adaptation and remove d.
adaptive
filter
x
y
delay
s

## Slide 18: a) Prediction
Filter now predicts future values of x from past values.
adaptive
filter
x
y
delay
s

## Slide 19: b) System Identification
Broadband signal s applied to inputs of both unknown system and adaptive filter
adaptive
filter
x
y
d
e
unknown
plant
s

## Slide 20: b) System Identification
Broadband signal s applied to inputs of both unknown system and adaptive filter
adaptive
filter
x
y
d
e
unknown
plant
s
Notes: We’d like the same input to give the same output from both blocks.

## Slide 21: b) System Identification
Adaptive filter tries to emulate characteristics of unknown plant.
adaptive
filter
x
y
d
e
unknown
plant
s
Notes: In order to reduce the variance of the error signal.

## Slide 22: b) System Identification
After (successful) adaptation, plant characteristics have been identified.
adaptive
filter
x
y
d
e
unknown
plant
s
Notes: The adaptive filter is a model of the unknown plant.

## Slide 23: b) System Identification
Adaptive filter has learned input-output characteristics of unknown plant.
adaptive
filter
x
y
d
e
unknown
plant
s

## Slide 24: b) System Identification
Similar inputs to adaptive filter and unknown plant will yield similar outputs.
adaptive
filter
x
y
d
e
unknown
plant
s

## Slide 25: b) System Identification Application
Long-distance telephone echo cancellation
Notes: Echoes, due to impedance mismatches at the termination of long-distance telephone connections, can be distracting to users.

## Slide 26: b) System Identification Application
Ideally, hybrid routes incoming signal to and outgoing signal from telephone.
Notes: In order to see how the aforementioned impedance mismatches may occur, and lead to echoes , we will consider some simplified models of telephone circuits.
These may be slightly outdated but still serve to demonstrate an application of system identification using adaptive filters.
Ideally, a hybrid (located at a local exchange where local circuits are connected to long-distance circuits) passes signals from its input to the local circuit and from the local circuit to its output.
Signals should not be passed directly from hybrid input to hybrid output.
In practice, however, some leakage of this nature occurs due to impedance mismatches (between hybrid and long-distance circuits).
Leakage of incoming signals to the output port of a hybrid, in conjunction with delays in the long-distance circuit, leads to echoes.
Essentially, the hybrid leakage path is an unknown system element. Even if an echo is 40 dB down on an incoming signal, it may be apparent to a user.

## Slide 27: b) System Identification Application
Due to impedance mismatches, some of the incoming signal is returned.

## Slide 28: b) System Identification Application
Resultant echo can be distracting if connection is long-distance.

## Slide 29: b) System Identification Application
This hybrid leakage path is modeled by the adaptive filter.

## Slide 30: b) System Identification Application
Adaptation should be disabled in the presence of an outgoing signal.
Notes: This is an example of a system identification or direct modeling configuration. The unknown plant to be identified is the hybrid leakage path. The success of the scheme relies on the ability of the adaptive filter to match the characteristics of the hybrid leakage path.
Adaptation should be disabled while the local user is talking.