## Slide 1: Adaptive Filters Equalization and Noise Cancellation

## Slide 2: c) Equalization
Adaptive filter tries to recover delayed version of s from x.
adaptive
filter
x
y
d
e
unknown
plant
s
delay

## Slide 3: c) Equalization
Adaptive filter tries to recover delayed version of s from x.
adaptive
filter
x
y
d
e
unknown
plant
s
delay

## Slide 4: c) Equalization
x is formed by passing s through unknown plant.
adaptive
filter
x
y
d
e
unknown
plant
s
delay

## Slide 5: c) Equalization
Delay is included to allow for propagation of signals through plant and filter.
adaptive
filter
x
y
d
e
unknown
plant
s
delay

## Slide 6: c) Equalization
After (successful) adaptation, adaptive filter takes on inverse characteristics of plant.
adaptive
filter
x
y
d
e
unknown
plant
s
delay
Notes: i.e., in order to recover s from x.

## Slide 7: c) Equalization Application
Unknown plant might be a communication channel.
adaptive
filter
x
y
d
e
channel
s
delay
Notes: A very good question is how do we know desired signal d at far end (if we do know it, why are we bothering with equalization)

## Slide 8: c) Equalization Application
It is common to adjust filter at start of transmission using pre-arranged signal.
Notes: Pre-arranged signal is usually some form of pseudorandom noise sequence (with a wide spectrum).

## Slide 9: d) Noise Cancellation
primary sensor picks up signal s
adaptive
filter
y
d
e
signal
source
reference
sensor
primary
sensor
s
Notes: An adaptive noise canceller subtracts an estimate of the noise (in the received signal (s+n0)) from that received signal to give improved Signal to Noise Ratio (SNR).
Ordinarily, it would be inadvisable to attempt to subtract (estimated) noise from the received signal because this might, in fact, increase average noise power.
Assuming that n0 is correlated with n1 (both noise signals originate from the same source but reach the primary and reference sensors by different paths.)
And assuming that signal s is uncorrelated with either n0 or n1...

## Slide 10: d) Noise Cancellation
Unfortunately, this is corrupted by additive noise n0.
adaptive
filter
y
d
e
signal
source
noise
source
reference
sensor
primary
sensor
s
+
n
0
Notes: An adaptive noise canceller subtracts an estimate of the noise (in the received signal (s+n0)) from that received signal to give improved SNR.
Ordinarily, it would be inadvisable to attempt to subtract (estimated) noise from the received signal because this might, in fact, increase average noise power.
Assuming that n0 is correlated with n1 (both noise signals originate from the same source but reach the primary and reference sensors by different paths).
And assuming that signal s is uncorrelated with either n0 or n1...

## Slide 11: d) Noise Cancellation
Noise canceller will attempt to subtract noise n0 from signal at primary sensor .
adaptive
filter
y
d
e
signal
source
noise
source
reference
sensor
primary
sensor
s
+
n
0
Notes: An adaptive noise canceller subtracts an estimate of the noise (in the received signal (s+n0)) from that received signal to give improved SNR.
Ordinarily, it would be inadvisable to attempt to subtract (estimated) noise from the received signal because this might, in fact, increase average noise power.
Assuming that n0 is correlated with n1 (both noise signals originate from the same source but reach the primary and reference sensors by different paths).
And assuming that signal s is uncorrelated with either n0 or n1...

## Slide 12: d) Noise Cancellation
reference sensor positioned to pick up noise but not signal
adaptive
filter
y
d
e
signal
source
noise
source
reference
sensor
primary
sensor
s
+
n
0
Notes: An adaptive noise canceller subtracts an estimate of the noise (in the received signal (s+n0)) from that received signal to give improved SNR.
Ordinarily, it would be inadvisable to attempt to subtract (estimated) noise from the received signal because this might, in fact, increase average noise power.
Assuming that n0 is correlated with n1 (both noise signals originate from the same source but reach the primary and reference sensors by different paths).
And assuming that signal s is uncorrelated with either n0 or n1...

## Slide 13: d) Noise Cancellation
reference sensor positioned to pick up noise but not signal
Reference noise n1 is not identical to n0.
adaptive
filter
y
d
e
signal
source
noise
source
n
1
reference
sensor
primary
sensor
s
+
n
0
Notes: An adaptive noise canceller subtracts an estimate of the noise (in the received signal (s+n0)) from that received signal to give improved SNR.
Ordinarily, it would be inadvisable to attempt to subtract (estimated) noise from the received signal because this might, in fact, increase average noise power.
Assuming that n0 is correlated with n1 (both noise signals originate from the same source but reach the primary and reference sensors by different paths).
And assuming that signal s is uncorrelated with either n0 or n1...

## Slide 14: d) Noise Cancellation
However, we will assume that n0 and n1 are correlated and each is uncorrelated with s.
adaptive
filter
y
d
e
signal
source
noise
source
n
1
reference
sensor
primary
sensor
s
+
n
0
Notes: An adaptive noise canceller subtracts an estimate of the noise (in the received signal (s+n0)) from that received signal to give improved SNR.
Ordinarily, it would be inadvisable to attempt to subtract (estimated) noise from the received signal because this might, in fact, increase average noise power.
Assuming that n0 is correlated with n1 (both noise signals originate from the same source but reach the primary and reference sensors by different paths).
And assuming that signal s is uncorrelated with either n0 or n1...

## Slide 15: d) Noise Cancellation
Role of adaptive filter is to estimate n0 from n1.
adaptive
filter
y
d
e
signal
source
noise
source
n
1
reference
sensor
primary
sensor
s
+
n
0
Notes: An adaptive noise canceller subtracts an estimate of the noise (in the received signal (s+n0)) from that received signal to give improved SNR.
Ordinarily, it would be inadvisable to attempt to subtract (estimated) noise from the received signal because this might, in fact, increase average noise power.
Assuming that n0 is correlated with n1 (both noise signals originate from the same source but reach the primary and reference sensors by different paths).
And assuming that signal s is uncorrelated with either n0 or n1...

## Slide 16: d) Noise Cancellation
Role of adaptive filter is to estimate n0 from n1.
Intuitively, this appears feasible.
adaptive
filter
y
d
e
signal
source
noise
source
n
1
reference
sensor
primary
sensor
s
+
n
0
Notes: An adaptive noise canceller subtracts an estimate of the noise (in the received signal (s+n0)) from that received signal to give improved SNR.
Ordinarily, it would be inadvisable to attempt to subtract (estimated) noise from the received signal because this might, in fact, increase average noise power.
Assuming that n0 is correlated with n1 (both noise signals originate from the same source but reach the primary and reference sensors by different paths).
And assuming that signal s is uncorrelated with either n0 or n1...

## Slide 17: d) Noise Cancellation
Adaptive filter seeks to minimize average power in signal e.
adaptive
filter
y
d
e
signal
source
noise
source
n
1
reference
sensor
primary
sensor
s
+
n
0
Notes: An adaptive noise canceller subtracts an estimate of the noise (in the received signal (s+n0)) from that received signal to give improved SNR.
Ordinarily, it would be inadvisable to attempt to subtract (estimated) noise from the received signal because this might, in fact, increase average noise power.
Assuming that n0 is correlated with n1 (both noise signals originate from the same source but reach the primary and reference sensors by different paths).
And assuming that signal s is uncorrelated with either n0 or n1...

## Slide 18: d) Noise Cancellation
It is unreasonable to expect adaptive filter to estimate uncorrelated s from n1 .
adaptive
filter
y
d
e
signal
source
noise
source
n
1
reference
sensor
primary
sensor
s
+
n
0
Notes: An adaptive noise canceller subtracts an estimate of the noise (in the received signal (s+n0)) from that received signal to give improved SNR.
Ordinarily, it would be inadvisable to attempt to subtract (estimated) noise from the received signal because this might, in fact, increase average noise power.
Assuming that n0 is correlated with n1 (both noise signals originate from the same source but reach the primary and reference sensors by different paths).
And assuming that signal s is uncorrelated with either n0 or n1...

## Slide 19: d) Noise Cancellation
Minimizing average power in e equivalent to equaling average power in s
adaptive
filter
y
d
e
signal
source
noise
source
n
1
reference
sensor
primary
sensor
s
+
n
0
Notes: An adaptive noise canceller subtracts an estimate of the noise (in the received signal (s+n0)) from that received signal to give improved SNR.
Ordinarily, it would be inadvisable to attempt to subtract (estimated) noise from the received signal because this might, in fact, increase average noise power.
Assuming that n0 is correlated with n1 (both noise signals originate from the same source but reach the primary and reference sensors by different paths).
And assuming that signal s is uncorrelated with either n0 or n1...

## Slide 20: d) Noise Cancellation
Effectively, adaptive filter learns difference in paths between noise source and sensors.
adaptive
filter
y
d
e
signal
source
noise
source
n
1
reference
sensor
primary
sensor
s
+
n
0
Notes: The adaptive filter acts on noise n1 to produce a close replica of noise n0, which is then subtracted from the primary sensor signal (s+n0) with the objective of making (s+n0)-y a best fit to s.

## Slide 21: d) Noise Cancellation
Noise cancellation application viewed as system identification problem
Notes: Ignoring signal s, and viewing n0 as being the output of a system whose input is n1, the noise cancellation configuration resembles system identification.

## Slide 22: d) Noise Cancellation Applications
aircraft cockpit noise
electrocardiography

## Slide 23: Closed Loop Adaptive Filter Configurations
Four basic configurations are prediction, system identification, equalization, and noise cancellation.
Common to each is the notion of adaptive filter minimizing average power in e.
We can understand the applications without knowing exactly how adaptive filter works.
Notes: Summary.