## Slide 1: The Arm Cortex-M4 Processor Architecture
Part 2

## Slide 2: Module Syllabus
Cortex-M4 memory map
  Bit-band operations
  Cortex-M4 program image and endianness
Arm Cortex-M4 processor instruction set
  Arm and Thumb instruction set
  Cortex-M4 instruction set

## Slide 3: Cortex-M4 Memory Map
The Cortex-M4 processor has 4 GB of memory address space
  Support for bit-band operation (detailed later)
The 4GB memory space is architecturally defined with a number of regions
  Each region is designed for particular recommended uses.
  Easy for software programmers to port between different devices
Note that, despite the default definitions, the actual usage of the memory map can also be flexibly defined by the user, other than some fixed memory addresses such as the internal private peripheral bus (PPB)
Notes: The Arm Cortex-M4 memory map describes the organization of the processor’s address space. The address space contains data sources and sinks such as internal and external RAM and ROM as well as buses, peripherals, and further parts and equipment.
The total memory space of a 32-bit system like the Cortex-M4 is 2^32 = 4GB. It is split and separated into regions with different functionality, which can be individually changed, apart from some fixed assigned addresses, e.g., of the internal PPB of the processor.

## Slide 4: Arm Cortex-M4 Memory Map
Private peripherals
e.g., NVIC, SCS
Mainly used for external peripherals
e.g., SD card
Mainly used for external memories
e.g., external DDR, FLASH, LCD
Mainly used for on-chip peripherals
e.g., AHB, APB peripherals
Mainly used for data memory
e.g., on-chip SRAM, SDRAM
Mainly used for program code
e.g., on-chip FLASH
Vendor-specific
Memory
External device
External RAM
Peripherals
SRAM
Code
0xFFFFFFFF
0xE0000000
PPB
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE0100000
Reserved for other purposes
ROM table
External PPB
Embedded trace macrocell
Trace port interface unit
Reserved
System Control Space, including
Nested Vectored Interrupt
Controller (NVIC)
Reserved
Fetch patch and breakpoint unit
Data watchpoint and trace unit
Instrumentation trace macrocell
External PPB
Internal PPB
Notes: The Arm architecture uses a single flat address space of 2^(32) 8-bit bytes. Byte addresses are treated as unsigned numbers running from 0 to 2^(32) – 1. The above figure shows the memory regions of ARMv7-M architecture. Each region has a defined memory type, and some regions have additional memory attributes. The memory type and attributes determine the behavior of accesses to the region.

## Slide 5: Arm Cortex-M4 Memory Map
Code region
  Primarily used to store program code
  Can also be used for data memory
  On-chip memory, such as on-chip FLASH
SRAM region
  Primarily used to store data, such as heaps and stacks
  Can also be used for program code
  On-chip memory; despite its name “SRAM,” the actual device could be SRAM, SDRAM, etc
Peripheral region
  Primarily used for peripherals, such as Advanced High-performance Bus (AHB) or Advanced Peripheral Bus (APB) peripherals
  On-chip peripherals
Notes: The code region with 0x00000000- 0x1FFFFFFF address range is the executable region for the program core. Data can also be put here.
The SRAM region with 0x20000000- 0x3FFFFFFF address range is the executable region for data. Code can also be put here. This region includes the bit band and bit band alias areas.
The peripheral region with 0x40000000- 0x5FFFFFFF address range is used for peripherals attached to the core on the address and data bus. This region includes bit band and bit band alias areas.

## Slide 6: Arm Cortex-M4 Memory Map
External RAM region
  Primarily used to store large data blocks or memory caches
  Off-chip memory, slower than on-chip SRAM region
External device region
  Primarily used to map to external devices
  Off-chip devices, such as SD cards
PPB
  Provides access to internal and external processor resources
Notes: The external region 0x60000000 - 0x9FFFFFFF address range is the executable region for data.
The external device region with 0xA0000000 - 0xDFFFFFFF address range is the external device memory, which is primarily used to map external devices.
The PPB region with 0xE0000000 - 0xE00FFFFF address range provides access to internal and external processor resources.

## Slide 7: Cortex-M4 Memory Map Example
AHB/ APB
External SRAM,
FLASH
External LCD
SD card
Cortex-M4
PPB
SCS
NVIC
Debug CTRL
On-chip FLASH
(Code Region)
On-chip SRAM
(SRAM Region)
Peripheral Region
External memory interface
(External RAM Region)
External device interface
(External Device Region)
Timer
UART
GPIO
Chip Silicon
Vendor specific
Memory
External device
External RAM
Peripherals
SRAM
Code
0xFFFFFFFF
0xE0000000
PPB
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
0xE00FFFFF
0xE0100000
Notes: In this figure, a structural example of the memory map is given. Beginning at the top, the processor internal elements connected to the PPB, such as debug ctrl and NVIC, are implemented. All additional components are connected to the processor via the AHB , including the on-chip peripherals such as the timer, general purpose input/output ports, or communication systems like UART. Directly attached to the high-performance bus are the chip internal memory components for the ROM (flash) and RAM. However, external memory and peripheral components share a common interface with the AHB among several components.

## Slide 8: Bit-band Operations
Bit-band operations allow a single load/store operation to access a single bit in the memory, for example, to change a single bit of =32-bit data:
  Normal operation without bit-band (read-modify-write)
    Read the value of 32-bit data
    Modify a single bit of the 32-bit value (keep other bits unchanged)
    Write the value back to the address
  Bit-band operation
    Directly write a single bit (0 or 1) to the “bit-band alias address” of the data
Bit-band alias address
  Each bit-band alias address is mapped to a real data address
  When writing to the bit-band alias address, only a single bit of the data will be changed
Notes: For bit-wise data manipulations with 32-bit operations, Arm has introduced an alternative: the bit band operations.
The standard operation without bit-band is read-modify-write: First, we load a full 32-bit word into the registers. Then, we manipulate the corresponding bit with AND, OR, XOR instructions in full word length, and, finally, we write the word back. If this operation (read-modify-write) is interrupted, there can be a data loss. One way to avoid data loss is the interrupt disabling using a supervisor mode or by using bit banding operations.
Using bit-band operation, the corresponding data word is bitwise aliased into bit-band-memory area. So every original bit has now the aliased size of a word. The bits to be manipulated can be directly accessed with word wise operating instructions. Because of the aliasing, everything modified within the “linked copy” of the data will directly be changed in the original data.

## Slide 9: Arm Cortex-M4 Memory Map
For example, in order to set bit[3] in word data in address 0x20000000:
Read-modify-write operation
  Reads the data (0x21) from the address 0x20000000
  The interrupt changes the data of 0x20000000 address to 0x79 and then returns
  Writes back the modified old data
  0x79 has been lost!
;Read-Modify-Write Operation
LDR R1, =0x20000000 ;Setup address
LDR R0, [R1] ;Read 0x21
ORR.W R0, #0x8 ;Set bit[3]
STR R0, [R1] ;Write back 0x29
Interrupt!
...
LDR R1, =0x20000000 ;Setup address
STR R2,[R1] ;Write back 0x79
...
Return!
Notes:   Let’s say that we want to set bit[3] in word data in address 0x20000000.
  Usually we read the data from the address, then modify them and, finally, we write back the new value.
  In this example, you can see that the read-modify-write cycle is interrupted, and the value of the address 0x20000000 is changed by the ISR right after reading the data from the address.
  After returning from the routine, the application continues its normal execution but the modification and write back will be done based on the old value. Consequently, the change that was made by the ISR will be lost.

## Slide 10: Bit-band Operation Example
Bit-band operation
  Directly set the bit by writing “1” to address 0x2200000C, which is the alias address of the fourth bit of the 32-bit data at 0x20000000.
  In effect, this single instruction is mapped to two bus transfers: read data from 0x20000000 to the buffer, and then write to 0x20000000 from the buffer with bit [3] set
;Bit-band Operation
LDR R1, =0x2200000C ;Setup address
MOV R0, #1 ;Load data
STR R0, [R1] ;Write
Notes: Alternatively, using the bit band operation you can see that we set the desired bit by writing “1” to the alias address and, with a single instruction, we can set the desired bit of the 0x20000000 address to 1, thereby avoiding any data loss.

## Slide 11: Bit-band Alias Address
Each bit of the 32-bit data is one-to-one mapped to the bit-band alias address.
  For example, the fourth bit (bit [3]) of the data at 0x20000000 is mapped to the bit-band alias address at 0x2200000C
  Hence, to set bit [3] of the data at 0x20000000, we only need to write “1” to address 0x2200000C
  In Cortex-M4, there are two predefined bit-band alias regions: one for the SRAM region, and one for peripherals region
0x20000000
0x20000004
0x20000008
Real 32-bit data address
0x22000000
0x22000080
0x22000100
0x2200000C
0x22000018
Bit-band alias address
Notes: The SRAM-area 0x20000000-0x200FFFFF may be directly accessed and manipulated by 32-bit-instructions in the bit-band alias area 0x22000000-0x23FFFFFF, simulating and bitwise manipulating as every original bit is mapped to a byte:
0x22000000 equals Bit 0 of 0x20000000
0x22000004 equals Bit 1 of 0x20000000
0x22000008 equals Bit 2 of 0x20000000
0x22000020 equals Bit 0 of 0x20000001
...
bit-band-address = bit-band-basis-address + (byte-offset × 32) + bit[0-7] × 4)
0x22000020 = 0x22000000 + 1 × 32 + 0 × 4

## Slide 12: Bit-band Alias Address
SRAM region
  32MB memory space (0x22000000 – 0x23FFFFFF) is used as the bit-band alias region for 1MB data (0x20000000 – 0x200FFFFF)
Peripherals region
  32MB memory space (0x42000000 – 0x43FFFFFF) is used as the bit-band alias region for 1MB data (0x40000000 – 0x400FFFFF)
External RAM
Peripherals
SRAM
Code
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1MB Bit-band region
32MB Bit-band alias
31MB non-bit-band region
0x20000000
0x20100000
0x22000000
0x23FFFFFF
0x21FFFFFF
1MB Bit-band region
32MB Bit-band alias
31MB non-bit-band region
0x40000000
0x40100000
0x42000000
0x43FFFFFF
0x41FFFFFF
Notes: SRAM and peripheral regions include bit band and bit band alias areas.

## Slide 13: Benefits of Bit-band Operations
Faster bit operations
Fewer instructions
Atomic operation, avoid hazards
  For example, if an interrupt is triggered and served during the read-modify-write operations, and the interrupt service routine modifies the same data, a data conflict will occur
Interrupt occurs
Read data at 0x00
Modify bit [1]
Read data at 0x00
Modify bit [1]
Write data back
Write data back
Interrupt returns
Bit [1] modified by ISR is overwritten
by the main program
Interrupt Service Routine
Main program
Notes: Bit-band operations require fewer (in fact, only one) instructions, and therefore are called “atomic” because they cannot be split further.
This also protects them from data corruption caused by interrupts that could modify the just read memory. If the bit manipulation is performed in the traditional way, the memory block is read first, and directly after the reading an interrupt occurs. Such an interrupt could theoretically modify the just read data in their original destination. After the interrupt releases the processor again, the bit manipulation continues and writes the modified, but not out dated, data back; therefore, a data corruption has occurred.
This cannot happen with bit band operations, because they modify the data within one single step.

## Slide 14: Cortex-M4 Program Image
The program image in Cortex-M4 contains
  Vector table: includes the starting addresses of exceptions (vectors) and the value of the main stack point (MSP)
  C start-up routine
  Program code: application code and data
  C library code: program codes for C library functions
0x00000000
Code region
Start-up routine &
Program code &
C library code
Vector table
Program
Image
Initial MSP value
Reset vector
NMI vector
Hard fault vector
MemManage fault
Reserved
PendSV
SysTick
External Interrupts
Bus fault
Usage fault
Reserved
SVCall
Debug monitor
Notes: A program starting at 0x00000000 is subdivided into the following parts. First, the vector tables are located. To save memory space, they are consolidated to bytes or words, so-called bit vectors. Therefore, a vector needs to be evaluated bitwise to interpret the meaning or origin of the change. The size of the vector table is 64 byte + 4 byte for each used interrupt vector. The start-up routine, program code, and static libraries are located beyond the vector table.

## Slide 15: Cortex-M4 Program Image
After reset, the processor:
  First reads the initial MSP value
  Then reads the reset vector
  Then branches to the start of the program execution address (reset handler)
  Subsequently executes program instructions
Reset
Fetch initial value for MSP
(Read address 0x00000000)
Fetch reset vector
(Read address 0x00000004)
Fetch 1st instruction
(Read address of reset vector)
Fetch 2nd instruction
(Read subsequent instructions)
Notes: After reset, the MSP initializes the address of the beginning of the stack. Then, the reset vector defines the address of the first line of executable code and is located at address 0x00000004. From now on, the program can be started and executed line by line.

## Slide 16: Cortex-M4 Endianness
Endian refers to the order of bytes stored in memory
  Little endian: lowest byte of a word-size data is stored in bit 0 to bit 7
  Big endian: lowest byte of a word-size data is stored in bit 24 to bit 31
Cortex-M4 supports both little endian and big endian
However, endianness only exists in the hardware level
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
0x00000000
0x00000004
0x00000008
Address
[7:0]
[15:8]
[23:16]
[31:24]
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
[7:0]
[15:8]
[23:16]
[31:24]
Word 1
Word 2
Word 3
Word 1
Word 2
Word 3
Little endian 32-bit memory
Big endian 32-bit memory
Notes: Endianness describes the order in which bytes have to be combined in halfwords or words. For Arm architectures, the endianness has little significance as either word wise operations (4 byte) are performed automatically in the correct order by the instruction set, or the information is stored in single bytes regardless of any endianness.
Endianness is only important if half words (2 bytes) are manually stored byte wise. In this case, we must consider whether the most significant byte is stored first or last. If the most significant byte is stored at the highest bit positions, this is called “little endianness”. In contrast, if the most significant byte is stored at the lowest bit positions, this is called “big endianness”.

## Slide 17: Arm Cortex-M4 Processor and Thumb Instruction Sets
Early Arm instruction set
  32-bit instruction set, called the Arm instructions
  Powerful and good performance
  Larger program memory compared to 8-bit and 16-bit processors
  Larger power consumption
Thumb-1 instruction set
  16-bit instruction set, first used in ARM7TDMI processor in 1995
  Provides subset of Arm instructions, with better code density compared to 32-bit RISC architecture
  Code size is reduced by ~30%, but performance is also reduced by ~20%
Notes: The Arm standard instruction set is 32 bits long with three operand formats for load and store operations, where most instructions can be executed conditionally and in a single cycle. One side effect of the early Arm instruction set is that it required larger program memory than 8- or 16-bit processors, and larger power consumption as more information needed to be moved.
By comparison, Thumb-1 is a 16‐bit instruction set which is optimized for code density from C code. It is a subset of the Arm instruction set functionality with better code density, but worse performance. Thumb instructions are executed unconditionally, and many of the data processing instructions use a 2‐address format. As a result of the dense encoding, Thumb instruction formats are less regular than Arm instruction formats.

## Slide 18: Arm and Thumb Instruction Set
Mix of Arm and Thumb-1 instruction sets
  Benefit from both 32-bit Arm (high performance) and 16-bit Thumb-1 (high code density)
  A multiplexer is used to switch between two states: Arm state (32-bit) and Thumb state (16-bit), which requires a switching overhead
Thumb-2 instruction set
  Consists of both 32-bit Thumb instructions and original 16-bit Thumb-1 instruction sets
  Compared to 32-bit Arm instructions set, code size is reduced by ~26%, with similar performance
  Capable of handling all processing requirements in one operation state
Incoming
Instructions
Thumb remap
to Arm
Arm
Instruction
decoder
Instructions
Executing
T bit, 0: select Arm,
1: select Thumb
0
1
Notes: In earlier processor architectures, Arm and Thumb 1 instructions could be mixed, but required switching a multiplexer between the two instruction sets. That reduces the speed due to the switching overhead.
Thumb-2 is a superset of the Thumb instruction set. Thumb-2 introduces 32-bit instructions that are mixed with the 16-bit instructions. The Thumb-2 instruction set covers almost all the functionality of the Arm instruction set. Thumb-2 is backwards compatible with the ARMv6 Thumb instruction set.
The most important difference between the Thumb-2 instruction set and the Arm instruction set is that most Thumb-2 instructions are unconditional, where as almost all Arm instructions can be conditional.
Thumb-2’s performance is close to or better than that of the Arm instruction set, and has the code density of the original Thumb 1.

## Slide 19: Cortex-M4 Instruction Set
Cortex-M4 processor
  Armv7-M architecture
  Supports 32-bit Thumb-2 instructions
  Can handle all processing requirements in one operation state (Thumb state)
  Compared with traditional Arm processors (which use state switching), advantages include:
    No state switching overhead: both execution time and instruction space are saved
    No need to separate Arm code and Thumb code source files, which makes the development and maintenance of software easier
    Easier to get optimized efficiency and performance
Notes: The Cortex-M4 implements the Armv7-M instruction set. Armv7-M supports a large number of 32-bit instructions that Thumb-2 technology introduced into the Thumb instruction set. The Floating-point (FP) extension adds single-precision floating-point instructions to the Thumb instruction set.
The Thumb instruction stream is a sequence of halfword-aligned halfwords. Each Thumb instruction is either a single 16-bit halfword in that stream, or a 32-bit instruction consisting of two consecutive halfwords in that stream.

## Slide 20: Cortex-M4 Instruction Set
Arm assembly syntax:
  label
    mnemonic operand1, operand2, … ; Comments
  Label is used as a reference to an address location.
  Mnemonic is the name of the instruction.
  Operand1 is the destination of the operation.
  Operand2 is normally the source of the operation.
  Comments are written after “ ; ”, which does not affect the program, e.g.:
  MOVS R3, #0x11 ;Set register R3 to 0x11
  Assembly code can be assembled by either Arm assembler (armasm) or assembly tools from a variety of vendors (e.g., GNU tool chain). When using the GNU tool chain, the syntax for labels and comments is slightly different.
Notes: Labels are symbolic representations of addresses. You can use labels to mark specific addresses that you want to refer to from other parts of the code.
Mnemonic is the name of the instruction. Most data processing instructions can optionally update the condition flags according to the result of the operation. You can also execute an instruction conditionally, based on the condition flags set in another instruction, either immediately after the instruction that updated the flags, or after any number of intervening instructions that have not updated the flags.
Conditional execution is available by using conditional branches or by adding condition code suffixes to instructions. The condition code suffix enables the processor to test a condition based on the flags. If the condition test of a conditional instruction fails, then the instruction does not execute, does not write any value to its destination register, does not affect any of the flags, and does not generate any exception.
An instruction operand can be an Arm register, a constant, or another instruction-specific parameter.
Instructions act on the operands and often store the result in a destination register.
When there is a destination register in the instruction, it is usually specified before the operands.
Note that instruction mnemonics, pseudo-instructions, directives, and symbolic register names can be written in all uppercase or all lowercase, but not mixed. Labels and comments can be in uppercase or lowercase, or mixed.

## Slide 21: Arm Cortex-M4 Instruction Set: Overview
Instructions supported by the Cortex-M4 processor can be grouped as follows:
Memory access instructions
General data processing instructions
Multiply and divide instructions
Saturating instructions
Packing and unpacking instructions
Bitfield instructions
Branch and control instructions
Miscellaneous instructions
Floating-point instructions
Notes: Memory access instructions:
Addresses can be accessed directly by indicating the explicit or relative address at which the content is stored. It can also be accessed indirectly, by pointing to an address where the address for the content is stored. Indirect addressing is a particular advantage if large fields need to be manipulated, e.g., sorted, and the data of one element are not limited to a single memory cell, but are a structure of many memory elements. In this case, the addresses of the root elements are sorted, which is less effort than sorting the elements themselves.
General data processing instructions:
The instructions for general data processing contain everything for mathematical operations, bit manipulation, and comparison.
  Multiply and divide instructions:
There are two ways to multiply and divide. The first is to right- and left-shift the bits of a number (division by two and multiplication by two, respectively) and the second is bitwise multiplication and addition.
  Saturating instructions:
Saturating instructions cover data-range over- and underflow for different kinds of integer and floating-point additions and subtractions.
  Packing and unpacking instructions:
  Packing and unpacking contains range and precision changing operations.
  Bitfield instructions:
Bitfield instructions are designed for a similar purpose as packing und unpacking instructions. If two bitfields of different length have to be processed for logical operation, then their sizes have to be aligned.
  Branch and control instructions:
Control structures are used if the control must be transferred to another part of the instruction space, or when the next PC must not be executed.
Branches are conditional transfers of control, when the target address is close to the current PC location.
Jumps are unconditional transfers of control with unpredictable distance of jump.
  Miscellaneous instructions:
Further, unclassified instructions are mainly used for superordinate actions like debugging, interrupting, and synchronization.
Floating-point instructions:
Floating point instructions are instructions that deal with floating point registers and operations.

## Slide 22: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
ADC, ADCS | {Rd,} Rn, Op2 | Add with Carry | N,Z,C,V
ADD, ADDS | {Rd,} Rn, Op2 | Add | N,Z,C,V
ADD, ADDW | {Rd,} Rn, #imm12 | Add | N,Z,C,V
ADR | Rd, label | Load PC-relative Address | 
AND, ANDS | {Rd,} Rn, Op2 | Logical AND | N,Z,C
ASR, ASRS | Rd, Rm, <Rs¦#n> | Arithmetic Shift Right | N,Z,C
B | label | Branch | 
BFC | Rd, #lsb, #width | Bit Field Clear | 
BFI | Rd, Rn, #lsb, #width | Bit Field Insert | 
BIC, BICS | {Rd,} Rn, Op2 | Bit Clear | N,Z,C
BKPT | #imm | Breakpoint | 
BL | label | Branch with Link | 
BLX | Rm | Branch indirect with Link | 
BX | Rm | Branch indirect | 

## Slide 23: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
CBNZ | Rn, label | Compare and Branch if Non Zero | 
CBZ | Rn, label | Compare and Branch if Zero | 
CLREX |  | Clear Exclusive | 
CLZ | Rd, Rm | Count Leading Zeros | 
CMN | Rn, Op2 | Compare Negative | N,Z,C,V
CMP | Rn, Op2 | Compare | N,Z,C,V
CPSID | i | Change Processor State, Disable Interrupts | 
CPSIE | i | Change Processor State, Enable Interrupts | 
DMB |  | Data Memory Barrier | 
DSB |  | Data Synchronization Barrier | 
EOR, EORS | {Rd,} Rn, Op2 | Exclusive OR | N,Z,C
ISB | - | Instruction Synchronization Barrier | 

## Slide 24: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
IT |  | If-Then condition block | 
LDM | Rn{!}, reglist | Load Multiple registers, increment after | 
LDMDB, LDMEA | Rn{!}, reglist | Load Multiple registers, decrement before | 
LDMFD, LDMIA | Rn{!}, reglist | Load Multiple registers, increment after | 
LDR | Rt, [Rn, #offset] | Load Register with word | 
LDRB, LDRBT | Rt, [Rn, #offset] | Load Register with byte | 
LDRD | Rt, Rt2, [Rn, #offset] | Load Register with two bytes | 
LDREX | Rt, [Rn, #offset] | Load Register Exclusive | 
LDREXB | Rt, [Rn] | Load Register Exclusive with Byte | 
LDREXH | Rt, [Rn] | Load Register Exclusive with Halfword | 
LDRH, LDRHT | Rt, [Rn, #offset] | Load Register with Halfword | 

## Slide 25: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
LDRSB, LDRSBT | Rt, [Rn, #offset] | Load Register with Signed Byte | 
LDRSH, LDRSHT | Rt, [Rn, #offset] | Load Register with Signed Halfword | 
LDRT | Rt, [Rn, #offset] | Load Register with word | 
LSL, LSLS | Rd, Rm, <Rs¦#n> | Logical Shift Left | N,Z,C
LSR, LSRS | Rd, Rm, <Rs¦#n> | Logical Shift Right | N,Z,C
MLA | Rd, Rn, Rm, Ra | Multiply with Accumulate, 32-bit result | 
MLS | Rd, Rn, Rm, Ra | Multiply and Subtract, 32-bit result | 
MOV, MOVS | Rd, Op2 | Move | N,Z,C
MOVT | Rd, #imm16 | Move Top | 
MOVW, MOV | Rd, #imm16 | Move 16-bit constant | N,Z,C
MRS | Rd, spec_reg | Move from Special Register to general register | 
MSR | spec_reg, Rm | Move from general register to Special Register | N,Z,C,V

## Slide 26: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
MUL, MULS | {Rd,} Rn, Rm | Multiply, 32-bit result | N,Z
MVN, MVNS | Rd, Op2 | Move NOT | N,Z,C
NOP |  | No Operation | 
ORN, ORNS | {Rd,} Rn, Op2 | Logical OR NOT | N,Z,C
ORR, ORRS | {Rd,} Rn, Op2 | Logical OR | N,Z,C
PKHTB, PKHBT | {Rd, } Rn, Rm, Op2 | Pack Halfword | 
POP | reglist | Pop registers from stack | 
PUSH | reglist | Push registers onto stack | 
QADD | {Rd, } Rn, Rm | Saturating double and Add | Q
QADD16 | {Rd, } Rn, Rm | Saturating Add 16 | 
QADD8 | {Rd, } Rn, Rm | Saturating Add 8 | 

## Slide 27: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
QASX | {Rd, } Rn, Rm | Saturating Add and Subtract with Exchange | 
QDADD | {Rd, } Rn, Rm | Saturating Add | Q
QDSUB | {Rd, } Rn, Rm | Saturating double and Subtract | Q
QSAX | {Rd, } Rn, Rm | Saturating Subtract and Add with Exchange | 
QSUB | {Rd, } Rn, Rm | Saturating Subtract | Q
QSUB16 | {Rd, } Rn, Rm | Saturating Subtract 16 | 
QSUB8 | {Rd, } Rn, Rm | Saturating Subtract 8 | 
RBIT | Rd, Rn | Reverse Bits | 
REV | Rd, Rn | Reverse byte order in a word | 
REV16 | Rd, Rn | Reverse byte order in each halfword | 
REVSH | Rd, Rn | Reverse byte order in bottom halfword and sign extend | 
ROR, RORS | Rd, Rm, <Rs¦#n> | Rotate Right | N,Z,C

## Slide 28: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
RRX, RRXS | Rd, Rm | Rotate Right with Extend | N,Z,C
RSB, RSBS | {Rd,} Rn, Op2 | Reverse Subtract | N,Z,C,V
SADD16 | {Rd, } Rn, Rm | Signed Add 16 | GE
SADD8 | {Rd, } Rn, Rm | Signed Add 8 | GE
SASX | {Rd, } Rn, Rm | Signed Add and Subtract with Exchange | GE
SBC, SBCS | {Rd,} Rn, Op2 | Subtract with Carry | N,Z,C,V
SBFX | Rd, Rn, #lsb, #width | Signed Bit Field Extract | 
SDIV | {Rd,} Rn, Rm | Signed Divide | 
SEV |  | Send Event | 
SHADD16 | {Rd,} Rn, Rm | Signed Halving Add 16 | 
SHADD8 | {Rd,} Rn, Rm | Signed Halving Add 8 | 
SHASX | {Rd,} Rn, Rm | Signed Halving Add and Subtract with Exchange | 

## Slide 29: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
SHSAX | {Rd,} Rn, Rm | Signed Halving Subtract and Add with Exchange | 
SHSUB16 | {Rd,} Rn, Rm | Signed Halving Subtract 16 | 
SHSUB8 | {Rd,} Rn, Rm | Signed Halving Subtract 8 | 
SMLABB, SMLABT, SMLATB, SMLATT | Rd, Rn, Rm, Ra | Signed Multiply Accumulate Long (halfwords) | Q
SMLAD, SMLADX | Rd, Rn, Rm, Ra | Signed Multiply Accumulate Dual | Q
SMLAL | RdLo, RdHi, Rn, Rm | Signed Multiply with Accumulate (32 x 32 + 64), 64-bit result | 
SMLALBB, SMLALBT, SMLALTB, SMLALTT | RdLo, RdHi, Rn, Rm | Signed Multiply Accumulate Long, halfwords | 
SMLALD, SMLALDX | RdLo, RdHi, Rn, Rm | Signed Multiply Accumulate Long Dual | 
SMLAWB, SMLAWT | Rd, Rn, Rm, Ra | Signed Multiply Accumulate, word by halfword | Q
SMLSD | Rd, Rn, Rm, Ra | Signed Multiply Subtract Dual | Q
SMLSLD | RdLo, RdHi, Rn, Rm | Signed Multiply Subtract Long Dual | 
SMMLA | Rd, Rn, Rm, Ra | Signed Most significant word Multiply Accumulate | 

## Slide 30: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
SMMLS, SMMLR | Rd, Rn, Rm, Ra | Signed Most significant word Multiply Subtract | 
SMMUL, SMMULR | {Rd,} Rn, Rm | Signed Most significant word Multiply | 
SMUAD | {Rd,} Rn, Rm | Signed dual Multiply Add | Q
SMULBB, SMULBT SMULTB, SMULTT | {Rd,} Rn, Rm | Signed Multiply (halfwords) | 
SMULL | RdLo, RdHi, Rn, Rm | Signed Multiply (32 x 32), 64-bit result | 
SMULWB, SMULWT | {Rd,} Rn, Rm | Signed Multiply word by halfword | 
SMUSD, SMUSDX | {Rd,} Rn, Rm | Signed dual Multiply Subtract | 
SSAT | Rd, #n, Rm {,shift #s} | Signed Saturate | Q
SSAT16 | Rd, #n, Rm | Signed Saturate 16 | Q
SSAX | {Rd,} Rn, Rm | Signed Subtract and Add with Exchange | GE
SSUB16 | {Rd,} Rn, Rm | Signed Subtract 16 | 
SSUB8 | {Rd,} Rn, Rm | Signed Subtract 8 | 

## Slide 31: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
STM | Rn{!}, reglist | Store Multiple registers, increment after | 
STMDB, STMEA | Rn{!}, reglist | Store Multiple registers, decrement before | 
STMFD, STMIA | Rn{!}, reglist | Store Multiple registers, increment after | 
STR | Rt, [Rn, #offset] | Store Register word | 
STRB, STRBT | Rt, [Rn, #offset] | Store Register byte | 
STRD | Rt, Rt2, [Rn, #offset] | Store Register two words | 
STREX | Rd, Rt, [Rn, #offset] | Store Register Exclusive | 
STREXB | Rd, Rt, [Rn] | Store Register Exclusive Byte | 
STREXH | Rd, Rt, [Rn] | Store Register Exclusive Halfword | 
STRH, STRHT | Rt, [Rn, #offset] | Store Register Halfword | 
STRT | Rt, [Rn, #offset] | Store Register word | 
SUB, SUBS | {Rd,} Rn, Op2 | Subtract | N,Z,C,V

## Slide 32: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
SUB, SUBW | {Rd,} Rn, #imm12 | Subtract | N,Z,C,V
SVC | #imm | Supervisor Call | 
SXTAB | {Rd,} Rn, Rm,{,ROR #} | Extend 8 bits to 32 and add | 
SXTAB16 | {Rd,} Rn, Rm,{,ROR #} | Dual extend 8 bits to 16 and add | 
SXTAH | {Rd,} Rn, Rm,{,ROR #} | Extend 16 bits to 32 and add | 
SXTB16 | {Rd,} Rm {,ROR #n} | Signed Extend Byte 16 | 
SXTB | {Rd,} Rm {,ROR #n} | Sign extend a byte | 
SXTH | {Rd,} Rm {,ROR #n} | Sign extend a halfword | 
TBB | [Rn, Rm] | Table Branch Byte | 
TBH | [Rn, Rm, LSL #1] | Table Branch Halfword | 
TEQ | Rn, Op2 | Test Equivalence | N,Z,C
TST | Rn, Op2 | Test | N,Z,C

## Slide 33: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
UADD16 | {Rd,} Rn, Rm | Unsigned Add 16 | GE
UADD8 | {Rd,} Rn, Rm | Unsigned Add 8 | GE
USAX | {Rd,} Rn, Rm | Unsigned Subtract and Add with Exchange | GE
UHADD16 | {Rd,} Rn, Rm | Unsigned Halving Add 16 | 
UHADD8 | {Rd,} Rn, Rm | Unsigned Halving Add 8 | 
UHASX | {Rd,} Rn, Rm | Unsigned Halving Add and Subtract with Exchange | 
UHSAX | {Rd,} Rn, Rm | Unsigned Halving Subtract and Add with Exchange | 
UHSUB16 | {Rd,} Rn, Rm | Unsigned Halving Subtract 16 | 
UHSUB8 | {Rd,} Rn, Rm | Unsigned Halving Subtract 8 | 
UBFX | Rd, Rn, #lsb, #width | Unsigned Bit Field Extract | 
UDIV | {Rd,} Rn, Rm | Unsigned Divide | 
UMAAL | RdLo, RdHi, Rn, Rm | Unsigned Multiply Accumulate Accumulate Long (32 x 32 + 32 +32), 64-bit result | 

## Slide 34: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
UMLAL | RdLo, RdHi, Rn, Rm | Unsigned Multiply with Accumulate (32 x 32 + 64), 64-bit result | 
UMULL | RdLo, RdHi, Rn, Rm | Unsigned Multiply (32 x 32), 64-bit result | 
UQADD16 | {Rd,} Rn, Rm | Unsigned Saturating Add 16 | 
UQADD8 | {Rd,} Rn, Rm | Unsigned Saturating Add 8 | 
UQASX | {Rd,} Rn, Rm | Unsigned Saturating Add and Subtract with Exchange | 
UQSAX | {Rd,} Rn, Rm | Unsigned Saturating Subtract and Add with Exchange | 
UQSUB16 | {Rd,} Rn, Rm | Unsigned Saturating Subtract 16 | 
UQSUB8 | {Rd,} Rn, Rm | Unsigned Saturating Subtract 8 | 
USAD8 | {Rd,} Rn, Rm | Unsigned Sum of Absolute Differences | 
USADA8 | {Rd,} Rn, Rm, Ra | Unsigned Sum of Absolute Differences and Accumulate | 
USAT | Rd, #n, Rm {,shift #s} | Unsigned Saturate | Q
USAT16 | Rd, #n, Rm | Unsigned Saturate 16 | Q

## Slide 35: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
UASX | {Rd,} Rn, Rm | Unsigned Add and Subtract with Exchange | GE
USUB16 | {Rd,} Rn, Rm | Unsigned Subtract 16 | GE
USUB8 | {Rd,} Rn, Rm | Unsigned Subtract 8 | GE
UXTAB | {Rd,} Rn, Rm,{,ROR #} | Rotate, extend 8 bits to 32 and Add | 
UXTAB16 | {Rd,} Rn, Rm,{,ROR #} | Rotate, dual extend 8 bits to 16 and Add | 
UXTAH | {Rd,} Rn, Rm,{,ROR #} | Rotate, unsigned extend and Add Halfword | 
UXTB | {Rd,} Rm {,ROR #n} | Zero extend a Byte | 
UXTB16 | {Rd,} Rm {,ROR #n} | Unsigned Extend Byte 16 | 
UXTH | {Rd,} Rm {,ROR #n} | Zero extend a Halfword | 
VABS.F32 | Sd, Sm | Floating-point Absolute | 
VADD.F32 | {Sd,} Sn, Sm | Floating-point Add | 
VCMP.F32 | Sd, <Sm ¦ #0.0> | Compare two floating-point registers, or one floating-point register and zero | FPSCR

## Slide 36: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
VCMPE.F32 | Sd, <Sm ¦ #0.0> | Compare two floating-point registers, or one floating-point register and zero with Invalid Operation check | FPSCR
VCVT.S32.F32 | Sd, Sm | Convert between floating-point and integer | 
VCVT.S16.F32 | Sd, Sd, #fbits | Convert between floating-point and fixed point | 
VCVTR.S32.F32 | Sd, Sm | Convert between floating-point and integer with rounding | 
VCVT<B¦H>.F32.F16 | Sd, Sm | Converts half-precision value to single-precision | 
VCVTT<B¦T>.F32.F16 | Sd, Sm | Converts single-precision register to half-precision | 
VDIV.F32 | {Sd,} Sn, Sm | Floating-point Divide | 
VFMA.F32 | {Sd,} Sn, Sm | Floating-point Fused Multiply Accumulate | 
VFNMA.F32 | {Sd,} Sn, Sm | Floating-point Fused Negate Multiply Accumulate | 
VFMS.F32 | {Sd,} Sn, Sm | Floating-point Fused Multiply Subtract | 
VFNMS.F32 | {Sd,} Sn, Sm | Floating-point Fused Negate Multiply Subtract | 
VLDM.F<32¦64> | Rn{!}, list | Load Multiple extension registers | 

## Slide 37: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
VLDR.F<32¦64> | <Dd¦Sd>, [Rn] | Load an extension register from memory | 
VLMA.F32 | {Sd,} Sn, Sm | Floating-point Multiply Accumulate | 
VLMS.F32 | {Sd,} Sn, Sm | Floating-point Multiply Subtract | 
VMOV.F32 | Sd, #imm | Floating-point Move immediate | 
VMOV | Sd, Sm | Floating-point Move register | 
VMOV | Sn, Rt | Copy Arm core register to single precision | 
VMOV | Sm, Sm1, Rt, Rt2 | Copy 2 Arm core registers to 2 single precision | 
VMOV | Dd[x], Rt | Copy Arm core register to scalar | 
VMOV | Rt, Dn[x] | Copy scalar to Arm core register | 
VMRS | Rt, FPSCR | Move FPSCR to Arm core register or APSR | N,Z,C,V
VMSR | FPSCR, Rt | Move to FPSCR from Arm Core register | FPSCR
VMUL.F32 | {Sd,} Sn, Sm | Floating-point Multiply | 

## Slide 38: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
VNEG.F32 | Sd, Sm | Floating-point Negate | 
VNMLA.F32 | Sd, Sn, Sm | Floating-point Multiply and Add | 
VNMLS.F32 | Sd, Sn, Sm | Floating-point Multiply and Subtract | 
VNMUL | {Sd,} Sn, Sm | Floating-point Multiply | 
VPOP | list | Pop extension registers | 
VPUSH | list | Push extension registers | 
VSQRT.F32 | Sd, Sm | Calculates floating-point Square Root | 
VSTM | Rn{!}, list | Floating-point register Store Multiple | 
VSTR.F<32¦64> | Sd, [Rn] | Stores an extension register to memory | 
VSUB.F<32¦64> | {Sd,} Sn, Sm | Floating-point Subtract | 
WFE |  | Wait For Event | 
WFI |  | Wait For Interrupt | 

## Slide 39: Cortex-M4 Instruction Set
Cortex-M4 suffix
  Some instructions can be followed by suffixes to update processor flags or execute the instruction on a certain condition.
Suffix | Description | Example | Example explanation
S | Update APSR (flags) | ADDS R1, #0x21 | Add 0x21 to R1 and update APSR
EQ, NE, CS, CC, MI, PL, VS, VC, HI, LS, GE, LT, GT, LE | Condition execution e.g., EQ = equal, NE = not equal, LT = less than | BNE label | Branch to the label if not equal

## Slide 40: Data Insertion and Alignment
Insert data inside programs
  DCD: insert a word-size data
  DCB: insert a byte-size data
  ALIGN:
    Used before inserting a word-size data
    Uses a number to determine the alignment size
For example:
  …
  ALIGN 4 ; Align to a word boundary
  MY_DATA DCD 0x12345678 ; Insert a word-size data
  MY_STRING DCB “Hello”, 0 ; Null terminated string
  …
Notes: DCB and DCD define the initial runtime contents of the memory. A DCB directive allocates one or more bytes of memory, whereas a DCD directive allocates one or more words of memory, aligned on 4-byte boundaries.
The ALIGN directive aligns the current location to a specified boundary, by padding with zeros or NOP instructions to ensure that the data and code is aligned to appropriate boundaries.