## Slide 1: Multithreading
Module 9

## Slide 2: Module Syllabus
Multitasking
Fine-grained multithreading
  Thread selection
  Case study
Coarse-grained multithreading
  Case study
Simultaneous multithreading (SMT)
  SMT policies
  Case study
Notes: This module looks at multithreading; that is, sharing a core between threads from the same or different applications at some granularity.

## Slide 3: Motivation
Multicore processors are the most generic way of extracting coarse-grained parallelism.
  Allow exploitation of thread-level parallelism (within a program) and process-level parallelism (across applications).
They are also the most simple extension of a uniprocessor.
  Simply replicate the core several times on the chip.
  Add the logic for implementing cache coherence, etc.
However, they come at significant costs.
  Over 2x area and power cost for a simple replication of the core and private caches
Other architectural choices allow us to extract this parallelism with fewer overheads.
  Such as sharing the core between threads at some granularity
This module considers the trade-offs involved in achieving this.
Notes: In the previous module, we looked at multicore processors, the methods of communicating between cores and techniques to ensure data are propagated when required. Multicore processors are a common way of exploiting thread-level parallelism (TLP) that exists in the system. For the area price of an additional core, two threads can run (one on each core), essentially doubling the throughput of the system. Each core remains the same though, so the throughput of each core may well be suboptimal. If we want to exploit TLP, we may be able to do so without moving to multicore by sharing the core between several threads. This will increase the throughput of the core itself with vastly lowered costs compared to multicore. In certain application domains that don’t need the full processing power of a single core for each thread (e.g., databases, online transaction processing), this can be a seductive proposition. When multiple threads share a core at some granularity, we call it multithreading.

## Slide 4: Multitasking
Each of our cores can currently be shared by multiple threads.
  Mediated and controlled by the operating system
This enables multitasking by having each thread (task) run for a fixed period of time.
  Short periods give the appearance that all threads actually run concurrently.
The process of changing between running threads is called a context switch.
  The OS saves (switches out) the state (context) of the running thread.
  And replaces it with the state of another thread, which can then run on the core.
Thread A
Thread B
Context switch
Thread C
Notes: We start, however, with a look at how a core without multithreading support is shared between threads. A thread is a single execution context (i.e., architectural registers, memory information, etc.) that the operating system (OS) schedules to run on a particular core. An application is a process made up from one or more threads, and in a shared-memory system, all threads from the same process share an address space.
Without multithreading support in the core, sharing is achieved through a system called multitasking that is controlled and mediated by the OS. The OS periodically picks the thread to run on the core and schedules it in by performing a context switch. Here, all the state, or context, of the currently running thread is saved to memory, and the context of the soon-to-be-run thread is restored to the core. If context switches occur often enough, then to the user, there is the illusion of the threads running concurrently, whereas in reality, they aren’t. However, there is a trade-off to be made, since context switches take time to perform, time that is not spent running application code, and so the shorter the time between context switches, the more overhead and inefficiency there is in the system.

## Slide 5: Multitasking
During a context switch, the OS has to save the thread’s state, which for the core is
  Contents of the (architectural) register file
  Program counter (PC)
  Memory-management information, such as the page table base register
Saving all this state can be very slow.
  Usually, 100 s of cycles
Can we improve this situation to achieve
  Fewer cycles required for context switching
  Better throughput from the core
Without the full-blown costs of going to multicore?
Notes: The thread’s context is made up of all externally visible state. This includes the architectural registers and program counter, along with memory-management information (all of the page tables). Many processors provide logic to avoid having to save and remove all this information (e.g., process ID bits within the translation lookaside buffer (TLB)). However, there can still be a considerable cost to context switching, on the order of hundreds of cycles. Ideally, we’d be reducing this so that context switches could occur more frequently between the threads whose state is saved within the processor.

## Slide 6: Multithreading
Reducing the context-switch overhead is easy if we’re prepared to pay a small price for it.
By adding extra storage to the core, we can hold the context for more than one thread.
  The price here is area devoted to the context storage.
This means that a context switch between two threads with stored contexts is much faster.
  Only a few cycles instead of several hundreds
  Because the storage is all very close to the core
We now have a core capable of multithreading.
This core works at arbitrary granularity.
  i.e., with many cycles between each switch
  Or even selecting a new thread every cycle
Core
A
B
C
D
Notes: We can obviously achieve our aim of faster context switches by providing storage in the processor for a number of different thread contexts and simply saving and restoring to these when switching between those particular threads (we’ll have to go to memory for others). The operating system can decide which threads have their context saved on the processor. However, now that the context switches take so short a time (only a few cycles), we don’t want the overhead of invoking the OS to make the decision to switch. What makes more sense is to let the core take care of that itself. In other words, the core has the contexts of a number of different threads available to it, and the core decides when to fetch instructions from each of them. A core that can make these decisions is a core that supports multithreading. We’ll now explore the different types of multithreading that define how the core makes these decisions and their microarchitectural impact.

## Slide 7
Fine-grained Multithreading

## Slide 8: Fine-grained Multithreading
Now that we have the ability to switch to a new thread, when should we do it?
With fine-grained multithreading, we switch to a new thread every cycle.
This means that in each stage of the pipeline is an instruction from a different thread.
We can use a simple round-robin policy for choosing the next thread to fetch from.
  If the thread is stalled, send a NOP instead.
Thread A
Thread B
Thread C
Thread D
Thread E
Fetch
Decode
Execute
Memory
Writeback
Notes: With fine-grained multithreading, we don’t switch to a new thread solely on a long-latency event, but every cycle. A simple approach is to simply fetch from an ordered set of threads one at a time (i.e., round robin) and send a nop down the pipeline if the thread is stalled for some reason. With enough threads and a short, single-issue pipeline, this can mean that we guarantee that only one instruction from any thread will be present in the core at any time. This means that we don’t have to implement interlocks for data dependencies between instructions through registers. We could go further and replace the data cache with a scratchpad, which will provide strong performance guarantees about the execution time of each instruction.
Of course, more complex schemes exist for choosing threads to fetch from that don’t permit these simplifications but do increase the potential performance of the core.
Fine-grained static multithreading with a simple round-robin policy might be preferred to using a low-frequency multicore processor since, with enough threads, the multithreaded core provides better throughput since it rarely stalls the pipeline. In addition, threads share data at the L1 cache (or scratchpad), whereas in a multicore sharing likely occurs at the L2 or nearer memory.

## Slide 9: Trade-offs of Fine-grained Multithreading
Provided no two instructions from the same thread are in the pipeline together
Benefits
No thread-switch overhead
No need for pipeline interlocking
  No two instructions will have a data dependency through registers (they might through memory).
No need for branch prediction logic
  All branches executed before the next instruction are fetched from the same thread.
Hides short pipeline bubbles
Improved core throughput
Downsides
Need to support a large number of threads
  So as to hide most short-latency pipeline bubbles and avoid nops
  This comes at an area cost.
Single-threaded performance suffers.
  Since threads only get an instruction fetched every N cycles
  But this can bring strong performance guarantees.
Notes: This slide shows the trade-offs of fine-grained multithreading, assuming that each instruction within the pipeline comes from a different thread. The main downsides are that single-threaded performance suffers and that a large number of threads may need to be supported to hide the majority of stalls.

## Slide 10: Dynamic Thread Selection
The most simple approach to fine-grained multithreading always fetches from a thread.
  Even when that thread is stalled – a nop is fetched instead.
However, the presence of nops reduces the performance of the core.
  This is wasteful of the time-slot when other threads have actual work to do.
We can change the basic round-robin thread-switching policy to improve the situation.
  Order threads as in round robin.
  Skip a thread if it is stalled and would have sent a nop into the pipeline.
This kind of dynamic thread selection improves throughput even more.
  But needs additional logic to implement it
  And either needs the dependence-check logic adding back in
  Or extra logic to detect when there are fewer ready threads than pipeline stages
Notes: Ideally, we wouldn’t send nops down the pipeline since they don’t do any useful work. We can improve the performance of the core by altering the fetch policy so that it dynamically determines which thread to fetch from each cycle. An intuitive scheme maintains the round-robin policy but simply skips threads that are stalled. Of course, we can’t get the performance guarantees or omission of dependence-check logic discussed in previous slides, but do get higher throughput. Other policies exist, too, to prioritize threads and alter the order in which they are selected for fetch.

## Slide 11: Dynamic Thread Selection
Thread A
Thread B
Thread C
Thread D
Thread E
Thread F
Thread G
Static round-robin selection
Dynamic round-robin thread selection
Stall
Time
Notes: This slide shows an example of dynamic thread selection with seven threads. Colored rectangles show instructions for each thread and yellow rectangles are timeslots where that thread would be stalled (assuming a 5-stage pipeline). If the static round-robin policy is used for fetch, shown in the upper bar, then each thread is a fetch from, or a nop sent down the pipeline in the yellow slots. The lower bar shows the dynamic policy where threads are still selected in the same order, but skipped if they are stalled. Therefore, the stall cycles are saved, and the whole execution finished 8 cycles earlier than before. In this example, there is still only ever a maximum of one instruction from any thread in the pipeline at any given time.

## Slide 12: Case Study: Sun’s Niagara (UltraSPARC T1)
Each core of eight supports four concurrent threads.
Threads removed from selection on long-latency events
This allows provision of only 16KiB instruction and 8KiB data caches.
Notes: The Niagara processor was designed for server environments (e.g., web servers and databases) and optimized for throughput rather than single-threaded performance. It contained eight cores, each supporting four threads. Within each core, the register files and store buffers are replicated so each thread can have a private set. Almost all of the remaining structures are shared across the 6-stage pipeline (fetch, thread-select, decode, execute, memory, writeback), including L1 cache, TLB, and functional units. A single instruction from one thread is selected on each cycle; the set of threads to choose from is dynamically created depending on the instruction type and pipeline events. For single-cycle ALU operations, instructions from the same thread can be selected on subsequent cycles; for an L1 cache access of three cycles, the thread stalls for two cycles before becoming available for selection again. From the available threads, the thread-select logic gives priority to the least-recently used thread.
More information can be found in the paper: Niagara: a 32-way multithreaded Sparc processor. P. Kongetira, K. Aingaran, and K. Olukotun. IEEE Micro, volume 25, issue 2, March-April 2005.

## Slide 13
Coarse-grained Multithreading

## Slide 14: Coarse-grained Multithreading
An alternative design point is course-grained multithreading.
  Switching less often (and flushing when doing so) means the core requires less per-thread state.
An obvious point to switch is when the thread is stalled for some reason, e.g., a cache miss.
Switching at fixed frequency
Switching on long-latency event
Thread A
Thread B
Thread C
Stall
Thread switch
Notes: The most conceptually similar multithreading technique to the multitasking seen earlier is coarse-grained multithreading. Here, the core executes a single thread at time just like a non-multithreading core, but performs a thread switch when the thread experiences some long-latency event, such as a cache miss (especially a last-level cache miss). The reasoning behind this is that upon an event such as this, the thread will not be able to make forward progress until the data have returned from the memory hierarchy. The core will be idle, and therefore not performing useful work. Instead, if we switch threads, the newly switched-in thread can execute its instructions, and the core is once again being used.
In the example above, there are three threads. If switching were to occur at a fixed frequency (i.e., after a certain number of cycles), then thread A would execute a bit, then experience a cache miss, and the core would stall (yellow). Its data would return, more instructions would be executed until another cache miss and stall. After that, only a few instructions would be executed before a thread switch (orange), and thread B could get a turn. Both threads B and C experience a single stall during their time on the core. On the other hand, if thread switching were to occur upon the cache miss, then A would execute a few instructions before switching to B, which would execute until its own cache miss, at which point C would be switched in. There are more thread switches but no idle time during stalls, so the overall effect is a gain in performance (throughput).
Note that we use the terminology “thread switch” to mean a fast context switch made by the core between threads whose contexts are stored in the processor, and “context switch” to mean changing the threads whose contexts are mapped to the core, which is performed by the operating system.

## Slide 15: Coarse-grained Multithreading
The switch to a new thread increases the throughput of the core.
  Although switching takes time, we only do it for stalls that are longer than that overhead.
However, care has to be taken in how the switch is implemented.
In particular, instructions after the long-latency event must be squashed.
  This adds to the switching time.
To avoid the additional design complexity of handling instructions from different threads in the pipeline at any given time, the pipeline has to be flushed before switching.
  This incurs in an overhead.
  Finer granularities may justify handling instructions from different threads within the pipeline at the same time.
Notes: The thread-switch implementation needs to ensure that instructions in the pipeline after the one that caused the long-latency event are squashed. The alternative is to change the core so that instructions from multiple threads can be present at the same time, which adds to the complexity of the design (but does reduce the thread-switch time).

## Slide 16: Coarse-grained Multithreading
Reasons for switching threads
L1 or L2 cache miss
  Accessing main memory takes hundreds of cycles, and if the thread-switch penalty is small enough, even an L1 miss can be partially hidden.
Complex ALU operation
  A floating-point divide may take tens of cycles and may not be pipelined.
Timeout
  This ensures fairness for compute-bound threads.
Higher priority thread becomes ready.
Methods to reduce thread-switch penalty
Implement a short pipeline.
  This reduces the time until the pipeline becomes full again.
Add a thread-switch buffer
  Essentially prefetch a few instructions from each thread into a buffer so that they can be fetched (for real) immediately after a switch.
Provide pipeline registers for each thread.
  So now no instructions need to be squashed on a long-latency event, but added complexity.
Notes: This slide shows different reasons for switching threads that the core might implement. Generally, a timeout is required so that a compute-bound thread can be pre-empted and doesn’t starve other threads.
The slide also shows techniques for reducing the thread-switch penalty (i.e., the time taken to stop executing one thread and start another). A thread-switch buffer holds the first few instructions that each thread will execute, meaning that it is very quick to start executing (once the thread’s context is switched in).

## Slide 17: Case Study: Intel Montecito (Itanium 2)
Support for two threads per core
  Duplicates all architectural and some microarchitectural state
Each thread is given an “urgency” value.
  Larger urgency means higher priority.
  Urgency is dynamically updated based on system events.
Thread switching possibly occurs on
  L3 cache miss or data return
  Timeout, software hint, or other system event
Diagram shows two threads with events.
  Colored when switched in, white when switched out
  Urgency value inside boxes
5
5
5
4
5
5
7
7
4
5
6
6
5
Thread switch
L3 miss
Data return
Thread A
Thread B
After timeout, A executes even with a lower urgency value
Notes: Intel’s Itanium 2 processor, codename Montecito, was a dual-core processor where each core supported coarse-grained multithreading for two threads. All architectural and some microarchitectural state was duplicated (such as the advanced load address table (ALAT) and return address stack). Other structures were shared but contained tags to avoid one thread polluting the other (e.g., the branch predictor). There were five reasons for switching threads: an L3 cache miss or data return, timeout, software hint, ALAT invalidation, and transition to low-power mode.
Each thread was given an urgency value in the range 0-7 with 5 being the default. An L3 cache miss decreased the urgency (saturating at 0) and data return increased it again (saturating at 5). If a thread was switched out due to a timeout, then it was given the urgency value of 7. Whenever the urgency value was altered by a cache miss, the two threads were compared and a thread switch performed to the higher of the two.
The diagram shows an example execution. The top bar is thread A and the bottom is thread B. The different shades of blue show execution of that thread’s instructions whereas white is when the thread is switched out. Inside each portion of the bar is the urgency value for that thread. L3 misses are yellow; data return is green; orange is a thread switch.
Initially, both threads have urgency value 5 and thread A is executing. It experiences an L3 miss, so its urgency is reduced to 4, which triggers a thread switch since B’s urgency is higher. A’s data return during B’s execution, increasing A’s urgency again, but since it is not higher than B’s, then no thread switch occurs. After a while, a timeout occurs and another thread switch, and this raises B’s urgency to 7. At this point, A executes even though its urgency value is lower than B’s, because B already had its share of time on the core, hence the timeout. A executes and then experiences another cache miss, which switches it out. B executes with urgency 7, and although its cache misses reduce its urgency, it never drops below A’s urgency, so no further thread switches occur. Note that when B’s data return, its urgency is not increased due to the saturation at 5.
More information can be found in the paper: Montecito: a dual-core, dual-thread Itanium processor. C. McNairy and R. Bhatia. IEEE Micro, volume 25, issue 2, March-April 2005.

## Slide 18: Beyond Coarse-grained Multithreading
Coarse-grained multithreading allows us to hide some of the stall latency.
  The core performs useful work again once thread switching has occurred.
  And the techniques discussed previously help reduce the thread-switch penalty.
However, we don’t switch often, so smaller pipeline stalls still exist.
  For example, ALU operations taking only a few cycles
Either pay the price of per-thread pipeline registers or suffer the switching penalty.
  Per-thread pipeline registers may be overkill if switching occurs infrequently.
Or we can move in the other direction and allow instructions from multiple threads per pipeline stage simultaneously.
Notes: Whilst coarse-grained multithreading provides some benefits, we may be able to increase throughput further by allowing instructions from multiple threads to intermingle throughout the whole pipeline, as we’ll see next.

## Slide 19
Simultaneous Multithreading (SMT)

## Slide 20: Simultaneous Multithreading
Coarse- and fine-grained multithreading enable higher throughput from a core.
  By switching to a new thread either every cycle or on certain events
These are called temporal multithreading.
  Each pipeline stage holds instructions from only a single thread – the core is shared across time.
  Instructions from different threads can occur in the pipeline at different stages.
However, in superscalar cores, this does not increase pipeline utilization.
  During periods of low IPC in a particular thread, some functional units are idle.
Simultaneous multithreading is a way to tackle this.
  Instructions from multiple threads can occupy a pipeline stage at the same time.
  This increases the number of ready instructions available to execute.
Notes: Superscalar cores do not often realize their full throughput potential, since threads rarely have enough instructions ready on each cycle to sustain the peak performance that the core is designed for. This is especially true during program phases containing low instructions per cycle (IPC). Moving from coarse-grained multithreading to fine-grained multithreading, the obvious next step is to continue integration of instructions from different threads within the pipeline and that leads to simultaneous multithreading, which can help improve throughput expanding the set of instructions ready on each cycle and by using core resources (e.g., functional units) more fully.

## Slide 21: Simultaneous Multithreading
SMT allows instructions from different threads to be in-flight concurrently.
  All the way through the pipeline
Instructions from multiple threads are:
  Fetched, decoded, renamed, dispatched, issued, executed, and committed each cycle
Microarchitectural resources throughout the pipeline are shared between threads.
  This means that there should be fewer unused resources because more independent instructions exist.
As with other forms of multithreading, the designer has to duplicate architectural state.
  PC, register file, page table base register, etc.
And implement fetch logic to fetch instructions from one or more threads in each cycle
  As well as the additional logic to distinguish between threads within the pipeline
Notes: Within an SMT core, throughout the pipeline instructions from multiple threads are in-flight concurrently. Although stages of the pipeline may make decisions based on the thread, an instruction comes from (e.g., fetch and issue), the majority of other stages do not.

## Slide 22: SMT Example
Instruction issue in a 4-way superscalar core
Thread D
Thread C
Thread B
Thread A
Time
SMT execution
Notes: This slide shows an example of SMT execution. Each of the four threads is shown in isolation at the top of the slide. We assume a 4-way superscalar core, showing the issue stage of the pipeline, with time in cycles moving left to right and represented by the rectangles. For each thread, the vertical stack of four rectangles indicates the four issue slots available to that thread in one cycle. Colored rectangles indicate where instructions would fill the issue slot; white rectangles are unfilled slots.
No thread alone fills all available issue slots with instructions. Some, such as thread D, have very few instructions that can be issued due to dependencies between instructions and multicycle operations.
At the bottom of the slide, the execution of these four threads on an SMT-enabled core is shown. A set of all ready instructions is maintained (not shown, initially filled in the order A-B-C-D), and instructions are placed in their issue slots when they are the oldest instruction for that slot and it is available. As can be seen, the overall execution time for each thread is increased, but for the majority of the cycles, all issue slots can be filled, significantly increasing core throughput.

## Slide 23: SMT Policies
Fetch policies
Flexibility in how instructions enter the pipeline
Fetch from one thread only in each cycle
  Round-robin selection
  Prioritize one thread over others, for example, the one with the fewest in-flight instructions
Fetch from multiple threads
  Needs additional logic to fetch from multiple cache lines in the same cycle
Issue policies
Flexibility in how instructions are issued to the functional units when ready
Issue from all threads in each cycle
  Skip threads that have no ready instructions
Prioritize instructions according to
  Their age (oldest first)
  Whether they are speculative (e.g., following an unresolved predicted branch)
Notes: The main policies governing thread selection in an SMT core are those around fetching instructions and issuing them to the functional units. Simple schemes use a round-robin approach, but thread priority can be incorporated to perturb this order.

## Slide 24: SMT Downsides
There are two main drawbacks with SMT, and fine-grained multithreading.
First, single-threaded performance may suffer.
  If two or more threads execute, they will contend for resources.
  Given the extra logic required within the core, the clock rate may not be as high as it could be otherwise.
Second, the complexity of the core increases.
  Extra hardware required throughout the pipeline, as well as within the TLB
  This requires more design, test, and verification time.
  The load/store queue, in particular, requires careful attention so as to respect the memory consistency model.
Notes: SMT does have some downsides, which are mainly that single-threaded performance may suffer and that the extra logic within the core increases complexity.

## Slide 25: SMT vs Multicore
SMT
Higher utilization of core structures through sharing
Single-threaded performance can suffer.
For a modest area and power increase, this provides support for multiple threads.
Memory-bound applications are a good fit because idle cycles can be filled.
CPU-bound applications are a poor fit because they are likely to slow down.
Multicore
Cores are fully duplicated, so threads have dedicated resources to use.
Single-threaded performance maintained
Power and area at least doubled through core duplication
Memory-bound applications don’t make best use of the core’s resources.
CPU-bound applications maintain their high IPC.
Notes: Compared to a multicore approach, SMT provides greater throughput at the expense of single-threaded performance and a small increase in area. Multicore, however, provides greater throughput of the system (not the core) whilst maintaining single-threaded performance, but with a significant increase in area. The best type of system depends on the target application domain and characteristics of the programs.

## Slide 26: SMT Case Study
Intel’s Netburst microarchitecture supports 2 threads.
Performance boosted by 25%
Die area increased only 5%
Three types of sharing for microarchitectural structures
Trace
cache
Fetch
queue
Rename
Schedule
Register
read
Execute
Data
cache
Register
write
Retire
queue
Notes: The Netburst microarchitecture was Intel’s first consumer (i.e., not server) processor to contain SMT, which Intel calls hyperthreading. Two threads were supported within the core with all processor resources shared apart from the program counter, register alias tables, instruction TLB, return stack predictor, interrupt controller, trace-cache next-instruction pointer and fill buffers, and instruction-streaming buffers.
Three types of sharing are implemented. With partitioned sharing, equal resources are given to each thread. Sharing the pipeline queues in the in-order part of the core is an example of this. With threshold sharing, each thread has a limit on the maximum number of resources it can hold at any time. The scheduler is shared in this manner. Finally, with full sharing, threads can occupy as much of the resource as they need. Caches are shared using this policy.
More information can be found in the paper: Hyperthreading technology in the netburst microarchitecture. D. Koufaty and D. T. Marr. IEEE Micro, volume 23, issue 2, March-April 2003.

## Slide 27: Case Study: Cortex-A65
Scheduled for 2020
Arm’s first SMT Cortex-A core
Cortex-A65 implements a 64-bit ISA only
Built on DynamIQ technology
  DSU contains all the interfaces to connect to the system on chip (SoC).
Dual-threaded, out-of-order execution
  Each thread is a PE.
Separate L1 instruction and data cache
  L2 cache is optional.
  L3 cache in DSU
Notes: The Cortex-A65 core is a power-efficient, mid-range, throughput computing oriented, Simultaneously MultiThreaded (SMT) core that implements the AArch64 execution state of the Armv8-A architecture. The Cortex-A65 core does not implement the AArch32 execution state of the Armv8-A architecture.
The diagram in this slide shows an example Cortex-A65 core configuration. The Cortex-A65 core has several interfaces to connect it to a SoC. The DSU manages all the interfaces. The DSU also contains the L3 cache
As an SMT core, the Cortex-A65 core supports two execution threads on each core. Each thread is a separate architectural Processing Element (PE), and so has a complete copy of the architectural state.
The simultaneous nature of the multithreading means that the Cortex-A65 core is able to issue and execute instructions from both threads simultaneously in the same cycle. Software views a thread on the Cortex-A65 core in the same way as it would view a core in a traditional, single-threaded, multi-core processor. Thus, existing software for both single core and multi-core can run unmodified on the Cortex-A65 core.
In an Arm DynamIQ Shared Unit (DSU) cluster, each Cortex-A65 core has a separate Level 1 (L1) instruction cache, a separate L1 data cache, and an optional private per-core Level 2 (L2) cache.
For more information, see the Arm® DynamIQ™ Shared Unit Technical Reference Manual and Arm Cortex-A65 Technical Reference Manual.

## Slide 28: Summary
We can increase the throughput of a core by implementing multithreading.
Coarse-grained multithreading is most similar to multitasking.
  Thread switching occurs on long-latency events.
  Because thread contexts are kept near the core, thread switching is much faster than an OS context switch.
Fine-grained multithreading increases throughput further.
  Can eliminate many short pipeline bubbles
  And can also provide strong performance guarantees in certain microarchitectures
SMT provides full sharing within each stage of the pipeline.
  This enables higher utilization of core structures.
All forms of multithreading exploit thread-level parallelism to improve performance.