## Slide 1: A SoC Case Study
Module 11

## Slide 2: Module Syllabus
System-on-Chip (SoC) concepts
Overview of typical IP blocks
Example SoC designs
Notes: In this final module, we will tie in together the concepts we have learned in the previous Computer Architecture modules and look at how some of those concepts are put together in a System-on-Chip (SoC).

## Slide 3: A System-on-chip (SoC) Case Study
In this final module, we are going to explore a modern System-on-Chip or “SoC.”
  SoCs are designed for particular markets and meet target design goals by combining many different IP blocks.
  They contain both programmable processors and application-specific IP.
We’ll examine each of its building blocks and main features.
And look at how each of these individual “IP” blocks are brought together
Notes: What is a SoC?
A SoC contains many different IP blocks, including programmable processors, integrated on one chip. They aim to meet design goals through a combination of hardware and software. SoCs emerged as transistor budgets grew and permitted greater levels of integration, and this helped to reduce both cost and power consumption.
IP blocks
When designing a SoC, it is typical to use intellectual property from several sources. Each IP core, or IP block, performs a particular function and is the intellectual property of one company. Examples of IP blocks include processor cores, GPUs, on-chip interconnect, peripherals, memory controllers, and off-chip interfaces.
Physical interfaces (“PHYs”)
When communicating off-chip, we must implement the physical layer functionality, the circuitry that actually drives the pins and receives the data according to a particular interface specification (e.g., USB).
The circuit or IP necessary for this is often abbreviated simply to “PHY,” short for “Physical Interfaces.” This is a common term especially when talking about interfaces such as DRAM (e.g., “DDR PHY”) and for off-chip communication standards such as USB (e.g., “a USB4 PHY”). PHYs are often provided as “hard” IP meaning that the final layout is provided. This removes the need for every user of the IP to try to produce the actual layout. For off-chip interfaces with very tight timing constraints, this can be challenging.
Logic libraries and embedded memories
When designing a chip, we will also need access to logic libraries and embedded memory (SRAM, register file, and ROM) compilers. Logic gates are contained within “standard cell libraries.” These contain hundreds of different logic gates with descriptions of their function, layout, power, and timing characteristics. EDA tools take hardware descriptions at the Register Transfer Level (RTL) and synthesize implementations built from standard cells.

## Slide 4: Why Create a Custom System-on-chip (SoC)?
Reduced cost
Reduced PCB area and volume
Increased performance and reduced power consumption
Product differentiation
SoCs integrate a range of IP types: processors, custom processors, accelerators, on-chip memories, peripherals and interfaces, etc.
Notes: There are clear advantages in greater levels of integration, e.g., improved performance and reduced cost, size and power consumption. Of course, there are also significant costs associated with designing and manufacturing a new SoC, e.g., the cost of making the unique set of masks needed to fabricate a chip. These Non-Recurring Engineering (NRE) costs must be recovered, normally through the manufacture of a very high number of chips. The costs mean that very large target markets are typically required to justify the design of high-performance SoCs, e.g., the mobile computing market.
Highly integrated, low-cost and low-power SoCs have also helped to create new markets such as the Internet-of-Things (IoT).

## Slide 5: System-on-chip (SoC) Design
Let’s define some high-level design goals and constraints for a SoC example:
Target market: client device (e.g., mobile phone, tablet, etc.)
Area = ~70-80 mm2 in 7 nm fabrication technology
Transistor budget: ~7-8 billion transistors
Performance: Excellent general-purpose performance over a wide range of workloads, e.g., image processing, 2D/3D graphics, machine learning applications. Some requirements for real-time processing capabilities
Off-chip memory bandwidth: 32 GB/s
Power: 2-3 W peak (only in short bursts on smartphones)
Notes: In this module, we will explore the architecture and technologies for SoCs that have the design goals and constraints that are suitable for mobile phones or tablet computers.
The target market helps us define some high-level goals and constraints based on things such as capacity of batteries (a smartphone battery has a capacity of ~10,000 mWh).
CPU power consumption (2-3 W in this example) is often limited to short bursts due to limited ability to dissipate heat. Laptops and tablets will be able to sustain higher power consumption with larger batteries and better cooling.
The cost per chip dictates the area available and the transistor budget. Note, the transistors used to create logic are relatively large compared to those in on-chip SRAM.
Off-chip bandwidth to main memory has grown quickly for mobile products as new memory standards are introduced (we assume a 64-bit bus below):
Date introduced/standard/memory bandwidth offered
2013 - LPDDR3 ~17 GB/s
2015 - LPDDR4 ~32 GB/s (i.e., 4 × 16-bit channels)
2019 - LPDDR5 ~44 GB/s (+30% over LPDDR4)

## Slide 6: High-level View of Our System-on-chip (SoC) Example
Cache Coherent Interconnect
4 MB Shared L3 Cache
GPU
(750 MHz)
Machine Learning
Accelerator
Display
Processor
Video
Processor
Interconnect
System
Control
Processor
(SCP)
Dedicated
Sensor
Processor
Memory Controller
DDR PHY
Off-chip interface PHYs
Peripheral IP
Memory System
32 GiB/s (LPDDR4X-4266, 4 × 16-bit channels)
Cellular
Radio
Processor
(real-time)
Core Private L1 Caches:
L1 I cache/D cache 64 KB each for big cores
L1 I cache/D cache 32 KB each for little cores
Core Private L2 Caches:
512 KB each for big cores
128 KB each for little cores
General-Purpose Multi-Core Processors (Cores × 8)
4 big cores: e.g., A76, 2.6 GHz
4 little cores: e.g., A55, 1.8 GHz
Private L1 & L2 caches
Notes: This slide shows a high-level overview of the main IP blocks in a SoC example that is based on the high-level goals and constraints from the previous slide.
General-Purpose Processors
The design has a mixture of high-performance “big” cores and more power-efficient “little” cores. Depending on the nature of the workload, we are able to schedule threads on the most appropriate core in order to minimize power consumption.
The multi-core design also allows us to take advantage of the process or thread-level parallelism.
GPU
A highly specialized processor for providing high-quality graphics, e.g., for 3D games, augmented reality and virtual reality applications. The GPU will also be able to accelerate other data-parallel workloads, e.g., computer vision, machine learning techniques, image processing algorithms, etc.
Machine Learning Accelerator
Modern machine techniques, such as Convolutional Neural Networks, represent a particularly compute-intensive workload that can benefit significantly from hardware acceleration.
Cellular Radio Processor
Cellular communications standards are complex and are often implemented with the aid of programmable processors. The processing requirements are significant and often require multiple processors. In addition, there are many hard real-time requirements that must be met to avoid dropping data and forcing it to be re-transmitted.
Dedicated Sensor Processor
A dedicated processor is employed to process sensor inputs (e.g., GPS, accelerometer, gyroscope, touch, microphone, etc.). The sensor processor may average, filter, and combine (or fuse) sensor inputs. This enables the sensors to be “always-on” without requiring significant amounts of the phone’s battery or processing resources.
System Control Processor (SCP)
Controls clocks and resets.
Is responsible for power state transitions for the power regions in the SoC.
Has direct control over the Power-Management Integrated Circuit (PMIC) on the board.
Video Processor
This is a specialized processor used for encoding and decoding video content. There are many different codecs to support, e.g., VP9, H.264, HEVC/H.265, etc.
Display Processor
Performs operations such as scaling, rotation, composing layers, picture quality enhancements.
Limits GPU workload (reduces power) – an example of where it is beneficial to extract certain functionality from the GPU and implement it as a separate, more specialized processor.
The display processor is also often paired with other IP for backlight management, HDR management, optimizations based on ambient light, etc.

## Slide 7: A Modern Arm System-on-chip (SoC)
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: Here is a more detailed view of our SoC example. Here, we have refined the design and mapped to IP available from Arm. The boxes in green show software libraries and tools for the SoC.

## Slide 8: Heterogeneous Multicore Cluster
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: This cluster of 8-cores are our general-purpose processors.
Here, we have 4 Cortex-A76 cores (the “big” cores) and 4 Cortex-A55 cores (the “LITTLE” cores) that form the Arm big.LITTLE architecture.
The DynamIQ Shared Unit (DSU) contains a shared L3 Cache, the Snoop Control Unit (SCU) to maintain cache coherence, power management circuitry, and interfaces to the rest of the system. The DSU is basically a cluster microarchitecture that integrates one or more cores to form a DynamIQ cluster. Note that the Cortex-A55 and Cortex-A76 must be implemented inside the DSU as the DSU contains the necessary I/Os to interface with the rest of the system.
If we profile a typical day of heavy smartphone use, we find that the majority of the time the CPUs will be in a deep sleep state (perhaps 80% of the time). Even when active, for the majority of the time, the processing requirements may be low with the LITTLE cores active 80-90% of the time and the big cores only 10-20%.
References:
https://www.hotchips.org/wp-content/uploads/hc_archives/hc29/HC29.22-Tuesday-Pub/HC29.22.80-Architectdure-Pub/HC29,22,820-DynamiQ-Greenhaigh-ARM.pdf
Additional reading:
https://community.arm.com/developer/ip-products/processors/b/processors-ip-blog/posts/where-does-big-little-fit-in-the-world-of-dynamiq?_ga=2.182919457.626413000.1569495113-171889455.1539079803
https://developer.arm.com/ip-products/processors/cortex-a/cortex-a76
https://developer.arm.com/ip-products/processors/cortex-a/cortex-a55

## Slide 9: Heterogeneity
There are different levels of heterogeneity within the SoC.
Cores running the same ISA but with different microarchitectures
  E.g., Cortex-A55 and Cortex-A76 in DynamIQ Shared Unit
  Allows general-purpose tasks to migrate to save power or increase performance
Cores extracting different types of parallelism
  E.g., Cortex-A cores vs Mali GPU
  The GPU is specialized to efficiently exploit data-parallel parallelism.
Cores specialized to specific tasks
  E.g., machine-learning processor
  These are highly specialized hardware accelerators designed for a narrow range of workloads.
Key aim: Reduce power consumption but increase performance
Notes: The different types of cores listed here make different trade-offs in terms of flexibility and efficiency. By creating a specialized core, we lose flexibility, but can make significant gains in terms of power efficiency and performance. General-purpose cores are still required in order to run the necessarily very broad range of programs and applications.
In practice, most applications will be partitioned across multiple core types. For example, we might benefit from the ability to run control-flow intensive code on our high-performance general-purpose cores and have the ability to offload data-parallel and machine-learning-related kernels to more specialized cores. Even if our target market was much narrower, programmable cores would most likely still be important and necessary.
One potential pitfall is to only consider algorithms that map well to highly parallel accelerators. While it is often possible to find highly parallel solutions, this may omit less regular solutions that actually perform less work, and hence require less power. It is also useful to remember that general-purpose cores are often augmented with their own powerful data-parallel SIMD extensions.

## Slide 10: Heterogeneity in Microarchitectures
An example is DynamIQ big.LITTLE.
  Next generation big.LITTLE Cortex-A CPUs in one cluster with a shared coherent memory
  Tasks that do not require high performance can migrate to the smaller cores (Cortex-A55).
  Tasks that need computing power run on the larger cores (Cortex-A76).
The key to this form of heterogeneity is ISA-compatibility.
  Both core types must run exactly the same ISA so as to enable migration at any point.
Shared L3 caches and separate voltage/frequency domains within each cluster.
  These improve performance and provide more opportunities for power saving.
Notes: An example is the DynamIQ cluster that has big and LITTLE cores.
Tasks that do not require high performance can migrate to the smaller cores (Cortex-A55). This saves power by running on the (relatively) simple in-order microarchitecture.
Tasks that need computing power run on the larger cores (Cortex-A76), so high performance is available when required.
However, both core types must run exactly the same ISA so as to enable migration at any point.

## Slide 11: Graphics and Display IP
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: Let’s now look at the graphics and display IPs in this SoC example.

## Slide 12: Graphics and Display IP
In the example shown in the previous slide:
Mali-G76 (see module 10)
  This is the SoC’s main GPU. Our SoC has 10 GPU cores providing 240 32-bit execution lanes (with INT8 support).
Mali-V76
  Video processor (video encode and decode)
Mali-D71
  Display processor (scaling, rotation, composing layers, picture quality enhancements)
Assertive Display 5 (AD5 )
  HDR management features
  Ambient light adaptivity and advanced power-saving features
  Gamut management
Notes: This slide details the Graphics and Display IPs that we have used in the SoC example.

## Slide 13: TrustZone
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: We will now learn about Arm TrustZone.

## Slide 14: What Is Security?
Security is a property of the system, which ensures that resources of value cannot be copied, damaged, or made unavailable to genuine users.
There are several fundamental security properties:
Confidentiality
    If an asset is confidential, it cannot be copied or stolen by a defined set of attacks.
Integrity
    If an asset has its integrity assured, it is defended against modification by a defined set of attacks.
Authenticity – may be provided if integrity cannot be
    If an asset is authentic, it is known to have not been modified by an attacker.
    In other words, the defender can detect any modifications made before the asset is used.
Notes: Before introducing what TrustZone is, it is important to understand what we define security as (shown in this current slide).
For more information, please see:
https://developer.arm.com/solutions/security-on-arm
https://developer.arm.com/docs/genc009492/latest/introduction

## Slide 15: TrustZone
TrustZone’s primary security objective:
This is achieved by partitioning all resources into two worlds:
  The secure world for the security subsystem
  The normal world for everything else
No normal world components can access secure world resources.
  This is enforced through hardware logic.
To enable the construction of a programmable environment that allows the confidentiality and integrity of almost any asset to be protected from specific attacks
Notes: TrustZone is an Arm technology that provides system-wide hardware isolation for trusted software.
TrustZone is not a one-size-fits-all approach to security, but an infrastructure to enable compliant components to work within to ensure security.
See https://developer.arm.com/ip-products/security-ip/trustzone

## Slide 16: Hardware Requirements
Reducing hardware overheads
Use two cores to implement two worlds.
    I.e., a dedicated core for the Secure world
    Costly in silicon area and power
TrustZone provides architectural extensions to allow one core to execute code from the normal and secure worlds.
“Secure Monitor Mode” acts as a gatekeeper for moving between worlds.
Secure Monitor
Notes: The most obvious way of implementing these two worlds (Normal world and Secure world) is through two cores, e.g., a dedicated core for the Secure world. However, this is costly in silicon area and power
TrustZone provides architectural extensions to allow one core to execute code from the Normal and Secure worlds. The “Secure Monitor Mode” acts as a gatekeeper for moving between worlds.

## Slide 17: TrustZone Processor Architecture
A core executes code from both Secure and Normal (Non-Secure) worlds by presenting two virtual processors to the outside world:
    The non-secure virtual processor can only access Non-Secure resources.
    The secure virtual processor can see all resources.
Virtual processors share the core through time slicing (see Module 9).
    They context switch through a dedicated core mode that performs the switch.
    One example is the Secure Monitor Call (SMC) instruction.
The secure monitor ensures all secure world state is inaccessible when switching to normal mode.
Notes: Additional reading:
TrustZone technology for Armv8-M architecture https://static.docs.arm.com/100690/0200/armv8m_trustzone_technology_100690_0200.pdf?_ga=2.172876068.626413000.1569495113-171889455.1539079803
https://www.arm.com/why-arm/technologies/trustzone-for-cortex-a
https://community.arm.com/developer/ip-products/processors/trustzone-for-armv8-m/f/trustzone-armv8-m-forum/10019/trustzone-of-the-cortex-m-vs-trustzone-of-the-cortex-a

## Slide 18: Memory Partitioning
Physical memory map is also partitioned into two worlds, i.e., Secure and Non-Secure regions.
  Virtual addresses in Non-Secure state can only map to Non-Secure physical addresses.
  Virtual addresses in Secure state can map to either Secure or Non-Secure physical addresses.
Memory transactions have a security attribute to indicate Secure or Non-Secure access.
Secure
0xFF_FFFF_FFFF_FFFF
0x00_0000_0000_0000
Non-secure
0xFF_FFFF_FFFF_FFFF
0x00_0000_0000_0000
0xFF_FFFF_FFFF_FFFF
0x00_0000_0000_0000
Architectural view on the physical address space
One physical address space for each world
Common implementation
Data are interleaved throughout memory
Notes: If TrustZone is implemented, the memory is also partitioned into Secure and Normal (Non-Secure) memory regions. Virtual Addresses in Non-Secure state can only map to Non-Secure Physical Addresses. On the other hand, Virtual Addresses in Secure state can map either to Secure or Non-Secure Physical Addresses.
Each memory transaction must indicate the security state of the address it is trying to access. Note that in this implementation, caches carry information about which physical address space was accessed, NOT which Virtual Address (VA) space.
The TLB entry has an additional bit to identify which “world” the data belong to.

## Slide 19: Generic Interrupt Controller
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: We will now look at the Generic Interrupt Controller in this SoC example.

## Slide 20: Generic Interrupt Controller
Performs interrupt management, prioritization, and routing
Boosts processor efficiency and interrupt virtualization
Arm GIC architecture
A fully coherent GPU simplifies software development and improves performance.
  Removing the need for software-managed cache maintenance
CoreLink CCI-600 Generic Interrupt Controller
  Supports DynamIQ cores
  Fully backward compatible with Arm v8.0 cores
Notes: What is the function of a GIC?
The GIC performs critical tasks of interrupt management, prioritization, and routing. GICs are extremely beneficial in boosting processor efficiency and supporting interrupt virtualization (e.g., interrupts in Virtual Machines). Interrupt virtualization will not be covered in this course. For more information on it, please read the Arm White Paper on Enterprise Virtualization, see https://developer.arm.com/ip-products/system-ip/system-ip/free-system-ip-whitepapers/enterprise-virtualization-whitepaper
The Arm GICs are usually implemented as a separate block of IP that is based on an Arm GIC architecture. There are different versions of the Arm GIC architecture (v1 is the earliest and GICv3/4 is the latest).
The SoC example shown in the previous slide uses an Arm CoreLink GIC-600 Generic Interrupt Controller.
The CoreLink GIC-600 is designed to support the DynamIQ cores, such as Cortex-A76 and Cortex-A55, while also being fully backward compatible with other Armv8.0 cores.
Arm provides several types of GICs, with the simplest being GIC-400 for systems with small CPU cores, and GIC-600 for higher performing cores.
References:
https://developer.arm.com/ip-products/system-ip/system-controllers/interrupt-controllers
https://static.docs.arm.com/ihi0069/d/IHI0069D_gic_architecture_specification.pdf?_ga=2.157174715.1822511761.1571662550-171889455.1539079803&_gac=1.148265285.1569863214.Cj0KCQjwz8bsBRC6ARIsAEyNnvoz2q5hVSPP1ljRrjvxw07z3lvU6IPfC3oRwZKQbIQkBEf8l21WI9UaAtrREALw_wcB
https://community.arm.com/developer/ip-products/system/f/embedded-forum/10379/gic-virtualization----gich_elrsr-and-hardware-interrupts

## Slide 21: Interconnect
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: We will now look at the interconnect in this SoC example.

## Slide 22: Cache Coherent Interconnect
CoreLink CCI-550 Cache Coherent Interconnect
Provides cache coherence between CPU clusters and the GPU, network interfaces, and the machine learning accelerator
A fully coherent GPU simplifies software development and improves performance.
  Removing the need for software-managed cache maintenance
Notes: The SoC example shown in the previous slide uses an Arm CoreLink CCI-550 interconnect. It is based on the Arm AMBA 4 ACE protocol. AMBA is an open-standard interconnect specification for communication between different IP blocks in a SoC.
The CoreLink CCI-550 interconnect provides a cache coherent interconnect between CPU clusters and other IP blocks in the SoC.
The interconnect itself is implemented as a number of different crossbars and control logic. It also contains a “snoop filter.” This keeps a record of addresses stored in the caches of the attached cores (or “ACE manager”). The snoop filter is often able to resolve coherence requests without the need to broadcast to all ACE interfaces. This mechanism helps to reduce both system power and latency.
The IP also contains a debug and performance monitoring interface, testing interfaces, and clock and power control interfaces.
References:
Corelink CCI 550 Cache Coherence Interconnect Technical Reference Manual
https://static.docs.arm.com/100282/0001/corelink_cci550_cache_coherent_interconnect_technical_reference_manual_100282_0001_01_en.pdf

## Slide 23: Interconnect
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: The Arm CoreLink Network Interconnect (NIC-450) offers highly configurable topology with Network on Chip (NoC)-like properties that enable you to build high performance, optimized, AMBA-compliant SoC connectivity.
CoreLink Network Interconnect is configurable across a wide range of applications from a single bridge component, e.g., an AHB to AXI protocol bridge, to a complex infrastructure that consists of up to 128 requesters and 64 completers in a combination of different AMBA protocols.

## Slide 24: Debug and Trace
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: We shall now look at the debug and trace IPs in the SoC example.
Why is debug and trace necessary in most SoC designs? This feature is not only needed for software development and troubleshooting, but it is also extremely useful for collection of diagnostic data in the system when required.
This SoC example uses a CoreSight SoC-600 and ELA-500.
https://developer.arm.com/ip-products/system-ip/coresight-debug-and-trace/coresight-technical-introduction?_ga=2.212414099.626413000.1569495113-171889455.1539079803

## Slide 25: Debug and Trace
Traditional debug (CoreSight SoC-600)
  Invasive debug where the processor is halted using breakpoints or watchpoints
  A debug connection is used to examine and modify registers and memory.
  It is possible to “single step” execution.
Trace (CoreSight SoC-600)
  Non-invasive debug with the processor running at full speed
  Delivers the trace off-chip in real-time or stores it in on-chip memory
  Traces are usually carefully compressed to make the best use of limited off-chip bandwidth (or on-chip memory).
  Various components can create traces.
Notes: The Arm CoreSight SoC-600 is a debug and trace IP that includes debug access, trace routing and termination, cross-triggering and time stamping.
For more information, see:
https://developer.arm.com/ip-products/system-ip/coresight-debug-and-trace/coresight-components/coresight-soc-600
https://developer.arm.com/ip-products/system-ip/coresight-debug-and-trace/coresight-components/coresight-ela-500-embedded-logic-analyser
https://community.arm.com/developer/ip-products/processors/b/processors-ip-blog/posts/how-to-debug-coresight-basics-part-1

## Slide 26: Debug and Trace
Embedded Logic Analyzer (CoreSight ELA-500)
  These IP blocks allow many (over 1500) internal logic signals to be monitored.
  Complex “triggers” can be constructed to start capturing signals.
  Signals are stored in on-chip SRAM for later analysis.
Notes: The CoreSight ELA-500 Embedded Logic Analyzer provides low-level signal visibility into the IPs – it provides visibility of load, stores, fetches, cache activity, none of which are available through instruction tracing. The embedded logic analyzer provides extra assistance with post-deployment debug by monitoring low-level signals.
Debug signals are connected from the IP being debugged to the ELA-500, which compares the signals with a target value and drives actions (as shown in image). There is an optional trace capability that can be used to generate a history of the debug signals at any point in time. Trigger conditions can be programmed over standard debug interfaces either directly by an on-chip processor or an external debugger.
Additional information:
https://developer.arm.com/ip-products/system-ip/coresight-debug-and-trace/coresight-components/coresight-ela-500-embedded-logic-analyzer
https://community.arm.com/developer/tools-software/tools/b/tools-software-ides-blog/posts/using-the-coresight-ela-500-embedded-logic-analyzer-with-arm-ds-5#targetText=Introduction,IP%20and%203rd%20party%20IP.&targetText=As%20well%20as%20accelerating%20debug,assistance%20for%20post%20deployment%20debug.

## Slide 27: Specialization
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: Having highly specialized hardware accelerators designed for specific tasks to boost performance is not uncommon in a SoC design nowadays. We shall now look at one example, which is the Machine Learning processor in our SoC example.

## Slide 28: Specialization – A Machine Learning Processor
A Machine Learning (ML) processor’s architecture is different to general-purpose cores.
  Different instructions
  Different programming model
  Different pipeline structure
  Different methods of communication
The ML processor executes convolutional neural-network inference efficiently.
  Design and execution tailored to the specifics of the algorithm
Notes: Machine learning processors specialize for neural-network inference and have massive efficiency uplift from CPUs, GPUs, and DSPs.
Neural networks have many applications within a smartphone or tablet, e.g., for improving the quality of photographs by first recognizing the type of scene that is about to be photographed or by post-processing images. Apps are also increasingly making use of neural networks for various forms of image classification and object recognition, face detection and solving the computer vision problems associated with augmented reality, etc.

## Slide 29: Specialization – A Machine Learning Processor
Specialized for neural-network inference
Example of Arm ML processor with 16 compute engines
  8-bit quantized integer support
  No caches
Convolutional neural networks statically mapped onto the compute engines
  Output feature maps interleaved across engines
  Weights held in that engine’s SRAM
  Input feature maps interleaved across all SRAMs
Notes: The diagram in this slide shows a block diagram of an Arm Machine Learning Processor, which has 16 compute engines. For more information, see https://www.hotchips.org/hc30/2conf/2.07_ARM_ML_Processor_HC30_ARM_2018_08_17.pdf
Reference:
https://developer.arm.com/ip-products/processors/machine-learning/arm-ml-processor

## Slide 30: Specialization
Specialization and heterogeneity are interlinked.
  We can think of the Cortex-A55s as being “specialized” for low-power computation.
Often with specialization, we think of larger changes than just the microarchitecture.
  Such as with the machine-learning processor
Other forms of specialized accelerator exist within the SoC.
  A cryptographic processor (CryptoCell-712) for secure boot, cryptographic functions, etc.
  A video processor (Mali-V76) for decoding videos
  A display processor (Mali-D71) for driving displays and offloading some imaging tasks from the GPU
Notes: There are other forms of “specialization” and they are interlinked with heterogeneity. For example, Cortex-A55 is “specialized” for low-power computation. Other types of specialized accelerators include crypto processor, video processor, and display processor.
What is a feature map?
In a convolutional neural network, we take the input data (or output from the previous layer) and using a convolution filter produce a feature map.

## Slide 31: DRAM Interface
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: We will now look at the memory controller in the SoC example.

## Slide 32: Memory Controller (DMC-500)
What does a memory controller have to do?
  Convert system memory requests to the necessary series of commands to access the correct rank, bank, row and column in an external SDRAM
  Buffer and reorder requests to optimize performance and meet QoS goals
  Error checking and handling
  Refresh control logic for SDRAM
What is it connected to? In our SoC example:
  Each memory controller (Arm DMC-500) supports dual AXI4 (128-bit) system interfaces.
  Connects to the actual DRAM PHY using a standard interface (called DFI).
Notes: In general, a memory controller manages the flow of data from the memory to the system. It reads, writes, and refreshes the SDRAM.
References:
https://developer.arm.com/ip-products/system-ip/memory-controllers/corelink-dmc-500

## Slide 33: Real-time Processing
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: You will notice that in our SoC example here, there is a Cellular Radio processor as shown in the orange box. In this example, the Cortex-R8 is used as a Cellular Radio processor.

## Slide 34: Real-time Processing
The software requirements for the latest cellular communications standards are complex.
  E.g., LTE Advanced Pro and 5G
Requires real-time multi-core processor
  In our SoC example, a quad-core coherent cluster of Cortex-R8 cores is used.
Low-latency and hard real-time requirements
  Large Tightly Coupled Memories (TCMs) in addition to traditional instruction/data caches
  Simple Memory Protection Unit (MPU) rather than virtual memory to reduce memory latency
  Extra interface ports to tightly couple the rest of the latency-sensitive modem system with cores
Reliability
  Improved error detection, correction, and containment schemes
Notes: The increasing complexity of today’s cellular communication standards requires the use of efficient real-time processors.
Hard real-time means that the processor can switch to handle a new critical event very rapidly, and with a known (deterministic) worst case delay. This worst case delay is typically just a few nanoseconds and enables interrupts from other parts of the system to be detected and acted upon very quickly. Layer 1 control tasks in LTE-Advanced Pro and 5G modems will handle multiple carriers and very high data rates. A processor must therefore run at a relatively high clock frequency and be able to very rapidly switch between tasks and handle incoming events. Unlicensed carriers, such as WiFi, provide much higher data and packet rates than LTE, and combining and controlling these diverse carriers requires a specialized processor. The Cortex-R8 with an eleven-stage pipeline can be clocked very rapidly to deliver the performance needed. The pipeline is “out-of-order,” which means that processing can continue even when some instructions are waiting for data from the slower external memory systems – this greatly reduces pipeline “stalls” and delivers the best possible performance.
(from “The Route to 5G,” Arm White Paper*)
Caches suffer from non-deterministic access latencies
Deterministic and low-latency memory accesses are important (e.g., for interrupts)
References:
https://community.arm.com/developer/ip-products/processors/b/processors-ip-blog/posts/arm-cortex-r8-paves-way-to-lte-advanced-pro-and-5g
https://developer.arm.com/ip-products/processors/cortex-r/cortex-r8
* https://community.arm.com/developer/ip-products/processors/b/processors-ip-blog/posts/the-route-to-5g---arm-whitepaper

## Slide 35
Other SoC Design Considerations
Notes: In the previous slides, we have looked at some of the major IP blocks in our SoC example. We will now briefly go through some technological features that would be good to consider when choosing an IP for a SoC design.

## Slide 36: SoC Considerations
Power domains
Virtualization
Reliability, Availability, and Serviceability (RAS)
Safety using Dual-Core Lock Step
Notes: The SoC considerations that we will cover in this module are shown in this slide.

## Slide 37: Power Domains
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: First of all, we will look at power domain features, specifically in the DynamIQ cluster in this SoC example.

## Slide 38: Power Domains
Providing power to all components of a system-on-chip is challenging.
  A SoC will implement multiple different domains to create independence between components.
  This enables power gating when a component is unused.
There will usually be a system-wide power controller.
  This can be programmed (through the kernel) to implement a specific power policy.
Notes: First of all, what are power domains and why are they needed?
In some SoCs, some level of power management (usually by a power controller) is crucial - it is challenging to supply power to all IPs and yet achieve the same power and performance trade-off. Therefore, power-gating is often used, which is a technique to reduce power consumption (static power leakage) when a component is not used – essentially “gate the power” to the unused component.
To facilitate effective power management, blocks of the circuit can be grouped together to have its own power mode independently of other parts of the circuit (and thus its own “power domain”). So, e.g., the circuit blocks in one power domain could be gated, while the rest of the circuit in the other power domain is fully operating. Or instead of completely gated, it could be in a retention mode, while the rest of the circuit is in fully operational mode.

## Slide 39: Power Domains
Within a DynamIQ cluster alone, there are multiple domains.
  Each core has its own power domain.
  Blocks with same color are in the same power domain.
Notes: The diagram in this slide shows the DSU clock domain, voltage domain, and power domains. Blocks in the DynamIQ cluster that are in the same power domain have the same color. Note that each core can be implemented in one, or more, separate power domains.
http://arminfo.emea.arm.com/help/topic/com.arm.doc.100453_0400_02_en/dsu_trm_100453_0400_02_en.pdf
http://arminfo.emea.arm.com/help/topic/com.arm.doc.100798_0400_00_en/cortex_a76_trm_100798_0400_00_en.pdf

## Slide 40: Virtualization
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: Depending on the purpose and capabilities of your SoC, you might want your application-specific processor to support virtualization.

## Slide 41: Virtualization
Virtualization is the ability to create virtual machines that act like real machines.
  A virtual machine is a software program that mimics a real system called the guest.
    Being a software program, it actually runs on a real machine called the host.
  To the user, it is (almost) indistinguishable from a real system.
    Difficult, if not impossible, to know that they are running on a virtual machine and not real hardware
A virtual machine contains all the functionality of the real system.
  E.g., both user and privileged ISAs
  Peripherals and other devices
  The ability to run an operating system (the guest)
The hypervisor provides a virtual system to each of the Guest OS and monitors their execution.
Notes: What is virtualization is basically the ability to create “virtual machines” that act like real machines. These virtual machines function like the real machine itself in terms of ISA, peripherals, and other devices, as well as the ability to host an OS (guest OS). A hypervisor manages the Guest OS’s and monitors their execution.
Why virtualization?
For server applications, virtualization is a well-established “must-have” with many use cases such as resource management, sand boxing, disaster recovery, and availability management.
For the automotive industry, virtualization provides isolation, whereby buggy or malicious application running on the open OS will not interfere with the “closed OS” that handles vehicle management apps.
For business applications, virtualization allows businesses to maintain control of enterprise data. It also allows users to choose device, have the OS and apps they want, and configure it the way they want.

## Slide 42: Virtualization
Notes: This diagram shows a comparison of a system without virtualization versus a system with virtualization.
Some of the functions of a hypervisor include memory management, device emulation, device assignment, exception handling, interrupt handling, scheduling, and context switching. For more information, see Hypervisor software topic in https://developer.arm.com/docs/den0013/latest/cortex-a-series-programmers-guide-version-40

## Slide 43: Virtualization
Hardware support can increase the efficiency of virtualization.
  Reducing the costs of switching between virtual machines
E.g., page-table translation for guest OS applications
  Processor supports a second stage of page-table translation.
CPU
Memory
Virtual address
Frame number
Page number
Offset
Physical address
.
.
.
Page table
Frame number
Offset
Physical address
.
.
.
Page table
Stage 1
Stage 2
Notes: Page-table translations can become complicated in the presence of virtualization. The next slide has more details – this one shows how this relates to the page-table translations performed in module 6. Essentially, the first stage of translation gets the physical address for the virtual machine, and the second accelerates the translation to the physical address where the guest OS application actually resides.
More details are available in the Arm whitepaper: https://www.arm.com/files/pdf/System-MMU-Whitepaper-v8.0.pdf

## Slide 44: Virtualization
In virtualization, memory management requires additional translation.
  The hypervisor has its own translation table.
  Additional translation stage using Intermediate Physical Address (IPA)
OS VA PA
Hardware
Translation table
Hypervisor IPA PA
Hardware
OS VA IPA
OS VA IPA
OS VA IPA
OS VA IPA
VA PA
Traditional system
Virtualized system with multiple OS’s
Stage-1 translation
Stage-2 translation
Legend:
Notes: If only one OS is running, the Virtual Address (VA) to Physical Address (PA) translation is as expected (covered in the previous module).
However, in a virtualized system with multiple OS’s managed by the hypervisor, how is the translation like? As shown in the diagram in this slide, first of all, the hypervisor itself would still need its own VA to PA translation. The OS will also need a VA to PA translation. But since each OS has its own translation table (that is independent from other OS’s), multiple OS’s might translate to the same PA.
To work around this “overlapping PA” scenario, an Intermediate Physical Address (IPA) is used. Each guest OS would translate the VA to an IPA, which is known as a Stage-1 translation. The hypervisor then translates the IPA to PA, which is known as the Stage-2 translation. Essentially, the hypervisor sorts out the overlapping PA issue so that each OS can access different PAs. Note that the Stage-2 translation is done with the use of additional tables that are under the control of the hypervisor and is invisible to the OS.
For more information, see http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.den0024b/index.html

## Slide 45: Safety - Dual Core Lock Step
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: In some applications, safety is absolutely crucial, and you may want to have an application processor that supports a Dual Core Lock Step mechanism.
Note: In this SoC example, the Cortex-A76 and DSU do not support Dual Core Lock Step. However, the Cortex-A76AE supports Dual Core Lock Step, and it must be used with the DSU-AE version.

## Slide 46: Dual Core Lock Step (DCLS)
DCLS is an industry-standard technique that runs the program twice on different hardware.
  Results compared at each cycle
  Introduces spatial and temporal redundancy into the system
Core 0
Core 1
Application and data
Checker
Correct?
Notes: DCLS is where you have two similar cores run the exact same program, and the results are compared with each other. If there is a mismatch, then the comparator/checker generates a fault that has to be addressed. This is particularly useful especially for applications where safety is a crucial concern, such as automotive.
Modern Arm cores (such as the Arm Cortex-A76AE) have a “Split-Lock” capability allowing the cores to run in lock step (“lock mode”) or configured as two independent cores (“split mode”).
References:
https://www.arm.com/why-arm/technologies/safety

## Slide 47
Backup Slides

## Slide 48: Heterogeneity in Microarchitectures
Cortex-A76
4-way superscalar, out-of-order processor
  8-wide issue
13-stage pipeline
Multilevel branch-target cache
  Branch unit has 2× fetch-unit bandwidth
128-entry instruction window
Two load/store pipelines access 64 KB L1D
  Optimized for memory-level parallelism
Cortex-A55
2-wide in-order superscalar
8-stage pipeline
  Sweet spot between power/area and frequency
Neural network-based branch predictor
  256-entry Branch Target Address Cache (BTAC)
Configurable L1D cache size
  Fully exclusive of L2
Independent load & store AGUs
  Address generation units
Notes: This slide gives a quick overview of the features of Cortex-A76 and Cortex-A55
Additional reading:
https://www.anandtech.com/show/11441/dynamiq-and-arms-new-cpus-cortex-a75-a55/4
https://www.anandtech.com/show/13614/arm-delivers-on-cortex-a76-promises
https://www.anandtech.com/show/12785/arm-cortex-a76-cpu-unveiled-7nm-powerhouse

## Slide 49: Reliability, Availability, and Serviceability (RAS)
DynamIQ Shared Unit
Memory System Integrated TrustZone
Cortex-A76
Mali-G76
CoreLink CCI-550
CoreLink GIC-600
I/O Coherent Requesters
NIC-450
NIC-450
MMU-600
Mali-D71
CoreSight SoC-600
LPDDR4x
ELA-500
Cortex-A55
DMC-500
SCP
Cortex-M3
CoreLink NIC-450
Peripherals
ELA-500
DMC-500
CryptoCell-712
Sensor Fusion
Cortex-Mx
Cellular Radio
Cortex-R8
AD5
LPDDR4x
MMU-600
Mali-V76
Machine Learning processor
Notes: Depending on the purpose and capabilities of your SoC, you might want your application-specific processor to have Reliability, Availability, and Serviceability (RAS).

## Slide 50: Reliability, Availability, and Serviceability (RAS)
What is RAS?
  Reliability – Continuity of correct service
  Availability – Readiness for correct service
  Serviceability – Ability to undergo modifications and repairs
Protects data integrity, makes systems more fault-tolerant
  Transient errors can be detected and corrected before they cause application or system failure.
  Failing components can be identified and replaced.
  Failure can be predicted ahead of time to allow replacement during planned maintenance.
Notes: What is RAS? RAS stands for Reliability, Availability, and Serviceability.
Reliability in the sense that there is continuity of correct service by your processor.
Availability in the sense that your processor is ready to operate the correct service.
Serviceability in the sense that your processor has the ability to undergo modifications and repairs.
RAS is important in most systems nowadays because it protects data integrity and helps make your system more fault-tolerant

## Slide 51: Why RAS?
Technology scaling provides smaller transistors - but also less reliable.
Multiple points in a processor’s life cycle where hard and soft errors can creep in
  During manufacture (process variation) or transistor aging
  As an effect of power fluctuations (voltage droops)
  Through particle strikes (e.g., caused by cosmic rays, gamma radiation)
These errors can cause the processor to perform calculations incorrectly.
  Either because a circuit has been corrupted (hard error)
  Or bits in the values used have been flipped (soft error)
Memory systems are most vulnerable.
  Especially DRAM, which contains small transistors, easily flipped
  But also caches, due to having a lot of memory cells close together, increasing the probability of a particle hit

## Slide 52: RAS Techniques
Terminology
  An error is any deviation of the correct behavior.
  A fault leads to an error – example of fault: manufacturing problem.
Techniques for Reliability
  Avoid error, correct the error, contain the scope of the error
Techniques for Availability
  Fault handling
  Minimize scope of failure
Techniques for Serviceability
  Fault and error reporting
Notes: Arm RAS terminology-wise, what is the difference between fault and error?
A fault leads to an error. The fault could be a manufacturing problem, e.g. On the other hand, an error is any deviation from the correct behavior.
This slide lists some of the techniques that are used for RAS.
Additional info:
Standard techniques are available to detect and correct errors here. The most common technique is adding Error-Correcting Codes (ECC) into DRAM and caches. Single Error Correction, Double Error Detection (SECDED) is also popular. This can be achieved using 8 extra bits per 64-bit value.
However, certain domains mandate higher reliability guarantees from the cores too. Safety-critical systems must meet stringent reliability requirements to get certified, e.g., Automotive Safety Integrity Levels (highest is ASIL-D)

## Slide 53: RAS in Armv8-A Profile
Arm introduced RAS specification for the Armv8-A profile.
Includes:
  Error recording in specific RAS registers.
  Supports fault injection for the purpose of testing fault handling software by programming some Error Record and Control registers.
  Optional cache protection with SED, interleaved parity, and SECDED capabilities.
  Error recovery and fault handling interrupt outputs.
  Error Synchronization Barrier instruction (ESB), which allows efficient isolation of errors
Notes: The RAS specification was introduced for Armv8-A. For more information on RAS specification for Armv8-A, see
https://static.docs.arm.com/ddi0587/b/ARM_DDI_0587B_RAS.pdf
This slide also lists some of the RAS features included in Armv8-A.
SED: Single Error Detect.
Interleaved parity: One bit of parity is applicable to the even bits of the word, and one bit of parity is applicable to the odd bits of the word.
SECDED: Single Error Correct, Double Error Detect.
RAS in Cortex-A76: http://arminfo.emea.arm.com/help/topic/com.arm.doc.100798_0400_00_en/cortex_a76_trm_100798_0400_00_en.pdf

## Slide 54
Other SoC Examples
Notes: Other SoC examples from different companies are shown here.

## Slide 55: Further Examples: Wireless IoT Soc
Nordic Semi nRF52832
Bluetooth 5 Low Energy SoC for smart home, sensor networks, wristwatches, remote control applications, etc.
Multiprotocol 2.4 GHz Radio
NFC-A Near Field Communication
64 MHz ARM Cortex-M4F
  With floating point (“F)” and DSP instructions
  3-stage pipeline with branch speculation
  Various sleep modes
Cost $2.50 or less at volume
512 KB
Flash with cache
64 KB
SRAM
GPIO
AHB Lite bus
APB bus
Processor
64 MHz ARM
Cortex-M4F CPU
Radio
Multi-protocol
2.4 GHz
NFC-A
tag
Oscillators
Power
supply
Timers/Counters
Analog I/O
Digital I/O
System Peripherals

## Slide 56: Further Examples: Wireless IoT Soc
Nordic Semi nRF52832
32 pin GPIO
12-bit/200 kSPS ADC
SPI/2-wire/I2S/UART/PDM/QDEC
128-bit AES ECB/CCM/AAR co-processor
On-chip DC/DC buck converter
Ultra-low standby current (0.3-1.6 µA @3 V), up to 15.2 mA when transmitting
3 mm × 3.2 mm WLCSP50 package (or 6 mm × 6 mm QFN48)
512 KB
Flash with cache
64 KB
SRAM
GPIO
AHB Lite bus
APB bus
Processor
64 MHz ARM
Cortex-M4F CPU
Radio
Multi-protocol
2.4 GHz
NFC-A
tag
Oscillators
Power
supply
Timers/Counters
Analog I/O
Digital I/O
System Peripherals
Notes: kSPS: kilo samples per second

## Slide 57: Further Examples: Intel Movidius Myriad X
Vision Processing Unit (VPU)
Intelligent machine vision, e.g., robotics, augmented and virtual reality, wearables, and smart city applications
>4 TOPS
Low-power <1 W
package 8.1 mm × 8.8 mm
Process: TSMC’s 16 nm FinFET
16 SHAVE vector processors
2.5 MB SRAM
Vision Accelerators
Neural Compute
Engine
(up to 1 TOPS)
Imaging
Accelerators
Processors
(2 × LEON4
SPARC V8 ISA)
USB 3.1
Quad SPI
I2S, 2× SD
10 GbE
PCIe 3.0
16 × MIPI lanes
Memory Controller
DDR PHY
LPDDR4, 32-bit@1600 MHz (12 GiB/s)

## Slide 58: Further Examples: Intel Movidius Myriad X
20+ fixed-function imaging and vision accelerators, 4K video HW encoder, neural compute engine (DNN accelerator)
SHAVE vector processors
VLIW-style processor with 128-bit vector operations. Each processor can perform multiple scalar and vector operations in parallel.
16 SHAVE vector processors
2.5 MB SRAM
Vision Accelerators
Neural Compute
Engine
(up to 1 TOPS)
Imaging
Accelerators
Processors
(2 × LEON4
SPARC V8 ISA)
USB 3.1
Quad SPI
I2S, 2× SD
10 GbE
PCIe 3.0
16 × MIPI lanes
Memory Controller
DDR PHY
LPDDR4, 32-bit@1600 MHz (12 GiB/s)
Notes: GbE: Gigabit Ethernet
https://en.wikichip.org/wiki/movidius/microarchitectures/shave_v2.0
https://arxiv.org/pdf/1810.04150