## Slide 1: Timer, GPIO and 7-Segment Peripherals
Intro to System-on-Chip Design course

## Slide 2: Learning Objectives
At the end of this lecture, you should be able to:
Describe the function of a timer and compare the functionality of a hardware and software timer.
Explain the function of each component in the standard architecture of hardware timers.
Explain the three modes of operation of the standard timer including ‘compare mode’, capture mode’ and pulse width modulation mode.
Outline the components of the AHB Timer peripheral and describe their functions.
Outline the components of the AHB GPIO peripheral and describe their functions.
Outline the components of the AHB 7-Segment display peripheral and describe their functions.

## Slide 3: Module Syllabus
General Architecture and Operation Modes of a Timer Peripheral
Design and Implementation of
  AHB Timer Peripheral
  AHB GPIO Peripheral
  AHB 7-Segment Display Peripheral

## Slide 4: Building a System on a Chip (SoC)
Memory
VGA
Peripheral
UART
Peripheral
Timer
Peripheral
GPIO
Peripheral
7-Segment
Peripheral
Arm CMSIS-Core
Application Programming Interface (API)
Application Design (e.g., Game)
Arm Cortex-M0
Processor
Hardware design
Software low-level drivers & libraries programming
Software high-level
application development
Peripheral Drivers
AHB
Notes: This module explores how to connect the three remaining peripherals to our SoC in order to enhance its functionality. The first is a timer peripheral used to generate interrupt signals; the second, a general purpose input/output peripheral; and the third is a 7-segment display unit.

## Slide 5: Timer Overview
A hardware timer is basically a digital counter that:
  Counts regular events, which normally refers to a clock source that has a relatively high and fixed frequency
  Increments or decrements at a fixed frequency
  Resets itself on reaching zero or a predefined value
  Generates an interrupt when reset
In contrast, a software timer is a similar function block but implemented in software. Software timers usually:
  Are based on hardware timers
  Increase or decrease when interrupted by a hardware timer
  Offer a lower level of time precision compared with hardware timers
  Can have multiple instances that are more than the actual hardware timers
Notes: One of the common requirements of a processor is to be able to turn on an output (such as an LED or relay) for a period of time. This functionality can be implemented in software (i.e., software timer) by turning on the device and then turning it off again, causing the microcontroller to decrement a specified number to zero. To avoid wasting processor time on this task (i.e., decrementing numbers), hardware timers can be used. This allows the processor to perform other tasks during the on time period. Hardware timers also offer higher levels of time precision, compared to software timers. A hardware timer is typically implemented as a digital counter, which uses the period system clock as the basic time unit. It can usually be reset when it reaches a predefined value and generate an interrupt signal. We will now look at the standard architecture of a hardware timer.

## Slide 6: Standard Architecture of Hardware Timers
A prescaler
  Takes the clock source as its input
  Divides the input frequency by a predefined value, e.g., 4, 8, 16
  Outputs the divided frequency to the other components
Timer Register
Compare Register
Prescaler
Comparator
Interrupt Event
Clock Source
Capture Register
Interrupt Event

## Slide 7: Standard Architecture of Hardware Timers
A timer register
  Increases or decreases at a fixed frequency
  Driven by the output from the prescaler; often referred to as ticks
Timer Register
Compare Register
Prescaler
Comparator
Interrupt Event
Clock Source
Capture Register
Interrupt Event
Notes: The timer register is a digital counter that can be incremented or decremented at a fixed rate that is specified by the frequency of the prescaler output signal.

## Slide 8: Standard Architecture of Hardware Timers
Compare register
  Is preloaded with a desired value, which is periodically compared with the value in the timer register
  If the two values are the same, an interrupt can be generated.
Timer Register
Compare Register
Prescaler
Comparator
Interrupt Event
Clock Source
Capture Register
Interrupt Event

## Slide 9: Standard Architecture of Hardware Timers
Capture register
  Loads the current value from the timer register upon the occurrence of certain events
  Can also generate an interrupt upon the occurrence of certain events
Timer Register
Compare Register
Prescaler
Comparator
Interrupt Event
Clock Source
Capture Register
Interrupt Event
Notes: The capture register is used to take a snapshot of the contents of the timer register at certain moments.

## Slide 10: Timer Operation Modes
Compare mode
Preload the compare register with a desired value
Increment or decrement the timer register
Compare the values of
the timer registers
Once the timer and compare register have equal values,
generate an interrupt signal
Reset the timer register
Timer Register
Compare Register
Prescaler
Comparator
Interrupt Event
Clock Source
Notes: A standard timer typically has three modes of operation: Compare Mode, Capture Mode, and PWM Mode. Here is an example of the operation of the timer in compare mode. First, the Compare Register is preloaded with a desired value; then, the Timer Register is incremented or decremented automatically at a rate defined by the signal frequency at the output of the prescaler. The values in the Compare Register and the Timer Register are automatically compared. Once equal, an interrupt can be generated and the timer register should be reset.

## Slide 11: Timer Operation Modes
Capture mode
The event source generates a sequence of pulses
Once an event occurs, the capture register will be enabled
The capture register then takes a “Snapshot” of the timer
An interrupt is sometimes generated
Timer Register
Capture Register
Prescaler
Interrupt Event
Event Source
Capture Enable

## Slide 12: Timer Operation Mode
Pulse-width modulation (PWM) mode
  PWD uses the width of the pulse to modulate an amplitude.
  Mainly used for power supplied electrical devices
  Pulse frequency ranges from a few kHz (e.g., motor drive) to hundreds of kHz (e.g., audio amplifier, computer power supplies).
Voltage
Time
Logic 1
Logic 0
Power Amplitude
Notes: The third operation mode is pulse-width modulation (PWM) mode. A PWM circuit modulates the amplitude of its output signal based on the width of the pulses at its input. The timer can generate pulses with varying widths in order to drive a PWM circuit. The diagram here shows the output signal (in red) of a PWM circuit driven by varying width pulses. It can be noted that the output voltage is proportional to the width of the input signal. When the timer is operated in this mode, its output frequency ranges from a few kHz to hundreds of kHz, depending on the applications. For example, to drive an audio amplifier, we need a few KHz signal.

## Slide 13: Timer Operation Modes
Example of PWM mode: To generate a PWM with 50% duty cycle
Preload the compare register with a 50
Increment of the timer register
Compare the values of
the timer registers
Once the values of the timer register exceed that of the compare register, the comparator output will be set to high
Reset the timer register when it reaches 100
The comparator output will be reset to a logic zero
Timer Register
Compare Register
Prescaler
Comparator
Interrupt Event
Clock Source
Load with duty cycle
Value, e.g., 50
Load reset value
e.g., 100
Notes: Let us now look at how we can use the time to generate a specific pulse width. Before we start, it is worth noting that pulses with variable widths have different duty cycles. The latter describes the proportion of the “1” state in one pulse period variable in each clock cycle.
The first thing we do is preload the compare register with a value (in this case, 50); then we increment the timer register while continuously comparing the values of compare with the timer registers. The comparator output will remain low as “a logic zero” until the value of the timer register exceeds that of the compare register, at which point the comparator output will be set to high. When the timer register reaches 100, it will reset itself, which will drive the comparator output to a logic zero. This effectively means that the PWM output signal is logic 1 50% of the time and logic zero the other 50% of the time. The actual width of the pulse also depends on the prescaler output signals, but we can modify this by loading different values in the compare register.

## Slide 14: Hardware Module Overview
Arm Cortex-M0
Processor
BRAM
System on Chip
Arm AMBA 3 AHB-Lite System Bus
32-bit Address Bus
32-bit Data Bus
Control Signals
VGA
Peripheral
Monitor
UART
Peripheral
To Host
Timer
Peripheral
GPIO
Peripheral
LED
7-Segment
Peripheral
7-Segment
Display
Notes: We will now learn how to design and implement an AHB timer peripheral. In effect, the implementation of the three operation modes can vary between different devices.

## Slide 15: AHB Timer
Operation principles:
  Contains a 32-bits counter that automatically counts downwards once it is enabled
  On reaching zero, it is reset to the value in the “load value” register.
  At the same time, an interrupt is generated.
AHB
Interface
Data [31:0]
Addr [31:0]
Control [31:0]
addr
Address
Decoder
Data [31:0]
Load [31:0]
Current [31:0]
Control [31:0]
32-bit
Counter
Prescaler
Clk
Notes: The block diagram of the timer peripheral is illustrated here. It consists of the following blocks: AHB Bus Interface, Address Decoder, Prescaler, a 32-bit Counter, and three 32-bit Registers. The AHB interface block is used to manage the flow of data and control signals from the AHB bus to the internal memory space in the timer peripheral. The operation principles of the proposed implementation are as follows. The 32-bit counter automatically counts downwards when it is enabled; when it reaches zero, it is reset to the value stored in the load register and an interrupt signal is generated. The current register holds the value of the 32-bit counter while the control register holds control signals used to start/stop the counter and set the prescaler. The address decoder generates a select signal to choose which of the three internal registers is read from or written to by the AHB bus interface.

## Slide 16: Timer Registers
The timer peripheral should have at least four registers
  Load value register
  The reset value when the timer reaches zero
  Current value register
  The current value of the 32-bit counter
  Control register
  Used to start/stop a counter and set the prescaler
Register | Address | Size
Base address | 0x5200_0000 | 
Load value | 0x5200_0000 | 4 Byte
Current value | 0x5200_0004 | 4 Byte
Control | 0x5200_0008 | 4 Byte
Notes: The internal memory space of the timer peripheral is divided between three registers: a load value register, a current value register, and a control register. Each of these occupies four bytes. The memory addresses for these registers are specified in this table.

## Slide 17: Hardware Module Overview
Arm Cortex-M0
Processor
BRAM
System on Chip
Arm AMBA 3 AHB-Lite System Bus
32-bit Address Bus
32-bit Data Bus
Control Signals
VGA
Peripheral
Monitor
UART
Peripheral
To Host
Timer
Peripheral
GPIO
Peripheral
LED
7-Segment
Peripheral
7-Segment
Display
Notes: We will now learn how to design and implement an AHB GPIO peripheral, which will be connected to LEDs.

## Slide 18: GPIO Overview
General-purpose input/output (GPIO)
  Used for general purpose; no special usage defined
  Widely used in most applications
  The direction of input/output is controlled by the direction register.
  A mask register is often used to mask out certain bits.
Direction Register
Bit [0] out
Bit [1] out
Bit [2] out
Bit [0] in
Bit [1] in
Bit [2] in
To External Devices
Notes: GPIO are general-purpose input/output pins with no special usage defined. Their functionality is typically specified by the users at run time. The availability of these generic additional pins facilitate the integration of third-party IP cores by SoC designers. GPIO are widely used in most applications, especially those that require readings from environment sensors. The direction of input/output is controlled by the direction register. A mask register is often used to mask out certain bits. The upper bound of input and output voltages of those pins is usually the supply voltage of the device. Exceeding this value can, in most cases, causes damage.

## Slide 19: AHB GPIO
Basic hardware architecture
  Only has the basic registers, namely data in, data out, and direction register
  Does not have a mask register or any other functions
AHB
Interface
Data [31:0]
Addr [31:0]
Control [31:0]
addr
Address
Decoder
Data [31:0]
Output Data [7:0]
Input Data [7:0]
Direction [7:0]
External
Devices
Notes: The block diagram of the AHB GPIO peripheral is illustrated here. It consists of the following blocks: an AHB Bus Interface, an Address Decoder, and three 8-bit Registers. The input data register holds the data read from external devices; the output data holds the data to be sent to external devices. The direction register contains control bits which determine the type of operation (read or write). The AHB interface block is used to manage the flow of data and control signals from the AHB bus to the internal memory space in this peripheral. The address decoder generates a select signal to choose which of the three internal registers is read from or written to by the AHB bus interface.

## Slide 20: GPIO Registers
The GPIO peripheral registers include
  Data registers
  Input data: the data read from external devices
  Output data: the data sent to external devices
  Direction register: controls whether it is a read or write operation
Register | Address | Size
GPIO base address | 0x5300_0000 | 
Data | 0x5300_0000 | 4 Byte
Direction | 0x5300_0004 | 4 Byte
Notes: The internal memory space of the GPIO peripheral is divided between three registers: an input register, an output register, and a direction register. Each occupies four bytes. The memory addresses for these registers are specified in this table.

## Slide 21: Hardware Module Overview
Arm Cortex-M0
Processor
BRAM
System on Chip
Arm AMBA 3 AHB-Lite System Bus
32-bit Address Bus
32-bit Data Bus
Control Signals
VGA
Peripheral
Monitor
UART
Peripheral
To Host
Timer
Peripheral
GPIO
Peripheral
LED
7-Segment
Peripheral
7-Segment
Display
Notes: We will now learn how to design and implement an AHB 7-segment peripheral, which interfaces the AHB bus with 7-segment display units.

## Slide 22: 7-Segment Display Overview
The 7-segment display uses seven segments and a dot to display numerals or letters.
Widely used in digital electronic devices, such as digital clocks, electronic meters
Simple control, easy to debug
Notes: A 7-segment display is used for displaying numbers or letters. It is used in many devices such as electronic meters, calculators, and digital clocks. This device has seven display elements that can be lit in different combinations to denote Arabic numbers. The seven segments are often arranged in a slanted style in order to help readability. These segments are of nearly uniform shape and size in most applications.

## Slide 23: AHB 7-Segment Display
The implementation of the 7-segment display varies from device to device; for example, Digilent Nexys series board uses twelve pins to control the 7-segment display
  Segment [6:0]: used to switch on or off one segment
  Dot [0:0]: used to switch the dot bit for one digit
  Anode [3:0]: used to select the four digits, switch on by “0”
Notes: For example, in the Nexys3 board, each of the four digits is composed of seven segments arranged in a “figure 8” pattern. This board uses twelve pins to control the display unit as follows:
Segment [6:0] (CA.CG): used to switch on or off one segment
Dot [0:0] (DP): used to switch the dot bit for one digit
Anode [3:0] (AN0---AN3): used to select the four digits, switch on by “0”

## Slide 24: AHB 7-Segment Display
To display different values on four digits, they need to be enabled one by one. For example, to display “1234,” the sequence can be:
  Anode [3:0]=0111; segment [6:0] = “1”
  Anode [3:0]=1011; segment [6:0] = “2”; and so on
The looping frequency can be set to about 1000Hz, which is
  Slow enough to allow each anode to switch on
  Fast enough for the human eye to visualize that all of the digits are on at the same time
Number ‘1’
Number ‘2’
Letter ‘A’

## Slide 25: AHB 7-Segment Display
The values of the four digits are stored in four registers.
The clock frequency is divided to loop the four digits.
Data [31:0]
Addr [31:0]
Control [31:0]
addr
Address
Decoder
Data [31:0]
Digit 1 [3:0]
Digit 2 [3:0]
Digit 3 [3:0]
Digit 4 [3:0]
Frequency
Divider
Clk
AHB
Interface
Select [1:0]
Anode [3:0]
Anode
Dec
7-Seg
Dec
Segments [7:0]
Notes: The block diagram of an example AHB 7-segment peripheral is illustrated here. It consists of the following blocks: an AHB Bus Interface, an address decoder, four 4-bit Registers, and a Frequency Divider driving the anode decoder. The AHB interface block is used to manage the flow of data and control signals from the AHB bus to the internal memory space in this peripheral. The address decoder generates a select signal to choose which of the four internal registers is to be written to by the AHB bus interface. The frequency divider is driven by the system clock and used to generate the 1 kHz signal driving the anode decoder block.

## Slide 26: 7-Segment Display Registers
The 7-segment peripheral has four registers
  Digit 1: the first digit on the 7-segment display
  Digit 2: the second digit on the 7-segment display
  Digit 3: the third digit on the 7-segment display
  Digit 4: the fourth digit on the 7-segment display
Register | Address | Size
Base address | 0x5400_0000 | 
Digit 1 | 0x5400_0000 | 4 Byte
Digit 2 | 0x5400_0004 | 4 Byte
Digit 3 | 0x5400_0008 | 4 Byte
Digit 4 | 0x5400_000C | 4 Byte
Notes: The internal memory space of the 7-segment display peripheral is divided between four registers, each of which occupies four bytes. The memory addresses for these registers are specified in this table.

## Slide 27: Memory Space
The memory space for all peripherals is allocated as follow:
Peripheral | Base address | End address | Size
MEM | 0x0000_0000 | 0x4FFF_FFFF | 167MB
VGA | 0x5000_0000 | 0x50FF_FFFF | 16MB
UART | 0x5100_0000 | 0x51FF_FFFF | 16MB
Timer | 0x5200_0000 | 0x52FF_FFFF | 16MB
GPIO | 0x5300_0000 | 0x53FF_FFFF | 16MB
7-segment | 0x5400_0000 | 0x54FF_FFFF | 16MB
Arm Cortex-M0
Processor
BRAM
System on Chip
Arm AMBA 3 AHB-Lite System Bus
32-bit Address Bus
32-bit Data Bus
Control Signals
VGA
Peripheral
Monitor
UART
Peripheral
To Host
Timer
Peripheral
GPIO
Peripheral
LED
7-Segment
Peripheral
7-Segment
Display
Notes: Once the designs of the timer, GPIO, and 7-segments peripherals are finished and their behavior is verified through digital simulations, they can be integrated with the SoC design we have already implemented. Our example SoC design will now have six peripherals, as shown here; each of these needs to have a unique memory space. The table in this slide shows the base and end addresses allocated to each peripheral.