## Slide 1: Programming an SoC using C Language
Intro to System-on-Chip Design course

## Slide 2: Learning Objectives
At the end of this lecture, you should be able to:
Outline the advantages and disadvantages of C and Assembly programming languages.
Outline the steps in which high level language programs like C are generated and downloaded onto the hardware.
Identify the data types supported by in Arm processors.
Describe how data is stored in RAM.
Identify how to call a C function from Assembly and call an Assembly function from C Identify how to write and call an assembly function inside C files.

## Slide 3: Module Syllabus
Principles of C Programming and Assembly Programming
Programming Cortex-M0 Processors using C Language and Assembly Language
Writing Assembly Functions Inside C Files

## Slide 4: Building a System on a Chip (SoC)
Memory
VGA
Peripheral
UART
Peripheral
Timer
Peripheral
GPIO
Peripheral
7-Segment
Peripheral
Arm CMSIS-Core
Application Programming Interface (API)
Application Design (e.g., Game)
Arm Cortex-M0
Processor
Hardware design
Software low-level drivers & libraries programming
Software high-level
application development
Peripheral Drivers
AHB
Interrupt
Notes: This module will explore the principles of C and assembly programming and how to use these two languages to program the Cortex-M0 processor.

## Slide 5: C and Assembly Language Review
Language | Advantages | Disadvantages
C | Easy to learn | Limited or no direct access to core registers and stack
 | Portable | No direct control over instruction sequence generation
 | Easy handling of complex data structures | No direct control over stack usage
Assembly | Allow direct control to each instruction step and all memory | Take longer time to learn
 | Allows direct access to instructions that cannot be generated with C | Difficult to manage data structure
 |  | Less portable
Notes: The Cortex-M0 processor can be programmed using C language, assembly language, or a mixture of both. The table here compares the use of C language and assembly language. C language is easy to learn, portable, and makes it easy to handle complex data structures, but it only allows limited access to core registers and the stack. The C programmer will also not have direct control over instruction sequence generation. It takes longer to learn assembly language and is it difficult to manage data structures, but it allows direct control over each instruction step and all memory. An SoC programmer typically needs to use a mix of both languages. Arm C compilers provide an embedded assembler so that assembly functions can be included in C program code easily. Similarly, most other C compilers provide an inline assembler for inlining assembly code within a C program file.

## Slide 6: Typical Program-Generation Flow
The generation of a program follows a typical development flow.
  Compile > Assemble > Link > Download
  The generated executable file (or program image) is stored in the program memory (normally an on-chip flash memory), to be fetched by the processor.
Data Output
C Code
Assembly Code
Machine Code
Libraries
Program Image
Compile
Assemble
Link
Download
Program Memory
Fetch
Decode
Execute
Processor
Processing
Data Input
Instruction
Fetch
Off-line Compilation
Typical program-generation flow
Notes: We are now going to see how programs in high level languages such as C are generated and downloaded onto the hardware. The figure here illustrates a typical development flow. In the first stage, the compilation happens, where the program is translated from a high level language into the assembly language of the specific processor to be programmed, in our case, the Cortex-M0. This is done using a compiler. The assembly language uses mnemonic codes to refer to the instruction sets. Such representation cannot be understood by the processor; therefore, we need to convert the instructions of the assembly program into their numeric values. These values are called machine codes, and this process is completed using the assembler. In the third stage, the object code file generated by the assembler is linked together with the object code files for any library functions used to produce an executable file. Finally, the generated executable file (or program image) is stored in the program memory (normally an on-chip flash memory), to be fetched by the processor.

## Slide 7: Program-Generation Flow with Arm Tools
Compile Using Armcc
Assemble Using Armasm
C Source Code
Assembly Source Code
Object Files (.o)
C/ C++
C/ C++
Libraries
Link Using Armlink
Executable Program Mage
Binary
.O Files
.S Files
.AXF File
.LIB file
.BIN File
.HEX File
Disassembly File
C, C++
ASM files
Download to Program Memory
Notes: The program generation flow using Arm tools is very similar to the generic flow we have just discussed, as can be seen in this diagram. The Arm tools-based flow, however, supports both assembly source files and C language source files; the armcc tool can convert C source code directly into object code, while the armasm tool converts the source files written in assembly language into object code. In the linking stage, the armlink tool can be used. The extensions of the files at the output of each stage of the compilation process is shown in red.

## Slide 8: Program Image
0x00000000
Initial MSP value
Code region
Start-up routine
Vector table
Program
Image
Reset vector
NMI vector
Hard fault vector
Reserved
SVC vector
Reserved
PendSV vector
SysTick vector
Interrupt vectors
0x00000000
0x00000004
0x00000008
0x0000000C
0x0000002C
0x00000038
0x00000040
0x0000003C
Program code
C library code
Notes:   Now that we understand the compilation stages of a program from a high level language to a binary file, we are going to examine the contents of the program image of the Cortex-M0. A program image (sometimes referred to as the executable file) usually refers to a piece of fully integrated code that is ready to execute. In the Cortex-M0, the program image is stored in the code region of the memory map. The program image includes a number of regions, namely, vector table, C start-up routine, program code, and C library code. We will now discuss the contents of these regions in more detail.

## Slide 9: Program Image
0x00000000
Initial MSP value
Code region
Start-up routine
Vector table
Program
Image
Reset vector
NMI vector
Hard fault vector
Reserved
SVC vector
Reserved
PendSV vector
SysTick vector
Interrupt vectors
0x00000000
0x00000004
0x00000008
0x0000000C
0x0000002C
0x00000038
0x00000040
0x0000003C
Program code
C library code
Notes: The vector table contains the starting addresses of exceptions (vectors). It also includes the initial value of the main stack point (MSP); this is stored in the first word of the vector table. It can be programmed in either C or assembly.

## Slide 10: Program Image
0x00000000
Initial MSP value
Code region
Start-up routine
Vector table
Program
Image
Reset vector
NMI vector
Hard fault vector
Reserved
SVC vector
Reserved
PendSV vector
SysTick vector
Interrupt vectors
0x00000000
0x00000004
0x00000008
0x0000000C
0x0000002C
0x00000038
0x00000040
0x0000003C
Program code
C library code
Notes: The linker may, in some cases, add C library code to the program image; for example, the divide function is typically imported from the C library. This is because there is no divide instruction in the Cortex-M0. Other cases where the C library code can be included in the program image is when using floating point operations.

## Slide 11: Program Image
0x00000000
Initial MSP value
Code region
Start-up routine
Vector table
Program
Image
Reset vector
NMI vector
Hard fault vector
Reserved
SVC vector
Reserved
PendSV vector
SysTick vector
Interrupt vectors
0x00000000
0x00000004
0x00000008
0x0000000C
0x0000002C
0x00000038
0x00000040
0x0000003C
Program code
C library code
Notes: The program code includes the sequence of the instructions that correspond to the program being executed; in addition, this part of the program image includes other types of information such as initial values of the variables, constant values, peripheral addresses, character strings, lookup tables, and graphic image data. Some of this information, such as initial values, needs to be used during program execution.

## Slide 12: Program Image
0x00000000
Initial MSP value
Code region
Start-up routine
Vector table
Program
Image
Reset vector
NMI vector
Hard fault vector
Reserved
SVC vector
Reserved
PendSV vector
SysTick vector
Interrupt vectors
0x00000000
0x00000004
0x00000008
0x0000000C
0x0000002C
0x00000038
0x00000040
0x0000003C
Program code
C library code
Notes: The start-up routine part of the program image zero is used to initialize data memory variables that are uninitialized at load time. It also sets up data memory such as global data variables. The start-up routine is automatically added to the program image by the compiler or linker. It is labelled “__main” by the Arm compiler, but may have a different label if other compilers are being used.

## Slide 13: Program Image in Global Memory
Reserved
External Device
External RAM
Peripherals
SRAM
Code
0xFFFFFFFF
0xE0000000
Private Peripheral Bus
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE0100000
Mainly used for data memory
e.g., on-chip SRAM, SDRAM
Mainly used for program image
e.g., on-chip FLASH
Notes: In the Cortex-M0, the program image is stored in the code region in global memory, up to 512 MB memory space, ranging from 0x00000000 to 0x1FFFFFFF. It is usually implemented on non-volatile memory, such as on-chip FLASH memory. It is normally separated from program data, which is allocated in the SRAM region (or data region). We are now going to look at the different data types supported by the Cortex-M0.

## Slide 14: Program Data Types
Data type | Size | Signed range | Unsigned range
char, int8_t, uint8_t | Byte | -128 to 127 | 0 to 255
short, int16_t, uint16_t | Half word | -32768 to 32767 | 0 to 65535
int, int32_t, uint32_t, long | Word | -2147483648 to 2147483647 | 0 to 4294967295
long , int64_t, uint64_t | Double word | -263 to 263-1 | 0 to 264-1
float | Word | -3.4028234 × 1038 to 3.4028234 × 1038 | 
double, long double | Double word | -1.7976931348623157 ×10308 to 1.7976931348623157 ×10308 | 
pointers | Word | 0x00 to 0xFFFFFFFF | 
enum | Byte/half word/word | Smallest possible data type | 
bool (C++), _bool(C) | Byte | True or false | 
wchar_t | Half word | 0 to 65535 | 
Notes: The type of program data that can be supported depends on the processor architecture and the compiler. This table summarizes the program data types supported in Arm processors, including the Cortex-M0. These types are also supported by all C compilers. Four data sizes are supported in Arm programming: byte (8-bit), half word (16-bit), word, and double word (64 bit).

## Slide 15: Data Qualifiers in C Language
const vs volatile
const
Never written by program
Can be put in ROM to save RAM
volatile
Can be changed outside of normal program flow: ISR, hardware register
Compiler must be careful with optimizations
Notes: The data types in the previous slides are called type specifiers. In addition, the C language also has type qualifiers. A type qualifier is a keyword that is applied to a type, resulting in a qualified type; in other words, type qualifiers are used to give additional information about a value, which ensure its correct use. We are going to look at two type qualifiers: const and volatile.
Const means that something is not modifiable; therefore, when a data object is declared as const, this means that it must not be altered in the execution of a program. The definition of an object as a const will typically contain an initializer, or, since it cannot be assigned, how would it get a value? However, this is not always the case. For example, if you were accessing a hardware port at a fixed memory address and promised only to read from it, then it would be declared const but not initialized.
A volatile qualifier is also used to specify the data type of an object, and it indicates that an object is open to change at any time. Therefore, it must be read from memory each time it is accessed. This qualifier is most often

## Slide 16: How Is Data Stored in RAM
Typically, data can be stored in three regions: static data, stack, and heap
  Static data: contains global variables and static variables
  Stack: contains temporary data for local variables, parameter passing in function calls, registers saving during exceptions, etc.
  Heap: contains the pieces of memory spaces that are dynamically reserved by function calls, such as “alloc(),” “malloc()”
Memory
Address
Grow
Downwards
High
Stack
Static
Data
Heap
Grow
Upwards
Low
Notes: The RAM in microcontrollers is used in different ways. Data can typically be stored in three regions: static data, stack, and heap. Static data includes static and global variables; stack region is used to store temporary data for local variables, registers during exceptions, and to pass parameter during function calls; heap region includes areas of memory that are dynamically reserved by function calls.

## Slide 17: Example of Data Storage
int a, b;
const char c=123;
int d=31;
void main(void) {
int i;
char f[32];
int *array;
array =(int*)malloc(128);
e = d + 7;
printf(“Hello!”);
}
Heap Data
Initialized Static Data
Stack Data
Zero-initialized Static Data
Usually stored in volatile memories, e.g., SRAM
Usually stored in non-volatile memories, e.g., FLASH
Runtime Library Code
Initialization Data
Constant Data
Program Code
.text
Startup Code
Notes: So far we have learned that in the Cortex-M0, the program image is stored in the code region in global memory. The latter (global memory) is up to 512 MB and is usually implemented on non-volatile memory, such as on-chip FLASH memory. We have also learned that program data is normally separated from the program image, and usually allocated in the SRAM region (or data region). In this slide, we can see an example of the data storage of a simple program. For example, the global variable d = 31 is stored in the static data region in the RAM. The constant (c = 123) is stored in the start-up routine section of the program image in order to save space on the SRAM. The part of the code performing addition (e = d + 7) will be stored in the program code region in the flash memory.

## Slide 18: Define Interrupt Vector in C
The interrupt vector can be defined in either C language or assembly language. For example, in C:
typedef void(* const ExecFuncPtr)(void) __irq;
#pragma arm section rodata="exceptions_area”
ExecFuncPtr exception_table[] = {
(ExecFuncPtr)&Image$$ARM_LIB_STACK$$ZI$$Limit, /* Initial SP */
(ExecFuncPtr)__main, /* Initial PC */
NMIException,
HardFaultException,
MemManageException,
BusFaultException,
UsageFaultException,
0, 0, 0, 0, /* Reserved */
SVCHandler,
DebugMonitor,
0, /* Reserved */
PendSVC,
SysTickHandler
/* Configurable interrupts start here...*/
};
#pragma arm section
Notes: First, we will learn how to define an interrupt vector. An interrupt vector can be programmed in either C language or assembly language. The toolchain typically determines the details of the vector table. This is because vector table entries need symbols generated by the compiler and linker. In this slide, we can see an example of how to define the vector table in C.

## Slide 19: Define Stack and Heap
The stack and heap can be defined in either C language (with a linker file) or assembly language. For example, in C:
/* Set stack and heap parameters */
#define STACK_BASE 0x10020000 //stack start address
#define STACK_SIZE 0x5000 //length of the stack
#define HEAP_BASE 0x10001000 //heap starts address
#define HEAP_SIZE 0x10000 – 0x6000 //heap length
/* inker generated stack base addresses */
extern unsigned int Image$$ARM_LIB_STACK$$ZI$$Limit
extern unsigned int Image$$ARM_LIB_STACKHEAP$$ZI$$Limit
…
Notes: It is also possible to define the sizes and base addresses of the stack and heap in C language using the #define directive, as illustrated in this example.

## Slide 20: Define Stack and Heap
Define stack and heap in assembly language:
Stack_Size EQU 0x00000400 ; 256KB of STACK
AREA STACK, NOINIT, READWRITE, ALIGN=4
Stack_Mem SPACE Stack_Size
__initial_sp
Heap_Size EQU 0x00000400 ; 1MB of HEAP
AREA HEAP, NOINIT, READWRITE, ALIGN=4
__heap_base
Heap_Mem SPACE Heap_Size
__heap_limit
Notes: Alternatively, we can use assembly language to define the sizes and base addresses of the stack and heap, as shown here.

## Slide 21: Accessing Peripherals in C
Define base addresses for peripherals.
Write a value to a peripheral register.
Read a value from a peripheral register.
#define AHB_VGA_BASE 0x50000000
#define AHB_UART_BASE 0x51000000
#define AHB_TIMER_BASE 0x52000000
#define AHB_GPIO_BASE 0x53000000
#define AHB_7SEG_BASE 0x54000000
#define NVIC_INT_ENABLE 0xE000E100
*(unsigned int*) AHB_TIMER_BASE = 0x3FFFF; //store a value to the peripheral
i=*(unsigned int*) AHB_GPIO_BASE; //read a value from the peripheral
Notes: In the Cortex-M0, it is also very easy to define the base address of a peripheral using C language, as illustrated in this example, where we use the directive #define to define the addresses of all six peripherals connected to our SoC. Once the address of a peripheral is defined, it can be written to and read using C language, as illustrated here.

## Slide 22: Calling a C Function from Assembly
When a C function is called from an assembly file, the following areas should be checked:
  Register R0, R1, R2, R3, R12, and LR could be changed; hence, it is better to save them to the stack.
  The value of SP should be aligned to a double-word address boundary.
  Input parameters have to be stored in the correct registers; for example, registers R0 to R3 can be used for passing four parameters.
  The return value is usually stored in R0.

## Slide 23: Calling a C Function from Assembly
ISR can be written in either assembly or C language; for example, in C:
Call a C function from the assembly code; for example:
void UART_ISR() {
char c;
c=*(char*) AHB_UART_BASE; //read a character from UART
…
}
UART_Handler PROC
EXPORT UART_Handler // label name in assembly
IMPORT UART_ISR // function name in C
PUSH {R0,R1,R2,LR} // context saving
BL UART_ISR // branch to ISR written in C
POP {R0,R1,R2,PC} // context restoring
ENDP
Notes: Here is an example of how to call a C function from assembly code. We have an ISR written in C that can read a character from UART. This ISR is called UART_ISR. In order to call this function from assembly code, we simply use the IMPORT keyword with the name of the function to be called (e.g., UART_ISR).

## Slide 24: Calling an Assembly Function from C
When calling an assembly function from C code, the following areas should be checked:
  If registers R4 to R11 need to be changed, they have to be stacked and restored in the assembly function.
  If another function is called inside the assembly function, the LR register needs to be saved on the stack and used for return.
  The function return value is normally stored in R0.

## Slide 25: Calling an Assembly Function from C
Write a function in assembly:
Calling an assembly function in C:
EXPORT add_asm
add_asm FUNCTION
ADDS R0, R0, R1
ADDS R0, R0, R2
ADDS R0, R0, R3
BX LR ; result is returned in R0
ENDFUNC
external int add_asm( int k1, int k2, int k3, int k4);
void main {
int x;
x = add_asm (11,22,33,44); // call assembly function
…
}
Notes: For example, if we have an assembly function that adds four values, as illustrated in this example (add_asm), we need to declare it in the C code before we can use it. In the example shown here, we declare the (add_asm) at the start of the C code and we use it in the main section.

## Slide 26: Embedded Assembly
The embedded assembler allows a developer to write assembly functions inside C files:
_asm int add_asm( int k1, int k2, int k3, int k4) {
ADDS R0, R0, R1
ADDS R0, R0, R2
ADDS R0, R0, R3
BX LR
}
void main {
int x;
x = add_asm (11,22,33,44); // call assembly function
…
}
Notes: When developing software applications, there may be cases when there is a need to embed the assembly code in the same program file as the C code. This feature is available for Arm Cortex-M0 programmers using an “embedded assembler”. The latter allows developers to write assembly functions inside C files. For example, the “my_add_e” function that adds four parameters could be written as shown here. This function can be called in C code in a manner similar to any other normal C functions, as follows: y = my_add_e(1, 2, 3, 4);