## Slide 1: Arm Cortex-M7 Processor Architecture Part 2
Notes: Hello and welcome.
In this video, we will look at Arm Cortex-M7 Processor Architecture. This is Part 2 of the course.

## Slide 2: Module Syllabus
Cortex-M7 Memory Map
Cortex-M7 Program Image and Endianness
Arm and Thumb Instruction Set Overview
Cortex-M7 Instruction Set
Notes: We will go through the Cortex-M7 memory map, program image and endianness, the Arm and Thumb instruction set overview, and the Cortex-M7 instruction set.

## Slide 3: Cortex-M7 Memory Map
The Cortex-M7 Processor has 4 GB of memory address space
  Support for bit-band operation (detailed later)
The 4GB memory space is architecturally defined as a number of regions
  Each region is given for recommended usage
  Easy for software programmer to port between different devices
Nevertheless, despite the default memory map, the actual usage of the memory map can also be flexibly defined by the user, except some fixed memory addresses, such as internal private peripheral bus
Notes: The Arm Cortex-M7 memory map describes the organization of the processor’s address space. The address space contains data sources and sinks such as internal and external RAM and ROM as well as buses, peripherals, and further parts and equipment.
The total memory space of a 32-bit system, like the Cortex-M7, is 2^32 = 4GB. It is split and separated into regions with different functionality, which can be individually changed, apart from some fixed assigned addresses, such as internal private peripheral bus.

## Slide 4: Cortex-M7 Memory Map
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE00FE000
PPB ROM table
0xE0043000
Private peripheral bus-Internal
Private peripheral bus
e.g. NVIC, SCS
System
0xFFFFFFFF
0xE0000000
Private peripheral bus-External
Mainly used for external peripherals
e.g. SD card
Mainly used for external memories
e.g. external DDR, FLASH, LCD
Mainly used for on-chip peripherals
e.g. AHB, APB peripherals
Mainly used for data memory
e.g. on-chip SRAM, SDRAM
Mainly used for program code
e.g. on-chip FLASH
0x40000000
0x20000000
External device
External RAM
Peripheral
SRAM
Code
0xA0000000
0x60000000
0x00000000
0xE0100000
Reserved for other purposes
0xE0040000
Processor ROM table
Private Peripheral Bus
CTI
ETM
Reserved(TPIU)
0xE00FF000
0xE0042000
0xE0041000
0xE0040000
Notes: The Arm architecture uses a single flat address space of 2^(32) 8-bit bytes. Byte addresses are treated as unsigned numbers running from 0 to 2^(32) - 1. The diagram here shows the memory regions of Armv7-M architecture. Each region has a defined memory type, and some regions have additional memory attributes. The memory type and attributes determine the behavior of accesses to the region.

## Slide 5: Cortex-M7 Memory Map
Code Region
  Primarily used to store program code
  Can also be used for data memory
  On-chip memory, such as on-chip FLASH
SRAM Region
  Primarily used to store data, such as heaps and stacks
  Can also be used for program code
  On-chip memory; despite its name “SRAM”, the actual device could be SRAM, SDRAM or other types
Peripheral Region
  Primarily used for peripherals, such as Advanced High-performance Bus (AHB) or Advanced Peripheral Bus (APB) peripherals. Example: On-chip peripherals
0x40000000
0x20000000
Peripheral
SRAM
Code
0x60000000
0x00000000
512MB
512MB
512MB
Notes: The code region with 0x00000000-0x1FFFFFFF address range is the executable region for the program core. Data can also be put here.
The SRAM region with 0x20000000-0x3FFFFFFF address range is the executable region for data. Code can also be put here.
The peripheral region with 0x40000000-0x5FFFFFFF address range is used for peripherals attached to the core on the address and data bus.
By arranging the typical code, data and peripheral regions into fixed locations, the processor design can optimise the speed of access over the internal buses.

## Slide 6: Cortex-M7 Memory Map
External RAM Region
  Primarily used to store large data blocks, or memory caches
  Off-chip memory, slower than on-chip SRAM region
External Device Region
  Primarily used to map to external devices
  Off-chip devices, such as SD card
Private Peripheral Bus (PPB)
  Used inside the processor core for internal control
  Within PPB, a special range of memory is defined as System Control Space (SCS)
  The Nested Vectored Interrupt Controller (NVIC) is part of SCS
1GB
1GB
512MB
Private peripheral bus-Internal
System
0xFFFFFFFF
0xE0000000
Private peripheral bus-External
External device
External RAM
0xA0000000
0xE0100000
0xE0040000
Notes: The external RAM region with 0x60000000-0x9FFFFFFF address range is the executable region for data.
The external device region with 0xA0000000-0xDFFFFFFF address range is the external device memory, which is primarily used to map external devices.
The Private Peripheral Bus (PPB) region with 0xE0000000-0xE00FFFFF address range provides access to internal and external processor resources.
Within the PPB region, a special range of memory is defined as the system control space (SCS). The Nested Vectored Interrupt Controller (NVIC) is part of the SCS.

## Slide 7: Cortex-M7 Memory Map Example
AHB bus
External SRAM,
FLASH
External LCD
SD card
Cortex-M7
PPB
SCS
NVIC
Debug Ctrl
On-chip FLASH
(Code Region)
On-chip SRAM
(SRAM Region)
Peripheral Region
External memory interface
(External RAM Region)
External device interface
(External Device Region)
Timer
UART
GPIO
Chip Silicon
Notes: In this figure, a structural example of the memory map is given. Beginning at the top, the processor internal elements connected to the PPB, such as debug control and NVIC, are implemented. All additional components are connected to the processor via the AHB (Advanced High-Performance Bus), including the on-chip peripherals such as the timer, general-purpose input/output ports, or communication systems like UART. Directly attached to the AHB are the chip internal memory components for the ROM (flash) and RAM. However, external memory and peripheral components share a common interface to the AHB, respectively, between several components.

## Slide 8: Cortex-M7 Program Image
The program image in Cortex-M7 contains:
  Vector table – includes the starting addresses of exceptions (vectors) and the value of the main stack point (MSP)
  C start-up routine
  Program code – application code and data
  C library code – program codes for C library functions
0x00000000
Code region
Start-up routine &
Program code &
C library code
Vector table
Program
image
SysTick
IRQ0
Initial MSP value
Reset
NMI
Hard fault
Memory Managemet fault
Reserved
PendSV
Bus fault
Usage fault
Reserved
SVCall
Reserved for Debug
IRQ1
IRQ2
.
.
.
IRQ239
Notes: A program starting at 0x00000000 is subdivided into the following parts:
  First, the vector tables are located.
  The start-up routine, the program code, and static libraries are located beyond the vector table.
Vector tables are created because many overarching features of a controller contain bitwise features, such as interrupts. To save memory space, they are consolidated into bytes or words, so-called bit vectors. Therefore, a vector needs to be evaluated bitwise to interpret the meaning or origin of the change.

## Slide 9: Cortex-M7 Program Image
After reset, the processor:
  First reads the initial MSP value
  Then reads the reset vector
  Branches to the start of the programme execution address (reset handler)
  Subsequently executes program instructions
Reset
Fetch initial value for MSP
(read address 0x00000000)
Fetch reset vector
(read address 0x00000004)
Fetch 1st instruction
(read address of reset vector)
Fetch 2nd instruction
(read subsequent instructions)
Notes: After reset, the MSP initializes the address of the beginning of the stack. Then, the reset vector defines the address of the first line of executable code and is located at address 0x00000004. From now on, the program can be started and executed line by line.
Note that the value at address 0x00000004 must always have bit [0] set, this is used to indicate that the reset handler is executed in Thumb state.

## Slide 10: Cortex-M7 Endianness
Endian refers to the order of bytes stored in memory:
  Little endian: lowest byte of a word-size data is stored in bit 0 to bit 7
  Big endian: lowest byte of a word-size data is stored in bit 24 to bit 31
Cortex-M7 supports both little endian and big endian
However, endianness only exists in the hardware level
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
0x00000000
0x00000004
0x00000008
Address
[7:0]
[15:8]
[23:16]
[31:24]
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
[7:0]
[15:8]
[23:16]
[31:24]
Word 1
Word 2
Word 3
Word 1
Word 2
Word 3
Little endian 32-bit memory
Big endian 32-bit memory
Notes: Endianness describes the order in which bytes have to be combined in halfwords or words. For Arm architectures, the endianness has little significance, as either word-wise operations (4 bytes) are performed automatically in the correct order by the instruction set or the information is stored in single bytes regardless of any endianness.
Endianness is only important if halfwords (2 bytes) are manually stored byte wise. In this case, we must consider whether the most significant byte is stored first or last. If the most significant byte is stored at the highest bit positions, this is called “little endianness”. On the other hand, if the most significant byte is stored at the lowest bit positions, this is called “big endianness”.

## Slide 11: Arm and Thumb Instruction Set
Early Arm instruction set
  32-bit instruction set, called the Arm Instructions
  Powerful and good performance
  Larger program memory compared to 8-bit and 16-bit processors
  Larger power consumption
Thumb-1 instruction set
  16-bit instruction set, first used in Arm7TDMI Processor in 1995
  Provides a subset of the Arm Instructions, giving better code density compared to 32-bit RISC architecture
  Code size is reduced by ~30%, but performance is also reduced by ~20%
Notes: The Arm standard instruction set is 32 bits long with three operand formats for load and store operations, where most instructions can be executed conditionally and in a single cycle. One side effect of the early Arm instruction set is that it required larger program memory than 8- or 16-bit processors and larger power consumption, as more information needed to be moved.
By comparison, Thumb-1 is a 16‐bit instruction set that is optimized for code density from C code. It is a subset of the Arm instruction set functionality with better code density, with minimal performance penalty. Thumb instructions are executed unconditionally, and many of the data processing instructions use a 2‐address format. As a result of the dense encoding, Thumb instruction formats are less regular than Arm instruction formats.

## Slide 12: Arm and Thumb Instruction Set
Mix of Arm and Thumb-1 instruction sets
  Benefit from both 32-bit Arm (high performance) and 16-bit Thumb-1 (high code density)
  A multiplexer is used to switch between two states: Arm state (32-bit) and Thumb state (16-bit), which requires a switching overhead
Incoming
instructions
Thumb remap
to Arm
Arm
Instruction
decoder
Instructions
executing
T bit, 0: select Arm,
1: select Thumb
0
1
Notes: In earlier processor architectures, Arm and Thumb-1 instructions could be mixed, but that required switching a multiplexer between the two instruction sets. That reduced the speed due to the switching overhead.

## Slide 13: Arm and Thumb Instruction Set
Thumb-2 instruction set
  Consists of both 32-bit Thumb instructions and original 16-bit Thumb-1 instruction sets
  Compared to 32-bit Arm instructions set, code size is reduced by ~26%, while keeping a similar performance
  Capable of handling all processing requirements in one operation state
Notes: Thumb-2 is a superset of the Thumb instruction set. Thumb-2 introduces 32-bit instructions that are mixed with the 16-bit instructions. The Thumb-2 instruction set covers almost all the functionality of the Arm instruction set. Thumb-2 is backward compatible with the Armv6 Thumb instruction set.
The most important difference between the Thumb-2 instruction set and the Arm instruction set is that most Thumb-2 instructions are unconditional, whereas almost all Arm instructions can be conditional.
Thumb-2’s performance is close to or better than that of the Arm instruction set, and has the code density of the original Thumb-1.

## Slide 14: Cortex-M7 Instruction Set
Cortex-M7 processor
  Armv7-M architecture
  Supports 32-bit Thumb-2 instructions
  Possible to handle all processing requirements in one operation state (Thumb state)
  Compared with traditional Arm processors (use state switching), advantages include:
    No state switching overhead – both execution time and instruction space are saved
    No need to separate Arm code and Thumb code source files, which makes the development and maintenance of software easier
    Easier to get optimised efficiency and performance
Notes: The Cortex-M7 processor is an implementation of the Armv7-M architecture.
Armv7-M supports a large number of 32-bit instructions that Thumb-2 technology introduced into the Thumb instruction set. Much of the functionality available is identical to the Arm instruction set supported alongside the Thumb instruction set in Armv6T2 and other Armv7 profiles. Thumb instructions are either 16-bit or 32-bit and are aligned on a two-byte boundary. 16-bit and 32-bit instructions can be intermixed freely.

## Slide 15: Cortex-M7 Instruction Set
Arm assembly syntax:
  label
    mnemonic operand1, operand2, … ; Comments
  Label is used as a reference to an address location;
  Mnemonic is the name of the instruction;
  Operand1 is the destination of the operation;
  Operand2 is normally the source of the operation;
  Comments are written after “ ; ”, which does not affect the program;
Notes: Here is the syntax of the Arm assembly.
The label is a symbolic representation of addresses. You can use labels to mark specific addresses that you want to refer to from other parts of the code.
Mnemonic is the name of the instruction, for example, ADD, MOV, etc. Most data processing instructions can optionally update the condition flags according to the result of the operation. You can also execute an instruction conditionally, based on the condition flags set in another instruction, either immediately after the instruction that updated the flags or after any number of intervening instructions that have not updated the flags.
Conditional execution is available by using conditional branches or by adding condition code suffixes to instructions. The condition code suffix enables the processor to test a condition based on the flags. If the condition test of a conditional instruction fails, then the instruction does not execute, does not write any value to its destination register, does not affect any of the flags, and does not generate any exception.
An instruction operand can be an Arm register, a constant, or another instruction-specific parameter.
Instructions act on the operands and often store the result in a destination register.
When there is a destination register in the instruction, it is usually specified before the operands.

## Slide 16: Cortex-M7 Instruction Set
For example
  MOVS R3, #0x11 ;Set register R3 to 0x11
  Note that the assembly code can be assembled by either Arm assembler (armclang) or assembly tools from a variety of vendors (e.g. GNU tool chain). When using GNU tool chain, the syntax for labels and comments is slightly different
Notes: Here is an example of an instruction set.
Note that instruction mnemonics, pseudo-instructions, directives, and symbolic register names can be written in all uppercase or all lowercase, but not mixed. Labels and comments can be in uppercase or lowercase, or mixed.

## Slide 17: Cortex-M7 Instruction Set
Mnemonic | Operands | Brief description | Flags
ADC, ADCS | {Rd,} Rn, Op2 | Add with Carry | N,Z,C,V
ADD, ADDS | {Rd,} Rn, Op2 | Add | N,Z,C,V
ADD, ADDW | {Rd,} Rn, #imm12 | Add | N,Z,C,V
ADR | Rd, label | Address to Register | 
AND, ANDS | {Rd,} Rn, Op2 | Logical AND | N,Z,C
ASR, ASRS | Rd, Rm, <Rs¦#n> | Arithmetic Shift Right | N,Z,C
B | label | Branch | 
BFC | Rd, #lsb, #width | Bit Field Clear | 
BFI | Rd, Rn, #lsb, #width | Bit Field Insert | 
BIC, BICS | {Rd,} Rn, Op2 | Bit Clear | N,Z,C
BKPT | #imm | Breakpoint | 
BL | label | Branch with Link | 
BLX | Rm | Branch indirect with Link and Exchange | 
BX | Rm | Branch indirect and Exchange | 
Notes: Here are some examples of the Arm instruction set.
For more information, see the Cortex-M7 Devices Generic User Guide.

## Slide 18: Cortex-M7 Instruction Set
Mnemonic extension | Meaning, integer arithmetic | Meaning, floating-point arithmetic | Condition flags
EQ | Equal | Equal | Z == 1
NE | Not equal | Not equal, or unordered | Z == 0
CS | Carry set | Greater than, equal, or unordered | C == 1
CC | Carry clear | Less than | C == 0
MI | Minus, negative | Less than | N == 1
PL | Plus, positive or zero | Greater than, equal, or unordered | N == 0
VS | Overflow | Unordered | V == 1
VC | No overflow | No unordered | V == 0
Condition codes
  Append to branch instruction (B) to make a conditional branch
  Full Arm instructions (not Thumb or Thumb-2) support conditional execution of arbitrary instructions. Note: Carry bit = not-borrow for compares and subtractions
Mnemonic extension | Meaning, integer arithmetic | Meaning, floating-point arithmetic | Condition flags
HI | Unsigned higher | Greater than, or unordered | C == 1 and Z == 0
LS | Unsigned lower or same | Less than or equal | C == 0 or Z == 1
GE | Signed greater than or equal | Greater than or equal | N == V
LT | Signed less than | Less than, or unordered | N != V
GT | Signed greater than | Greater than | Z == 0 or N != V
LE | Signed less than or equal | Less than, equal, or unordered | Z==1 or N !=V
None (AL) | Always (unconditional) | Always (unconditional) | Any
Notes: Most of the instructions also have an optional condition suffix (mnemonic extension).
The tables here list the available condition codes, their meaning, and the flags that are tested.
For example, if you add “NE” as a suffix to the branch instruction “B”, then the “BNE” instruction only executes if condition “Not Equals” is true. This condition is true if the Z flag is clear, so the BNE instruction would iterate the loop until the Z flag is set to 1.
Although most of the Thumb 32 instructions do not support conditional execution on their own, the unified assembly syntax and the IT (conditional execution instruction) allow conditional execution to be applied to most of the instruction set.

## Slide 19: Cortex-M7 Instruction Set
Intrinsic functions
  ISO/IEC C code cannot directly access some Cortex-M7 instructions.
  Instead, intrinsic functions that are provided by the CMSIS or a C compiler are used to generate some of these Cortex-M7 instructions.
  If a C compiler does not support an appropriate intrinsic function, you might have to use inline assembler to access the relevant instruction.
Instruction | CMSIS intrinsic function
CPSIE I | void __enable_irq(void)
CPSID I | void __disable_irq(void)
CPSIE F | void __enable_fault_irq(void)
CPSID F | Void __disable_fault_irq(void)
ISB | void __ISB(void)
DSB | void __DSB(void)
DMB | void __DMB(void)
REV | uint32_t __REV(uint32_t int value)
REV16 | uint32_t __REV16(uint32_t int value)
REVSH | uint32_t __REVSH(uint32_t int value)
RBIT | uint32_t __RBIT(uint32_t int value)
SEV | void __SEV(void)
WFE | void __WFE(void)
WFI | void __WFI(void)
Notes: There are some Cortex-M7 instructions that cannot be directly accessed by the ISO/IEC C code.
To generate some of such instructions, “intrinsic functions” that are provided by CMSIS or a C compiler are used instead.
This table shows the intrinsic functions that CMSIS provides to generate instructions that ISO/IEC C code cannot directly access.
Note that if a C compiler does not support an appropriate intrinsic function, you might have to use an inline assembler to access the relevant instruction.

## Slide 20: Useful Resources
  Cortex-M7 Technical Reference Manual:
  http://infocenter.arm.com/help/topic/com.arm.doc.ddi0489c/DDI0489C_cortex_m7_trm.pdf
  Cortex-M7 Devices Generic User Guide:
  http://infocenter.arm.com/help/topic/com.arm.doc.dui0646a/DUI0646A_cortex_m7_dgug.pdf
  Cortex-M7 Processor Overview:
  https://developer.arm.com/products/processors/cortex-m/cortex-m7
Notes: For more detailed information, see the Cortex-M7 processor documentation.