## Slide 1: CMOS VLSI Design Lecture 17: Clocking
Notes: Hello and welcome.

## Slide 2: Learning Objectives
At the end of this lecture, you should be able to:
Describe the implications of clock distribution networks on skew and clock power
Design clock generators using delay and phase-locked loops

## Slide 3: Clock Distribution
On a small chip, the clock distribution network is just a wire
  And possibly an inverter for clkb
On practical chips, the RC delay of the wire resistance and gate load is very long
  Variations in this delay cause clock to get to different elements at different times
  This is called clock skew
Most chips use repeaters to buffer the clock and equalize the delay
  Reduces but doesn’t eliminate skew
Notes: Good clock distribution network ensures that data signals are synchronized among synchronous datapaths to avoid skew.

## Slide 4: Example
Skew comes from differences in gate and wire delay
  With right buffer sizing, clk1 and clk2 could ideally arrive at the same time.
  But power supply noise changes buffer delays
  clk2 and clk3 will always see RC skew
Notes: Skew can be as a result of mismatched wires, mismatched buffers, gate delay, and variable loads, which may result delayed clock arrival times.

## Slide 5: Review: Skew Impact
Ideally full cycle is
available for work
Skew adds sequencing
overhead
Increases hold time too
Notes: Skew adds to sequencing overhead and also increases hold time. Therefore, the aim would be to minimize clock skew.

## Slide 6: Solutions
Reduce clock skew
  Careful clock distribution network design
  Plenty of metal wiring resources
Analyze clock skew
  Only budget actual, not worst-case skews
  Local vs. global skew budgets
Tolerate clock skew
  Choose circuit structures insensitive to skew
Notes: Clock skew can be reduced by careful design of clock distribution network.
Also, circuit structure can be chosen such that they are tolerant to clock skew.

## Slide 7: Clock Dist. Networks
Ad hoc
Grids
H-tree
Hybrid

## Slide 8: Clock Grids
Use grid on two or more levels to carry clock
Make wires wide to reduce RC delay
Ensures low skew between nearby points
But possibly large skew across die

## Slide 9: Alpha Clock Grids
Notes: Alpha clock grids are divided into driver panes
– 21064 is a one driver pane clock grid
– 21164 is a two driver panes clock grid
– 21264 is a sixteen driver panes clock grid

## Slide 10: H-Trees
Fractal structure
  Gets clock arbitrarily close to any point
  Matched delay along all paths
Delay variations cause skew
A and B might see big skew
Notes: Clock gets close to any point, which means low routing resources needed. However, this system can suffer from skew due to variations in branches delay.

## Slide 11: Itanium 2 H-Tree
Four levels of buffering:
  Primary driver
  Repeater
  Second-level
  clock buffer
  Gater
Route around
obstructions

## Slide 12: Hybrid Networks
Use H-tree to distribute clock to many points
Tie these points together with a grid
E.g., IBM Power4, PowerPC
  H-tree drives 16-64 sector buffers
  Buffers drive total of 1024 points
  All points shorted together with grid
Notes: Hybrid combines both H-tree and Grid.

## Slide 13: Clock Generation
Low frequency:
  Buffer input clock and drive to all registers
High frequency
  Buffer delay introduces large skew relative to input clocks
    Makes it difficult to sample input data
  Distributing a very fast clock on a PCB is hard

## Slide 14: Zero-Delay Buffer
If the periodic clock is delayed by Tc, it is indistinguishable from the original clock
Build feedback system to guarantee this delay
Phase-Locked
Loop (PLL)
Delay-Locked
Loop (DLL)
Notes: PLL and DLL employ a feedback system to match or change the phase of a clock signal.

## Slide 15: Frequency Multiplication
PLLs can multiply the clock frequency
Notes: From the output equation, it can be seen that N/M if not equal to 1 means the output frequency is derived from multiplying the input signal.

## Slide 16: Phase and Frequency
Analyze PLLs and DLLs in term of phase F(t) rather than voltage v(t)
Input and output clocks may
deviate from locked phase
  Small signal analysis

## Slide 17: Linear System Model
Treat PLL/DLL as a linear system
  Compute deviation DF from locked position
  Assume small deviations from locked
  Treat system as linear for these small changes
Analysis is not valid far from lock
  e.g., during acquisition at startup
Continuous time assumption
  PLL/DLL is really a discrete time system
    Updates once per cycle
  If the bandwidth << 1/10 clock freq, treat as continuous
Use Laplace transforms and standard analysis of linear continuous-time feedback control systems

## Slide 18: Phase-Locked Loop (PLL)
System
Linear Model
Notes: A phase-locked loop (PLL) contains a voltage-driven oscillator whose output is monitored and controlled to match the frequency of an input signal.

## Slide 19: Voltage-Controlled Oscillator
VCO
Notes: From the circuit Vctrl is used to control the power supplied to the ring oscillator, which ultimately controls the output frequency.

## Slide 20: Alternative Delay Elements
Notes: There are other alternative delay elements that could replace the inverters used in the ring oscillator in the pervious slide. This slide shows delay elements can be formed using transistor circuits, which can take in voltage, digital or current controls depending on the circuit architecture.

## Slide 21: Frequency Divider
Divide clock by N
  Use mod-N counter
Notes: The frequency divider feeds (reference frequency) the phase detector with a frequency derived by dividing the output frequency by a factor of N. The VCO can be controlled by changing N.

## Slide 22: Phase Detector
Difference of input and
feedback clock phase
Often built from phase-frequency detector (PFD)
Notes: The phase detector compares the input signal and the output from the feedback function to determine the appropriate control signal to apply to the Vco.

## Slide 23: Phase Detector
Convert up and down pulses into current proportional to phase error using a charge pump
Notes: A charge pump is used between the phase detector and the loop filter. Its function is to convert the voltage fluctuations from the phase detector to current.

## Slide 24: Loop Filter
Convert charge pump
current into Vctrl
Use proportional-integral control (PI) to generate a control signal dependent on the error and its integral
  Drives error to 0
Notes: One of the major functions of the loop filter is to remove high-frequency noise components from the phase detector output and outputs a voltage control for the Vco.

## Slide 25: PLL Loop Dynamics
Closed loop transfer function of PLL
This is a second order system
wn indicates loop bandwidth
z indicates damping; choose 0.7 – 1 to avoid ringing

## Slide 26: Delay Locked Loop
Delays input clock rather than creating a new clock with an oscillator
Cannot perform frequency multiplication
More stable and easier to design
  1st order rather than 2nd
State variable is now time (T)
  Locks when loop delay is exactly Tc
  Deviations of DT from locked value
Notes: A DLL negatively delays the input signal using series of delay elements whose delay effect can be controlled.

## Slide 27: Delay-Locked Loop (DLL)
System
Linear Model
Notes: Linear model shows that the output of the DLL is a delayed version of the input signal.

## Slide 28: Delay Line
Delay input clock
Typically use voltage-controlled delay line
Notes: Slide talks about the delay line and shows that a change in control voltage results in a change in time of input to output (overall time of the delay elements).

## Slide 29: Phase Detector
Detect phase error
Typically use PFD and charge pump, as in PLL
Notes: The phase detector compares the input signal and the output from the feedback function to determine the appropriate control signal to apply to the delay elements.
A charge pump is used between the phase detector and the loop filter. Its function is to convert the voltage fluctuations from the phase detector to current, which is then used to control the delay elements operation.

## Slide 30: Loop Filter
Convert error current
into control voltage
Integral control is sufficient
Typically use a capacitor as the loop filter
Notes: One of the major functions of the loop filter is to remove high-frequency noise components from the phase detector output and outputs a voltage control for the delay elements.

## Slide 31: DLL Loop Dynamics
Closed loop transfer function of DLL
This is a first-order system
t indicates time constant (inverse of bandwidth)
  Choose at least 10Tc for continuous time approx.