## Slide 1: CMOS VLSI Design Lecture 19: Test
Notes: Hello and welcome.

## Slide 2: Learning Objectives
At the end of this lecture, you should be able to:
Describe the stages of testing in chip design, debug, and manufacturing
Describe the stuck-at-fault model
Develop test vectors to find stuck-at-faults in combinational logic
Use scan chains to gain observability and controllability over a digital circuit
Design built-in self-test circuits
Describe the IEEE boundary scan methodology

## Slide 3: Testing
Testing is one of the most expensive parts of chips
  Logic verification accounts for > 50% of design effort for many chips
  Debug time after fabrication has enormous opportunity cost
  Shipping defective parts can sink a company
Example: Intel FDIV bug (1994)
  Logic error not caught until > 1 M units shipped
  Recall cost $450 M (!!!)

## Slide 4: Logic Verification
Does the chip simulate correctly?
  Usually done at HDL level
  Verification engineers write test bench for HDL
    Can’t test all cases
    Look for corner cases
    Try to break logic design
E.g., 32-bit adder
  Test all combinations of corner cases as inputs:
    0, 1, 2, 231-1, -1, -231, a few random numbers
Good tests require ingenuity

## Slide 5: Silicon Debug
Test the first chips back from fabrication
  If you are lucky, they work the first time
  If not…
Logic bugs vs. electrical failures
  Most chip failures are logic bugs from inadequate simulation
  Some are electrical failures
    Cross talk
    Dynamic nodes: leakage, charge sharing
    Ratio failures
  A few are tool or methodology failures (e.g., DRC)
Fix the bugs and fabricate a corrected chip

## Slide 6: Shmoo Plots
How to diagnose failures?
  Hard to access chips
    Picoprobes
    Electron beam
    Laser voltage probing
    Built-in self-test
Shmoo plots
  Vary voltage, frequency
  Look for cause of
  electrical failures
Notes: Shmoo plot graphically displays the systems response to a range of varying inputs.

## Slide 7: Manufacturing Test
A speck of dust on a wafer is sufficient to kill chip
Yield of any chip is <100%
  Must test chips after manufacturing before delivery to customers to only ship good parts
Manufacturing testers are
very expensive
  Minimize time on tester
  Careful selection of
  test vectors
Notes: Extensive testing can be done at the manufacturer’s end. However, this can be expensive.

## Slide 8: Manufacturing Failures
SEM images courtesy Intel Corporation

## Slide 9: Stuck-At-Faults
How does a chip fail?
  Usually failures are shorts between two conductors or opens in a conductor
  This can cause very complicated behavior
A simpler model: Stuck-At
  Assume all failures cause nodes to be “stuck-at” 0 or 1, i.e., shorted to GND or VDD
  Not quite true, but works well in practice
Notes: Stuck-At-Faults are functional fault model, which operates at the logic models of digital circuits. It models the input(s) or output of the logic gates when stuck at 1 or 0.

## Slide 10: Examples
Notes: Illustrates that the inputs to the gates can be connected to either power (stuck at 1) or ground (stuck at 0). This could be as a result of defects in manufacturing or error by the designer.

## Slide 11: Observability & Controllability
Observability: ease of observing a node by watching external output pins of the chip
Controllability: ease of forcing a node to 0 or 1 by driving input pins of the chip
Combinational logic is usually easy to observe and control
Finite-state machines can be very difficult, requiring many cycles to enter desired state
  Especially if state transition diagram is not known to the test engineer
Notes: The designer can also examine the VLSI system by observing the output from a set of input combination. It is also easy to force the input pins to a 0 or 1 and then observe the output.
Some circuits are difficult to test due to their different possible states, which may be complex.

## Slide 12: Test Pattern Generation
Manufacturing test ideally would check every node in the circuit to prove it is not stuck.
Apply the smallest sequence of test vectors necessary to prove each node is not stuck.
Good observability and controllability reduce the number of test vectors required for manufacturing test.
  Reduces the cost of testing
  Motivates design-for-test
Notes: Test pattern generation takes into consideration the list of possible faults and the lists of tests to check for those faults. Therefore, a set of test vectors will be used to detect the possible faults.
Good and careful TPG reduces the number of required test vectors.

## Slide 13: Test Example
    SA1 SA0
A3 {0110} {1110}
A2 {1010} {1110}
A1 {0100} {0110}
A0 {0110} {0111}
n1 {1110} {0110}
n2 {0110} {0100}
n3 {0101} {0110}
Y {0110} {1110}
Minimum set: {0100, 0101, 0110, 0111, 1010, 1110}
Notes: For the test example, let us examine the test pattern for stuck at 1 (SA1) fault for A3.
The A3 SA1, the test pattern ensures that if A3 is not stuck at 1, then Y = 0, else Y = 1. The same can be said for the rest test patterns.

## Slide 14: Design for Test
Design the chip to increase observability and controllability
If each register could be observed and controlled, test problem reduces to testing combinational logic between registers.
Better yet, logic blocks could enter test mode where they generate test patterns and report the results automatically.
Notes: DFT is a method of designing circuits, which eases test generation and applying the tests.
Sequential circuits contain flip-flops, which may be difficult to control and observe.

## Slide 15: Scan
Convert each flip-flop to a scan register
  Only costs one extra multiplexer
Normal mode: flip-flops behave as usual
Scan mode: flip-flops behave as shift register
Contents of flops
can be scanned
out and new
values scanned
in
Notes: In this method, all flip-flops are converted to scan FFs, which are then connected as configurable shift-registers whose contents can be shifted out and observed.

## Slide 16: Scannable Flip-flops
Notes: Circuit implementation of scannable FFs

## Slide 17: ATPG
Test pattern generation is tedious
Automatic Test Pattern Generation (ATPG) tools produce a good set of vectors for each block of combinational logic
Scan chains are used to control and observe the blocks
Complete coverage requires a large number of vectors, raising the cost of test
Most products settle for covering 90+% of potential stuck-at-faults
Notes: ATPG is the automation of test pattern generation using electronic design tools.

## Slide 18: Built-in Self-test
Built-in self-test lets blocks test themselves
  Generate pseudorandom inputs to comb. logic
  Combine outputs into a syndrome
  With high probability, block is fault-free if it produces the expected syndrome
Notes: Built-in Self-test (BIST) uses circuits inside blocks of circuit to test themselves.

## Slide 19: PRSG
Linear Feedback Shift Register
  Shift register with input taken from XOR of state
  Pseudorandom Sequence Generator
Step | Y
0 | 111
1 | 110
2 | 101
3 | 010
4 | 100
5 | 001
6 | 011
7 | 111 (repeats)
Y
Notes: This circuit generates a pseudorandom sequence of numbers, which can be used for tests.

## Slide 20: BILBO
Built-in Logic Block Observer
  Combine scan with PRSG & signature analysis
Notes: Using additional gates, more (total of 4) functions can be added to the test circuit.

## Slide 21: Boundary Scan
Testing boards is also difficult
  Need to verify solder joints are good
    Drive a pin to 0 and then to 1
    Check that all connected pins get the values
Through-hold boards used “bed of nails”
SMT and BGA boards cannot easily contact pins
Build capability of observing and controlling pins into each chip to make board test easier

## Slide 22: Boundary Scan Example
Notes: Boundary scan is used to observe and analyze the states of sub-blocks and VLSI.

## Slide 23: Boundary Scan Interface
Boundary scan is accessed through five pins
  TCK: test clock
  TMS: test mode select
  TDI: test data in
  TDO: test data out
  TRST*: test reset (optional)
Chips with internal scan chains can access the chains through boundary scan for unified test strategy.

## Slide 24: Summary
Think about testing from the beginning
  Simulate as you go
  Plan for test after fabrication
“If you don’t test it, it won’t work! (Guaranteed)”